## Slide 1: Recitation 11: MallocLab Part 1

## Slide 2: Outline
List Utilization
Structuring (meta)Data
GDB Exercises

## Slide 3: Malloc Internals
The heap consists of blocks of memory
  Some are allocated
  Some are free
What is responsible for tracking allocated blocks?
What is responsible for tracking free blocks?
Notes: Allocated blocks are tracked by the application, else they are leaked.

## Slide 4: List Utilization
The malloc package is responsible for tracking free blocks
  Blocks are tracked in a free list
  Malloc tries reusing these blocks to satisfy future allocation requests
mm-baseline uses an implicit list
  What is its memory utilization in the lab?

## Slide 5: Finding a block
What fit algorithm does mm-baseline use?
What other fit algorithms could be used?
If you switch from an implicit to explicit list representation, how does this change memory utilization?

## Slide 6: Finding a Best Block
You have implemented explicit list representation
  You were using best fit with explicit lists
You experiment with segregated lists and best fit
  Is there a better fit for a given allocation?
  What advantage(s) does segregated lists provide?

## Slide 7: Structuring (meta)Data
There are (at least) two different types of blocks:
  Allocated and free
What data is common between blocks?
What data might a free block need?
Is there any unused space in free blocks?
How can we overlap two different types of data at the same location?
Notes: Hdr is common
Prev / next is for free blocks (footer too, but that’s beyond this recitation)
The payload is unused
Unions! (See textbook)

## Slide 8: GDB Practice
Using GDB well in malloclab can save you HOURS* of debugging time
  Average 20 hours using GDB for “B” on malloclab
  Average 23 hours not using GDB for “B” on malloclab
Form pairs
  Login to a shark machine
  wget http://www.cs.cmu.edu/~213/activities/rec11.tar
  tar xf rec11.tar
  cd rec11
  make
Two buggy mdrivers
*Average time is based on Summer 2016 survey results

## Slide 9: Debugging mdriver
$ gdb --args ./mdriver -c traces/syn-mix-short.rep
(gdb) run
(gdb) backtrace
(gdb) disassemble
1) What function did backtrace indicate? What function was disassembled? What happened?
2) What line of assembly has crashed?

## Slide 10: Debugging mdriver cont.
(gdb) disassemble
=> 0x0...0404363 <+243>: mov %rcx,0x8(%rdi,%rsi,1)
(gdb) print /x <reg> // What register holds the memory location accessed?
// Does the address look valid?
// What about the other register?
Looking up from “=>”, which x86 instructions generate these values? (Hint: The instructions are implementing parts of:
block_t *block_next = (block_t *)(((char *)block) + get_size(block));
word_t *footerp = (word_t *)((block->payload) + get_size(block) - dsize);
Which component is invalid? Review mm.c and identify the bug.
Notes: In place, the write_header and write_footer lines have been swapped.
Write_footer uses get_size, which is uninitialized due to the swap. <- Students should recognize this and now view the code.
The “(%rax,%rdx,1)” is the block_next computation, lea computes the pointer, while mov computes the get_size.
0x8(%rdi, …) is converting block to block->payload.

## Slide 11: Debugging Mdriver-2
$ gdb --args ./mdriver-2 -c traces/syn-array-short.rep
(gdb) run
mm_checkheap will fail
Track the headers / footers for the blocks in the heap using
(gdb) watch *0x800000008 // And other addresses
Notes: This problem is tricky

## Slide 12: 5 Commands to Remember
backtrace
frame
disassemble
print <reg>
watch

## Slide 13: MallocLab Checkpoint
Due Thursday
Checkpoint should take approximately half of the time
Read the writeup
Use GDB
Ask us for debugging help