Network  Server  Design



		       MACH  Networking  Group



			 September  21,  1989



1.   Introduction



The network server is responsible for extending the local MACH
Inter-Process Communication abstraction over the network which
interconnects MACH hosts.  We have designed and implemented a new
version of the network server in a way in which we hope makes it more
efficient, easier to understand, more modular and easier to extend.
In particular we intend to use this new network server to experiment
with various ideas in the area of distributed systems networking, such
as:


    o 	evaluating the merits of various protocols for network
	interprocess communication ---  in  particular, we want to examine:

          -  connection-oriented  versus  connectionless  protocols,

          -  request-response  protocols  for  remote  procedure  calls,  and

	  -  the use of special-purpose protocols depending on the size or the
             destination of
             the  data  to  be  transported;

    o evaluating various models for the distribution of network
      functions between the operating system kernel and user
      processes, and how these two components should interact;

    o security  in  the  network  environment;

    o multicast  groups,  and  associated  delivery  problems;  and

    o copy-on-reference  operations  over  a  network.


This document describes the design of the network server and details
the interfaces to the modules that are used to implement it.  It is
intended for implementers rather than users.  This document reflects
the current state of the implementation, and does not constitute a
commitment for future developments.


In the next section the overall design of the network server is
explained.  The subsequent sections describe the structure of
individual modules.



2.   Overall Structure



2.1.   General Operation



The set of all network servers on a network cooperate to provide IPC
(Inter-Process Communication) between processes on different hosts on
that network.  They achieve that


				  1



cooperation by exchanging Network Server Messages.  Some of these
messages contain the data of IPC messages that are to be transported
across the network, while others are used by the network servers to
communicate information about the status of the operations in
progress, and to maintain a consistent view of the location of the
ports used in the network environment.  A small dispatcher header is
used to distinguish between these various network server messages.


The network servers maintain a space of Network Ports and each network
server maintains a mapping between ports local to its host and network
ports.  Each network port is represented by a Network Port Identifier
which contains information to locate the receiver and owner for the
network port and information which allows the security of the Mach
port abstraction to be maintained in the network environment.  (See
[2] for further details.)



2.2.   Control Structure



The server is structured as a collection of threads sharing the same
address space.  Each thread is used to perform one specific task
asynchronously with the other threads.  Typically, there is one thread
for each ``wait point'' in the system.  Wait points are most often
waits for IPC messages.  The thread is awakened whenever something
happens at this wait point, performs all operations pertinent to the
current event, and goes back to sleep.  Should the service of an event
require a further wait, another thread is signalled and asked to
continue operations after that wait.  In general, one thread should
not have more than one wait point.  Appropriate locking facilities are
used where threads must share access to data structures.  There are a
fixed number of threads in the system:



Timer	Used by all the other threads whenever they need to schedule
	some action to take place at some given time in the future.
	The most common use of this facility is to schedule packet
	retransmission.

IPC Send Waits for messages to arrive on any of the ports that are
	local representatives of remote network ports.  Upon reception
	of such a message, performs the necessary translations and
        initiates transmission on the network.  This thread does not wait
        for the transmission to complete; subsequent actions will be
	taken by the timer thread or by a transport receive thread.

IPC Re-Send is awakened when some other thread or some external
	condition indicates that a message previously handled by the
	IPC send thread should be re-sent either to the original or to
        another destination.  It essentially performs the same
	functions as the IPC send thread, but might take advantage of
        some work already done by the ormer.  This thread is called
	into action when a port is not found at the expected location,
	when a remote port is blocked, or when network errors occur.

Transport Receive (One or more per each transport protocol.)  Waits
	for packets to arrive from the network interface.  Processes
	these packets, perhaps assembling multiple packets into
	contiguous data and perhaps matching incoming packets with
	previously queued outgoing transmissions.  Passes IPC and
	other network server data received from remote network servers
	on to higher level modules for further processing.  As
        suggested above, this thread may use the services of the timer
	thread to schedule retransmissions of packets and to determine
	when a transmission should be aborted.

Notify Messages Waits for notify messages from the kernel to arrive on
	the server's notify port.  These messages indicate changes in
	the status of local ports (death, movements of rights or local
	IPC message accepted).  Takes appropriate action in
	each case to update the server's records and may destroy a
	port, transfer access


				  2



	rights to a network port to a remote network server or signal
	the IPC re-send thread to retry a message transmission.

Name Service Handles requests from other tasks for network name
	service.  Allows names to be looked up on this host, on a
	specific remote host or by broadcasting to all hosts.

Key Management Handles messages from the external Key Distribution
	Server.  These messages tell the network server to use new
	encryption keys for remote hosts.

Other Services A number of other threads may be used to provide other
	services included with the network server, such as monitoring
	and specialized name services.  In each case, the thread is
	waiting for requests on a particular service port.



In addition, if the operations to be performed upon reception of a
network message are too long, the Transport Receive threads may hand
the message to other specialized processing threads, in order to
remain available for new network messages.  Note that it is
impractical to allocate one thread to each IPC message in transit due
to resource limitations.



2.3.   Code Structure



The code is distributed between several modules, each pertaining to
some specific set of related operations or the management of some data
structure.  The main modules are:

Port Records Operations for the handling of port records.  The main
	data structure used is a database of port records, which
	maintains a mapping between local ports and network port
	identifiers, as well as keeping general status information on the
	ports themselves.  Almost every module uses this database to
	obtain information, and a number of modules modify the
	information to reflect new situations that they have
       detected.

Transport Protocols Provide the complete transport mechanism for a
	block of data of arbitrary size over the network.  There are
	several such modules implementing several protocols; some
	guarantee reliable delivery, others don't.  Clients of the
	transport protocols transmit messages by making a function
	call into the transport module; for all incoming messages a
	transport protocol calls a dispatcher function to deliver the
	message.

Dispatcher Dispatches incoming network messages assembled by the
	transport protocols to the appropriate module according the
	dispatcher type contained in the network message header.  The
	handler functions are directly called by the dispatcher.

IPC Message Handling Provides operations for receiving local IPC
	messages and handing them to the transport layer, and
	receiving messages from the transport layer and handing them
	to the local user processes.  To do this it must translate IPC	
	messages to and from a format appropriate for transmission on
	the network.  In particular it must translate ports, identify
	out-of-line data and, if necessary perform byte-swapping (this
	corresponds to the ISO presentation layer roughly).  It also
	handles the blocking mechanism for network ports.

Port Operations Provides all port translation functions for the IPC
	module.  Also handles transfers and deletion of port access
	rights due to the reception of notify messages from the kernel
	and from remote network servers.



				  3



Port Checkups Periodically verifies the information maintained in the
	local port records by consulting other network servers.

Port Search Implements the sequence of operations needed to update the
	information kept about a remote port when it is believed that
	the current information is incorrect.  The checkups module
	calls this module when it finds an inconsistency in the
	information maintained about a port.

Key Management Maintains a mapping between remote hosts and the keys
	that should be use to encrypt secure messages.  Also responsible for
	interfacing with the key distribution server to obtain new
	keys for remote hosts.

Crypt Provides functions to encrypt and decrypt network messages.

Network Name Service Provides a simple, host-directed network name
	look up service.

Memory Management Provides allocation and deallocation functions for
	all memory objects used in the network server.

Read/Write Lock Provides functions implementing read/write locks with
	multiple users.

Locked Queue Operations on shared (i.e.  locked) queues of objects.

Timer Service Allows other modules to schedule actions after a
	specified interval.



Other, miscellaneous modules provide for the generation of unique
identifiers, the initialization of the network server, the actual
transmission of datagrams over the network, and other ancillary
functions.



2.4.   Data Representation



There are a number of circumstances during the processing of IPC
messages when the server has to manipulate large amounts of data.  In
order to minimize overhead, large blocks of data are represented in a
special format designed to limit the need for data copying and space
allocation.


Any conceptually contiguous block of data may be stored internally as
a set of separate segments of any size, and a special sbuf
(Segmented Buffer) structure is used to identify the segments
constituting one block.  No special meaning is attached to how a block
is segmented, i.e.  the segments do not necessarily represent logical
parts of a block of data.  The segments reside in shared memory and
are accessible by every thread.  Data modification and data transfer
between modules are accomplished by operations on sbufs (typedef
struct {...}  sbuf_t, *sbuf_ptr_t).


For instance, if some data must be inserted at the head or the tail of
some existing buffer, a new segment is allocated and placed at the
right location in the sbuf.  If some data inside a buffer must be
modified (possibly changing its length), the sbuf is modified so that
the target data spans complete segments only, and those segments are
replaced in the sbuf by new segments containing the modified data.


Maximum efficiency for the allocation and deallocation of space for
the segments cannot be attained with a general mechanism,
consequently, space management is handled on a case by case basis by
the modules that use sbufs and is private to an individual module.
The information needed to deallocate the space used by segments of a
given sbuf is not kept in the sbuf itself, but is recorded by the
module that created each particular segment.  To simplify
record-keeping, no segment may be referenced in more than one (public)
sbuf.



                                                                4



Typically, when an sbuf is passed between modules, the system provides
a call-back procedure to signal the module that created the sbuf that
it is no longer needed.


Special macros are provided to extract data from an sbuf, making its
structure transparent to most modules.  Special macros are also
provided for inserting data, but for performance reasons, they cannot
be made entirely transparent.



3.   Port Records



3.1.   Description



The port record module maintains all the data associated with ports.
In particular it enables the network server to map local to network
and network to local ports.  An individual port record:



   typedef  struct  {...}  port_rec_t,  *port_rec_ptr_t;



contains the local port, the network port, status information about
the port, several fields used by the IPC module, several fields for
security, a reference count and a read/write lock.


A  network  port  identifier  has  the  following  structure:



   typedef  struct  {
          long             np_uid_high;
          long             np_uid_low;
   }  np_uid_t;



   typedef  struct  {
          netaddr_t    np_receiver;
          netaddr_t    np_owner;
          np_uid_t       np_puid;
          np_uid_t       np_sid;
   }  network_port_t,  *network_port_ptr_t;



where the np_puid is the network port's Public Unique Identifer and
the np_sid is the port's Secret Identifer.



   typedef  unsigned  long  netaddr_t;



is used to identify all network addresses within the network server.



3.2.   Interface



   boolean_t  pr_init()



initializes  the  port  records  module.


				  5



   void  pr_reference(port_rec_ptr)
   port_rec_ptr_t  port_rec_ptr;



increments the reference count for the port record.



   void  pr_release(port_rec_ptr)
   port_rec_ptr_t  port_rec_ptr;



decrements the reference count for the port record, unlocks it and
frees all memory associated with it if the reference count becomes
zero.



   void  pr_destroy(port_rec_ptr)
   port_rec_ptr_t                port_rec_ptr;



logically destroys a port record by removing it from all tables and
deallocating the local port associated with it.  The actual space
occupied by the port record is not freed until the reference count
becomes zero, but this function performs one pr_release before
exiting.



   port_rec_ptr_t  pr_np_puid_lookup(np_puid)
   np_uid_t                         np_puid;



looks up and locks a port record given a network port's public unique
identifier.



   extern  port_rec_ptr_t  pr_nportlookup(nport_ptr)
   network_port_ptr_t        nport_ptr;



looks up and locks a port record given a network port.



   portrec_ptr_t  pr_ntran(nport_ptr)
   network_port_ptr_t        nport;



looks up and locks a port record given a network port, creating a new
port record and allocating a new local port if necessary.



   extern  port_rec_ptr_t  pr_lportlookup(lport)
   port_t                            lport;



looks up and locks a port record given a local port.



   portrec_ptr_t  pr_ltran(lport)
   port_t                            lport;



looks up and locks a port record given a local port, creating a new
port record and allocating a new network port if necessary.


				  6



   boolean_t  nport_equal(nport_ptr_1,nport_ptr_2)
   network_port_ptr_t        nport_ptr_1;
   network_port_ptr_t        nport_ptr_2;



tests to see if two network ports are equal.



   void  pr_nporttostring(nport_str,nport_ptr)
   char                               *nport_str;
   network_port_ptr_t        nport_ptr;



returns in nport_str a printable representation of a network port.



   lock_queue_t  pr_list()



returns a list of all the local ports for which there is a port
record.  (See the section on locked queues for the definition of
lock_queue_t.)


In general, all functions that return a port record lock that record
before returning.  Functions that take a port record as an argument
require that record to be already locked on entry.  The reference
count normally reflects the presence of the port record in both the
local and global tables, but no additional reference is taken by any
of the above functions when returning a locked port record.  Note that
these functions will block on the lock if the record is already
locked.



4.   Transport Protocols



4.1.   Description



Several transport modules co-exist within the network server, each of
them implementing a different protocol.  Some protocols under
consideration are Delta-t, VMTP, NETBLT, TCP, UDP, and various
multicast schemes.  It is up to clients of the transport modules to
choose the one that satisfies their needs best.  All the transport
modules deliver messages into the same dispatcher, and are accessed
via separate entry points, grouped into a table similar to the Mach
device table.


The organization of each protocol module is up to each implementor.
Layered and non-layered approaches are both acceptable, as well as the
use of external servers, not residing in the same address space as the
network server.  Implementors are encouraged to use the sbuf mechanism
to represent and manipulate data internally, and to copy data only at
the last level before the network interface.  The timer module is
available for handling periodic retransmission and other protocol
functions needing timeouts.



4.2.   Interface



Because of an ongoing revision of the implementation, there are
currently two modes of operation for transport modules.


The first mode of operation specifies a simple send operation to
transmit a message to a given destination.  It is used by all modules
except the IPC module, to exchange information with the corresponding
modules in the network servers at other nodes.


				  7



The second mode of operation specifies a request-response interaction,
in which one node (the client) sends a request to another node (the
server), and then awaits the reception of exactly one response from
that server.  The transport protocol always supports the transmission
of a 32-bit completion code in the response, and may optionally
support the transmission of data in that same response.  This mode of
operation is used by the IPC module for the transmission of IPC
message data; it is intended to be the standard for all transport
protocols, and all other modules will be converted to use it.


Currently, each specific transport module only implements one or the
other mode of operation; and can therefore be used either by the IPC
module or by all other modules, but not both.  In the future, all
modules will be converted to the second mode of operations.


The following table is used to hold all the entry points for all the
possible transport modules.  Each transport module is assigned a
specific number, to be used as an index into this table when invoking
it, and to be used to identify it when it delivers a message to the
upper level.



   typedef  struct  {
          int              (*send)();
          int              (*sendrequest)();
          int              (*sendreply)();
   }  transport_sw_entry_t;



The entries in this table are filled by each transport module when it
initializes itself.  Any unused entry is set to the special function
transport_no_function, which simply returns after emitting an error
message.  The send entry is used for the simple send interface.  The
sendrequest and sendreply entries are used for the request-response
interface.  Any protocol supporting that interface must implement
sendrequest, but not necessarily sendreply, as described above.


In the following descriptions, xxx_ is used as a generic prefix, to be
replaced by the name of each transport module.



   boolean_t  xxx_init()



initializes the transport module and places the entry points in the
transport switch table.



   int  xxx_send(client_id,trid,data,to,service,crypt_level,cleanup)
   int                                   client_id;
   int                                   trid;
   sbuf_ptr_t                       data;
   netaddr_t                         to;
   int                                   service;
   int                                   crypt_level;
   int                                   (*cleanup)();



attempts to send message data to destination to.  client_id is an ID
used by the client to identify this message.  trid is a
transport-level ID used to identify a current request-response
interaction; it should be 0 if not used.  service is the kind of
service required for this message; possible values are:


				  8



    o TRSERV_NORMAL:  normal  transmission  of  a  single  message.

    o TRSERV_IPC: transmission of an IPC message, ``call-back''
      required.  (OBSOLETE)

    o TRSERV_RPC: transmission part of a request-response at the IPC
      level.  Pairing information required and ``call-back'' required.
      Note that the ``call-back'' can be implicitly be the delivery of
      the response if the RPC succeeds.  (OBSOLETE)

    o TRSERV_URGENT: transmission of an urgent single message, to be
      delivered before other non-urgent transmissions in progress if
      possible.



crypt_level determines what kind of encryption should be used to
protect the data.  Possible levels of encryption include:
CRYPT_DONT_ENCRYPT and CRYPT_ENCRYPT.  cleanup is a function supplied
by the client, to be called when the transmission is complete and the
message data is no longer needed.  Depending on the service requested,
it may indicate a simple local completion, or participate in the
``call-back'' mechanism.  It takes two arguments: the client ID, and a
completion code.


cleanup returns 0 when all is well.  xxx_send also returns a
completion code to indicate the immediate local result of the call.



   int xxx_sendrequest(client_id,data,to,crypt_level,reply_proc) 
   int		client_id; 
   sbuf_ptr_t 	data; 
   netaddr_t 	to; 
   int 		crypt_level;
   int   	(*reply_proc)();


attempts to send a request containing data to destination to.
client_id is an ID used by the client to identify this
request-response interaction.  crypt_level determines what kind of
encryption should be used to protect the data.  Possible levels of
encryption include: CRYPT_DONT_ENCRYPT and CRYPT_ENCRYPT.  reply_proc
is a procedure to be called from the transport module to deliver a
response.


xxx_sendrequest returns either TR_SUCCESS or a specific failure code.
In the first case, a request-response interaction is initiated, that
will terminate when reply_proc is called.  The data supplied in the
request must be kept valid by the caller for the whole duration of the
request-response interaction.  The reply procedure is guaranteed to be
called exactly once, with the following arguments:



   void  reply_proc(client_id,reply_code,data)
   int                     client_id;
   int                     reply_code;
   sbuf_ptr_t          data;



client_id is the ID given as argument to xxx_sendrequest.  reply_code
is a completion code supplied either by the transport module (in case
of transport errors) or by the server process that handled the
request.  data may contain data supplied by the server in the
response, or it may by null.  This data is kept valid by the transport
module only until reply_proc returns.


If xxx_sendrequest returns anything other than TR_SUCCESS, no
request-response interaction is initiated, and reply_proc is never
called.



                                                                9



The handler on the server side of a request-response interaction is
invoked via the dispatcher module (see below).  This handler must
return a code that determines how the response is sent.  If this code
is anything other than DISP_WILL_REPLY, a response containing that
code and no data is immediately sent back by the transport module.  If
this code is DISP_WILL_REPLY, no response is generated by the
transport module, and the higher-level module must explicit call
xxx_sendreply to terminate the request-response interaction:



   int  xxx_sendreply(trid,code,data,crypt_level)
   int                     trid;
   int                     code;
   sbuf_ptr_t          data;
   int                     crypt_level;



trid is a transport-level ID supplied by the dispatcher with the
request.  code and data are the reply code and data to be used in the
call to reply_proc on the client.  crypt_level determines what kind of
encryption should be used to protect the data.  data can be null.  If
it is not, the data must be kept valid by the caller only until
xxx_sendreply returns.


The procedure returns TR_SUCCESS or TR_FAILURE.  It is an error to
call xxx_sendreply for a terminated request-response interaction,
including one terminated by the handler returning a code other than
DISP_WILL_REPLY.  Similarly, it is an error for the handler to return
DISP_WILL_REPLY if the transport module in use does not implement
xxx_sendreply.


Note that since multiple threads are involved, the reply procedure may
be called before xxx_sendrequest returns.  Similarly, it is acceptable
for the server to call xxx_sendreply before returning from the handler
procedure for the request, provided that this handler eventually
returns DISP_WILL_REPLY.


The  completion  codes  for  transport  operations  are:



    o TR_CRYPT_FAILURE: the transmission failed either because of a
      local encryption or a remote decryption failure --- the local
      client module should try and get a new key for the destination
      host and then retry the transmission;

    o TR_SEND_FAILURE: something went wrong with the transmission
      before any data could be sent.

    o TR_FAILURE: something went wrong with the transmission within
      either the local or remote transport module; the error was
      detected too late to return TR_SEND_FAILURE.

    o TR_OVERLOAD: the transport module is currently overloaded.  No
      data was sent; the user should retry later.

    o TR_SUCCESS: the transmission was successful but it was not
      possible to determine whether the message was accepted by the
      remote client.

    o a client-specific completion code (see, for example, the codes
      returned by the IPC module).



Note that the transport-specific completion codes are in the same
space as the client-specific completion codes; care must be taken to
avoid collisions.



				  10



4.3.   Specific Transport Protocols



4.3.1.   Delta-t



Delta-t is a connectionless transport protocol in which each packet
sent over the network is individually acknowledged by the destination
network server before the next packet is sent.  All the
transport-level protocol handling is performed in the network server;
network access at the IP level is achieved through the Mach network
interface described below.  Retransmissions are scheduled using the
timer module.  In order to detect duplicate packets, information about
an incoming data packet is maintained by a network server either until
the next packet in a sequence is received or the information has been
held more that some minimum amount of time.


Delta-t currently implements the request-response interface without
deltat_sendreply.


Delta-t is suitable for transmitting messages containing small amounts
of data (less than a few packets in total).  If the message is part of
a RPC protocol in which the response to the request is expected
shortly, then it is better to use a more specialized request-response
protocol such as VMTP.



4.3.2.   VMTP



VMTP (Versatile Message Transport Protocol) is the request-response
protocol developed at Stanford by D.  Cheriton and his group [1 ].
The VMTP module creates a single well-known server entity to receive
all network requests, and keeps a pool of client entities to use on
the client side to initiate transactions.  Whenever vmtp_sendrequest
is called, an unused client entity is pulled out of that pool; it is
returned to the pool when the reply is delivered.  The actual VMTP
protocol handling module is in the kernel; it communicates with the
network server using sockets.


There are currently two versions of the VMTP module.  vmtp1 implements
the simple send interface and should not be used.  vmtp2 implements
the full request-response interface, and is suitable for IPC messages.



4.3.3.   TCP



The TCP module keeps a pool of TCP connections to the network servers
on other nodes.  Each connection is created when needed to transmit a
request, and is kept open as long as possible to service further
requests to the same destination.  Open connections are recycled using
a least-recently-used policy to limit their number.  The protocol
handling module is in the kernel; it communicates with the network
server using sockets.


TCP currently implements the full request-response interface, and is
suitable for IPC messages.



4.3.4.   Datagram



The ``datagram'' transport protocol simply provides an interface to
the UDP level.  It allows unreliable datagrams to be sent over the
network.



				  11



Datagram currently implements the simple send interface and cannot be
used to transmit IPC message data.



4.3.5.   Simple Request-Response



The simple request-response protocol permits the sending of a request
over the network for which a response is expected.  The data of the
request is guaranteed to fit in one network datagram.  This protocol
will treat responses as acknowledgements to requests and inform its
client either of the failure of the request (if no response was
received after some number of tries) or of the success of the request
in which case the response is returned to the client.  It is assumed
that a request can be handled without delay by the higher-level
protocol and the response is supplied on return from the request call.
Requests made using this protocol should be idempotent.


Although SRR is oriented toward request-response interactions, it
implements the simple send interface and not the request-response
interface.  It cannot therefore be used to transmit IPC message data.



5.   Dispatcher Module



5.1.   Operation



The dispatcher module is responsible for invoking the correct handler
procedure when some network message has been received.  It is called
by the various transport modules, examines the dispatcher header, and
selects the appropriate routine to call according to the message type
(incoming IPC, port death, and so on).


This module can optionally establish a separation between a network
thread and one or more other threads used to process the messages at
the network server level.  This last scheme is to be used if the
network thread would not be fast enough if it had to completely
process each message before listening to the net again.  Note that
with this mechanism, care must be taken to avoid problems when a
transport module deallocates the space used by incoming data before
that data has been processed at the higher level.

To allow communication between machines with different data
representation, the dispatcher header always use a standard
representation.  The rest of each message uses whatever representation
is in use on the sending machine; a code for that representation is
stored in the dispatcher header and made available to the message
handler modules.


To allow future expansion, the dispatcher also checks a version number
for each incoming message.


5.2.   Interface


As discussed in 4.2, there are currently two transport interfaces, to
which correspond two dispatcher interfaces.  The following table holds
a set of entry points for each message type.


   typedef  struct  {
          int              (*disp_indata)();
          int              (*disp_inprobe)();
          int              (*disp_indata_simple)();
          int              (*disp_rr_simple)();
          int              (*disp_in_request)();
   }  dispatcher_switch_t;

				  12





All modules place entry points in the table for each message type and
each type of handler procedure that they support and wish to receive
messages for.  Unused entries are set to the special procedure
disp_no_function; the network server is organized in such a way that
there are not collisions in the table.


disp_indata, disp_inprobe, disp_indata_simple and disp_rr_simple are
called by transport modules using the simple xxx_send interface, and
will eventually be eliminated.


disp_in_request is the sole entry point used with the request-response
interface.



   int  disp_init()



initializes the dispatcher module.



   int  disp_indata(trid,data,from,tr_cleanup,trmod,
                             client_id,crypt_level,broadcast)
   int                                   trid;
   sbuf_ptr_t                       *data;
   netaddr_t                         from;
   int                                   (*tr_cleanup)();
   int                                   trmod;
   int                                   client_id;
   int                                   crypt_level;
   boolean_t                         broadcast;



is the primary function used to dispatch incoming data in the simple
send mode of operation.  trid is a transport level identifier assigned
by the transport module trmod.  It should be used in the call to
tr_cleanup which signals to the transport module that the higher-level
module is finished with the data contained in the sbuf data.  Other
arguments are: from, the host that sent the data; client_id, an
identifier assigned by the client module within a prior call to
disp_inprobe (see below); crypt_level, the encryption level used to
send data over the network; and broadcast whether the data was
broadcast or not.  disp_indata returns DISP_FAILURE is the dispatcher
module did not find a higher-level routine to be called for the
incoming message type or if the version number of the incoming message
did not match the current version number of this implementation of the
network server; otherwise it returns the value returned by the
higher-level routine.



   int  disp_inprobe(trid,pkt,from,cancel,trmod,
                             client_id,crypt_level,broadcast)
   int                                   trid;
   sbuf_ptr_t                       pkt;
   netaddr_t                         from;
   int                                   *((*cancel)());
   int                                   trmod;


				  13



   int                                   *client_id;
   int                                   crypt_level;
   boolean_t                         broadcast;



allows the first packet of a message to be dispatched to a
higher-level probe routine.  This allows the higher-level routine to
decide before-hand whether to accept or reject an incoming message.
If it decides to accept the message based on the probe packet, the it
returns a client_id to allow it to later identify the whole incoming
message.  cancel (an out parameter) is called by the transport module
if it is unable to deliver the complete message after a probe has been
accepted.  It takes as argument the client_id and a reason code.
Other parameters are as for disp_indata.



   int  disp_indata_simple(client_id,data,from,crypt_level,broadcast)
   int                                   client_id;
   sbuf_ptr_t                       data;
   netaddr_t                         from;
   int                                   crypt_level;
   boolean_t                         broadcast;



is similar to disp_indata except that it is guaranteed that the data
is processed at the higher-level within the same thread that made the
call.  Hence there is no need for a tr_cleanup call because, when the
dispatcher call returns, the transport module knows that the data is
no longer needed and can do the cleanup synchronously.



   int  disp_rr_simple(data,from,crypt_level,broadcast)
   sbuf_ptr_t                       data;
   netaddr_t                         from;
   int                                   crypt_level;
   boolean_t                         broadcast;



allows a transport-level protocol to make a simple request-response
interaction with a higher level module.  The higher-level module
should process the request immediately and include the response on
returning from the call.  Note that this procedure is intended for
request-response interactions within the simple send mode of
operations, and not within the full request-response interface
described above.



   int  disp_in_request(trmod,trid,data_ptr,from,crypt_level,broadcast);
   int                                   trmod;
   int               trid;
   sbuf_ptr_t               data_ptr;
   netaddr_t               from;
   int               crypt_level;
   boolean_t               broadcast;



is the single function for dispatching in the request-response mode of
operation.  The arguments are similar to those of disp_indata.  The
data pointed to by data_ptr is valid only until this procedure
returns.  Any return value other than DISP_WILL_REPLY is interpreted
by the transport module as a completion code to be returned
immediately in a response to the client.  DISP_WILL_REPLY means that
the higher-level module assumes the responsibility to send a response,
and the transport module should do nothing when this procedure returns
(other than deallocate the space occupied by the data, if


				  14



appropriate).  Note that if the dispatcher returns DISP_FAILURE, that
code is returned to the client in the normal way.


In subsequent sections of this document, functions which are called
via the dispatcher module do not have their arguments described.  The
arguments are exactly as for the corresponding dispatcher function.



6.   IPC Message Handling



The IPC Message Transfer module implements the upper layer of the
mechanism used to communicate with remote ports.  It relies on a
separate transport module to provide the lower-level network
transmission operations, and communicates with it using sbufs.  To
maximize performance, the IPC module tries to identify messages that
are part of a remote procedure call (RPC), and attempts to map the
request-response structure of such calls into a request-response
interaction at the transport level.



6.1.   Normal Operation



The IPC module receives messages addressed to ports that are local
representatives of remote ports.  Upon reception of such a local IPC
message, the IPC module



1.  allocates a transaction record (ipc_rec) to keep information about
    the transfer in progress,

2.  consults the port records to find the remote port corresponding to
    the local port,

3.  generates an IPC Header to contain special information to be used
    by the remote network server,

4.  translates the ports and out-of-line pointers in the message so
    that they will be intelligible on the receiving node, and

5.  selects a transport protocol to use, and hands the whole message
    to the appropriate module via xxx_sendrequest.



Note that the breakup of the message into several packets is the task
of a transport module and not the IPC module.


All these operations are performed on a message represented using an
sbuf.  In general, the segments contained in the sbuf are:



    o the IPC receive buffer, containing the inline data;

    o each out-of-line data section;

    o the IPC header, allocated by this module; and

    o any special data structures needed for the message translation
      process, such as accessibility maps or a network port
      dictionary.



In the remote network server receiving the message, all the component
packets are assembled by the transport module, which calls the IPC
module and hands it an sbuf representing the whole message.  Typically
segments in that sbuf are part of packet


				  15



buffers in which the message was received.  The module uses ipc_rec
records to store information about current incoming messages.  It
performs all necessary translations (including byte-swapping and data
type conversion), copies the message into a send buffer, and delivers
it to its local destination.


The IPC module on the sending network server may not discard the
message immediately after calling the transport module to initiate a
transmission, because it may be necessary to effect a complete
retransmission, possibly to a new destination and with different
accompanying data.  This is the case when some exceptional events,
described in the next section, prevent the receiving network server
from delivering the message to its ultimate destination.  In addition,
some operations pertaining to security must be performed by the IPC
module on the sending node only when it is certain that the message
has been correctly transmitted.  For these reasons, the network server
on the receiving node uses the request-response transport mechanism to
return a completion code indicating if it was able to deliver the
message, or what happened if it was not.  Upon reception of this
completion code, the sending network server may deallocate its ipc_rec
and the message data, or undertake the appropriate recovery action in
case of error, including initiating a new transmission.



6.2.   Exceptional Events



The exceptional events are detected either at the transport level or
by the IPC module in the remote network server.  They are reported to
the sending IPC module through the request-response completion code
described above.  The IPC module must then freeze the current
transmission, and call another module to deal with that exception.
That module may in turn request the IPC module to attempt to retry the
transmission of any pending messages for a given destination port,
possibly after changing some information in the port's record.  In
that case, the IPC module will restart processing of any affected
messages as if that message had just been received on a local port.
As an optimization, it could reuse some of the information already
gathered, and stored in the record for this pending message.


Exceptional  events  include:



    o Modification of a port record while a message for that port is
      in transit by some other thread running concurrently with the
      IPC sending thread (for example in response to a port death
      message).  It simply triggers re-processing of the message.

    o Network failure, detected by the transport module.  The IPC
      module must decide to abort or retry the message, and find out
      if the port is dead.

    o Crypt failure, detected by the transport module at the local or
      remote node when it does not possess the correct key to encrypt
      or decrypt the message.  The IPC module calls the key management
      module to establish a new key.

    o Remote port not found at the expected node, signalled by the
      receiving IPC module --- a port search procedure is initiated (in
      another thread), and its completion will decide whether the
      transmission is to be restarted or aborted.

    o Remote port blocked, signalled by the remote IPC module.  The
      sending node suspends the message until further notice and
      indicates the situation in its port record.  A ipc_block record
      for the sending node is allocated at the receiving node.  When
      the port becomes unblocked, the list of those records is scanned
      and a special PORT_UNBLOCKED message is transmitted to each
      waiting network server, to indicate that transmission should be
      restarted.  If this unblock message is lost then the


				  16



      port checkups module will discover that the port has become
      unblocked and will retry the message transmission.



To avoid blocking the message delivery thread in the receiving network
server, all messages are always delivered using the SEND_NOTIFY option
of msg_send.  If the return from msg_send indicates that the local
port has become blocked, no other messages will be accepted for that
port until the kernel indicates that it has been unblocked.
Appropriate marking and locking of the port record guarantees that no
two threads can be in the situation of exercising the SEND_NOTIFY
option on the same port at the same time.  Note that this mechanism
does not require the receiving network server to return a port blocked
indication for a message accepted under the SEND_NOTIFY option,
thereby allowing the actual message delivery to be performed in
another thread after the dispatcher procedure has returned (the
current implementation does not take advantage of this feature).



6.3.   RPC Interactions



The IPC module offers an optimization for RPC interactions for which
the user is willing to accept some semantic restrictions:



    o the request message is followed by exactly one response message
      addressed to the reply port indicated in the request.

    o the reply port is local to the node issuing the request.

    o no new request is sent using the same reply port while awaiting
      a response on that reply port.

    o the  reply  port  is  not  deallocated  while  awaiting  a  response.

    o the receive rights for the reply port are not transferred while
      awaiting a response.

    o the reply port is not blocked or locked while awaiting a
      response.



If any of those rules is violated, the response is not guaranteed to
be delivered, or may be delivered out of order; the behavior of the
network server may vary from one instance of such an erroneous
situation to the next.  The user must specify the MSG_TYPE_RPC bit in
the msg_type field of the message header for the request to indicate
that he accepts those modified message semantics.


Whenever a valid request is received with the MSG_TYPE_RPC bit set,
the network server on the server side uses DISP_WILL_REPLY if possible
to delay the transmission of the completion code at the transport
level.  It keeps track of the pending request in a ipc_rec, and
considers a new IPC message destined to the reply port as the response
for the RPC interaction.  Instead of sending this message with a new
transport interaction, it places it in the response for the pending
interaction.  Because the transport interface does not provide an
end-to-end acknowledgment that the data portion of a response was
correctly handled by the IPC module on the client side, the network
server on the server side must rely on the above assumptions for
delivery of the response to the reply port.


This scheme also relies on the assumption that the response message
will eventually be sent from the same node that received the request
message, and that no other traffic involving the reply port takes
place until that response is delivered.  This assumption



				  17



may easily be invalidated both by erroneous actions on the part of the
client or server processes, or by normal operations such as request
forwarding.  Because resources in the transport module are tied up as
long as the response has not been delivered, the IPC modules on both
sides check for all events that may suggest that a response may not be
forthcoming in the normal way.  When any such event occurs, they force
the transmission of a dummy response to terminate the request-response
interaction, letting the real response, if any, proceed normally as a
new single IPC message.  The events causing such an abort include:



    o transfer of receive or ownership rights for the reply port.

    o transmission of a new message using the same reply port.

    o reception of a message on the reply port on the client side,
      from a source other the expected server.

    o reception of a message on the reply port on the server side,
      with the MSG_TYPE_RPC bit set.

    o timeout at the network server on the server side (triggered by
      the port checkups mechanism).



Note that none of these aborts compromise the semantics of an RPC;
they simply nullify the performance benefits of the RPC optimization
when the situation is not simple.  In addition, the network server
itself never sets the MSG_TYPE_RPC bit when delivering a message to a
local port, to avoid hidden forwarding problems.



6.4.   Message Ordering



A weak ordering of message delivery is provided through the use of a
queue of pending transactions for each remote network port.  This
queue operates in the following way:



    o all outgoing RPC requests and single IPC messages are queued in
      the order in which they are received on the local port.

    o as long as there are only RPC requests on the queue, each is
      transmitted as soon as it is queued; the system does not wait for a
      response before transmitting the next
       request.

    o as soon as one single IPC message is queued, newer messages (IPC
      or RPC) are queued but not transmitted until that IPC message is
      successfully transmitted and dequeued (including any number of
      retransmissions).

    o RPC responses are never queued; they are transmitted at once and
      never retransmitted.

    o whenever the status of the network port changes, retransmissions
      are initiated as needed in the order in which records are on the
      queue.

    o the local port is locked when the queue becomes too long and new
      messages cannot be transmitted.



This strategy guarantees that single IPC messages directed at the same
destination port from the same node are strictly ordered.  RPC's are
naturally ordered simply because the client waits for the response
before issuing the next request.  There are no ordering guarantees for
a single IPC immediately following the request for a RPC.


				  18



6.5.   Interface



   boolean_t  ipc_init()



initializes  the  IPC  module.



   int  ipc_in_request(trmod,trid,data_ptr,from,crypt_level,broadcast)



is called from disp_in_request when a RPC request or single IPC is
received over the network by a transport module.  It is the main entry
point for incoming messages.  See the dispatcher module for details
about the parameters to this call.



   void  ipc_in_reply(client_id,code,data_ptr)



is the procedure used by the IPC module to receive responses from the
transport module after a call to xxx_sendrequest for IPC message data.
See the transport module for details about the parameters to this
call.



   ipc_in_unblock(client_id,data,from,broadcast,crypt_level)



is called by disp_indata_simple when an unblock message is received
from a remote network server.  It will cause the message transmission
to be retried.  See the dispatcher module for details about the
parameters to this call.



   void  ipc_msg_accepted(port_rec_ptr)
   port_rec_ptr_t                port_rec_ptr;



is called by the local port operations module when it receives a
notify message from the kernel saying that a particular port is now
unblocked.  The IPC module will send unblock notification messages to
remote network servers that are blocked waiting to send a message to
the port.



   void  ipc_port_dead(port_rec_ptr)
   port_rec_ptr_t                port_rec_ptr;



is called by the local port operations module either when it receives
a notify message from the kernel saying that a particular port is now
dead or when it receives a message from a remote network server saying
that a particular network port is now dead.  The IPC module will clean
up any data structures it has associated with the deceased port.



   void  ipc_port_moved(port_rec_ptr)
   port_rec_ptr_t                port_rec_ptr;



is called by the local port operations module when it receives a
message from a remote network server saying that a particular network
port has moved.  The IPC module will abort any pending RPC's involving
this port.


				  19



   int  ipc_in_abortreq(trmod,trid,data_ptr,from,crypt_level,broadcast)



is called from disp_in_request when a request to abort a pending
request-response interaction is received over the network by a
transport module.  The data specifies which RPC is to be aborted.  If
it is still pending, a dummy response is sent at once; otherwise, this
request is ignored.  See the dispatcher module for details about the
parameters to this call.



   void  ipc_in_abortreply(client_id,code,data_ptr)



is the procedure used by the IPC module to receive responses from the
transport module after a call to xxx_sendrequest for a request to
abort a pending RPC.  See the transport module for details about the
parameters to this call.



   void  ipc_retry(port_rec_ptr)
   port_rec_ptr_t                port_rec_ptr;



is called from other modules when a message transmission should be
retried following some change in the port records.  It will cause the
retransmission to be executed in a special ``resend'' thread distinct
from the one making the ipc_retry call.



   void  ipc_freeze(port_rec_ptr)
   port_rec_ptr_t                port_rec_ptr;



is called from other modules when the status of a port becomes such
that no further transmissions should be attempted to that port.
Transmission will be resumed when ipc_retry is called.



7.   Port Operations



7.1.   Description



The functions provided by the port operations module are called in one
of the following three circumstances:



1.  A message is received from the local kernel notifying the network
    server about a change in condition of a local port.  These changes
    are:

          o the death of the local port;

          o the transfer of port access rights to another task
            (probably because the task holding the rights has died);
            and

          o the local unblocking of the port.

2.  A message is received over the network notifying the network
    server of a change in the remote network port's condition.  The
    possible changes are as for the local case except that they should be
    interpreted in the context of the remote port.

3.  Access rights to a port are being transferred in a normal IPC
    message which is about to be sent to a remote network server or has
    been received from a remote network server.


				  20



The behavior of the port operations module depends on whether the port
that it is handling must be treated securely or not.  For instance, if
send rights to a port are being transferred in an IPC message and the
port is meant to be secure, then a token should be created for the
port and transferred along with the network port identifier when the
message is sent to the remote network server.  Similarly, at the
receiving end, the port operations module should store the token in
the network port's record.  However, if the port is not meant to be
treated securely, then no transfer and storing of a token need be
done.


In general the port operations module will often have to directly
modify the port's records, it may retry or freeze the sending of an
IPC message, it may initiate a port search, or, when port rights are
being transferred, it will provide the information that must be sent
to the remote network server.  Conversely, it must process this
information when the information is received from a remote network
server.  In addition, when it is considering a secure port, it may
have to generate or check a token for the port or it may have to
transfer or check the key that represents receive or ownership rights
to the port.



7.2.   Interface



   boolean_t  po_init()



initializes the port operations module.



   po_check_ipc_seq_no(port_rec_ptr,  host_id,  ipc_seq_no)
   port_rec_ptr_t                port_rec_ptr;
   netaddr_t                         host_id;
   long                                 ipc_seq_no;



checks that the incoming IPC sequence number of a message is greater
that the last sequence number received for the network port with port
record port_rec_ptr from the network server on machine host_id.  This
check is only done for secure messages and ensures that complete IPC
messages cannot be replayed by a malicious party.



   typedef  struct  {...}  secure_info_t,  *secure_info_ptr_t;



is used to hold the key representing receiver or ownership rights to a
network port.



   long  po_create_token(port_rec_ptr,  token_ptr)
   port_rec_ptr_t                port_rec_ptr;
   secure_info_ptr_t           token_ptr;



creates a token for a port.  Stores the token in token_ptr and returns
the random number used to construct the token.



   void  po_notify_port_death(port_rec_ptr)
   port_rec_ptr_t                port_rec_ptr;



triggers handling of a local port death.  Marks the port's record as
deleted, sends out an unreliable port death notification messages and
does other local cleanups.


				  21



void  po_port_deallocate(lport)
port_t                              lport



deallocates a port but retains send rights to it.  This allows the
network server to transfer receive or ownership rights to a port to a
local task using the notification mechanism of the kernel.



   int  po_translate_lport_rights(client_id,lport,right,security_level,
                             destination_hint,port_data)
   int                                   client_id;
   port_t                              lport;
   int                                   right;
   int                                   security_level;
   netaddr_t                         destination_hint;
   pointer_t                         port_data;



is called by the IPC module to pack up the data that needs to be sent
to the host destination_hint in order to transfer the access rights
right to port lport.  The data that needs to be sent depends on the
security_level of the transfer.  The data is packed into the space
pointed to by port_data and the size of the network port data that has
been created is returned as the function's result.  The client_id is
an identifier remembered by the port operations module so that it can
match up a subsequent po_port_rights_commit (see below) with this call
of po_translate_lport_rights.



   po_port_rights_commit(client_id,  completion_code,  destination)
   int                                   client_id;
   int                                   completion_code;
   netaddr_t                         destination;



informs the port operations module that a transfer of rights to a
remote network host has either succeeded or failed.  The client_id
allows the port operations module to match this call with a previous
call of po_translate_lport_rights.  The completion_code can be one of
PO_RIGHTS_XFER_SUCCESS and PO_RIGHTS_XFER_FAILURE.  The destination
names the remote network server to which the port rights were actually
transferred.  It may be different from the destination_hint passed to
po_translate_lport_rights.



   int  po_translate_nport_rights(source,port_data,security_level,
                             lport,right)
   netaddr_t                         source;
   pointer_t                         port_data;
   int                                   security_level;
   port_t                              *lport;
   int                                   *right;



is called by the IPC module when it receives access rights to a remote
network port in a message from a remote network server.  The access
rights are contained in the data pointed to by port_data and were
received from the network server on host source and at security_level.
The port data received is handled according to what access rights are
being transferred and the local port corresponding to the network port
that was transferred is returned in lport.  In addition the actual
right transferred is returned in right and the size of the port data
that was processed is returned as the function's result.


				  22



   int po_handle_ro_xfer_request(request,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an incoming transfer of
receiver or ownership rights.



   int po_handle_ro_xfer_reply(client_id,reply,from,broadcast,crypt_level)



is called by disp_rr_simple to handle the response to a transfer of
receiver or ownership rights.



   int  po_handle_ro_xfer_hint(request,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an unreliable notification
of a transfer of receiver or ownership rights.



   int  po_handle_nport_death(hint,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an unreliable notification
of the death of a network port.



   int  po_handle_token_request(request,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an incoming request for a
token of receiver/owner authenticity.



   int po_handle_token_reply(client_id,reply,from,broadcast,crypt_level)



is called by disp_rr_simple to handle the response to a request for a
token of receiver/owner authenticity.



8.   Port Checkups



8.1.   Description



The port checkups module does a periodic probing of other network
servers to find out whether the status of network ports has changed.
In particular, it is the default way in which the network server finds
out about the death of a network port or the fact that receive or
ownership rights have moved to a different network server.  These
special conditions can also be detected as part of the normal
transmission of IPC messages across the network.  The port checkups
routine should only be called periodically and when the network server
is otherwise idle; in other words it is of low priority.


The checkups module needs to be able to look at the port records in
order to examine a ``aliveness'' parameter associated with each port
record.  The aliveness parameter is decremented by the port checkups
module every time it is called.  Only when it goes below some
predetermined value, is a checkup performed for the port.  Moreover,
the aliveness


				  23



parameter is updated to fully-alive when the IPC module has
successfully sent a message over the network to the port.  In other
words, if the port is in regular use then no checkup is done for it.


When the checkups module actually decides to send a checkup request to
find out about ports, it constructs an sbuf for each network server
that it must query.  An sbuf contains the ports in which it is
interested for which it believes the remote network server is
responsible.  To transmit and receive checkup information across the
network, the port checkups module uses the simple request-response
transport protocol.  After making a request by calling srr_send, the
checkups module will either receive a checkup reply or a failure
notification from the transport module.


On receiving a checkup request, the checkups module looks at each port
contained in the request.  If the information about the port that the
requester sent does not match the information held locally, then the
port in the checkup packet is marked as being ``bad''.  The checkup
reply packet is then sent back to the requester.


On receiving a checkup reply, the requester examines all the ports in
the reply and for those ports with a ``bad'' status it calls the port
search module.  It is up to the port search module to find out more
about the status of the port.  If no response was received to the
checkup request then the checkups module must call the port search
module for each port in the checkup request in order to resolve the
port's status (e.g.  to determine whether it is dead).


One other function of the checkups module is to determine whether
there exist any tasks with send rights to each port the network server
knows about.  This is in order to extend the MACH ``no-senders''
notification message into the network environment.  The checkups
module can determine that a network port has no senders if there has
been no interactions (the reception of either an IPC message or a
checkup request) involving this port for some period of time
(typically some number of checkup rounds).  If the network port has no
senders then the checkups module can deallocate send rights to the
corresponding local port and destroy the associated port record.


In addition the checkups module is responsible for handling hints
received saying that a remote network server has just restarted.  For
such a hint the checkups module calls the port search module for each
port that had the restarted network server as its owner or receiver.



8.2.   Interface



   boolean_t  pc_init()



initializes  the  checkups  module.



   int  pc_do_checkups()



is called by the timer module to perform a checkup.



   pc_handle_checkup_request(request,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an incoming checkup request.



				  24



   pc_handle_checkup_reply(client_id,reply,from,broadcast,crypt_level)



is called by disp_rr_simple to handle an incoming checkup reply.



   void  pc_send_startup_hint()



is called on start-up to send out a hint saying that this network
server has just restarted.



   int  pc_handle_startup_hint(hint,from,broadcast,crypt_level)


is called by disp_indata_simple to handle an incoming network server
restart hint.



9.   Port Search



9.1.   Description



The port search module is called when some other module (probably
either the port checkups module or the IPC module) determines that the
information held about a network port is no longer correct.  The task
of the port search module is to update that information, in particular
it may determine that the network port is dead.


The  search  procedure  is  basically  as  follows:



       query  network server  believed  to  be  the  receiver;
       if  receiver responds  with  useful  information
       then  believe it
       else {
             query  network  server  believed  to  be  the  owner;
             if  owner  responds  with  useful  information
             then  believe  it
             else  broadcast  a  request  for  information
       }



The response to a port search query can be one of:



    o port here, in which case the port search concludes successfully;

    o port here but receive or ownership transferred, in which case
      the port search concludes successfully with the port record
      updated to reflect the new owner or receiver;

    o port not here but receive and ownership rights transferred, in
      which case the port search continues by querying the new
      receiver;

    o port dead, in which case the port search concludes and the port
      is destroyed locally; or

    o port not known, in which case the port search continues by
      resorting to a broadcast query.


				  25



In addition, a query may receive no response in which case the port
search continues by resorting to a broadcast query.  To actually
transmit port search queries and responses the port search module uses
the simple request-response transport protocol.


The port search module is also responsible for authenticating a new
receiver or owner for a network port if the identity of the new
receiver or owner was obtained as a result of a broadcast search for
the port.  This authentication is only necessary is the port is being
handled securely.



9.2.   Interface



   boolean_t  ps_init()



initializes  the  port  search  module.



   ps_do_port_search(port_rec_ptr,new_information,new_nport_ptr,retry)
   port_rec_ptr_t                port_rec_ptr;
   boolean_t                         new_information;
   network_port_ptr_t          new_nport_ptr;
   int                                   (*retry)();



is called to begin a port search for the network port recorded in
port_rec_ptr.  If the caller has new_information about the port
(either the possible identity of a new receiver or owner for the port)
then that new information is contained in the network port pointed to
by new_nport_ptr.  retry is a function supplied by the client to be
called if the port search concludes successfully.  It takes as its
only parameter the port_rec_ptr.



   int  ps_handle_request(request,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an incoming port search
query.



   int  ps_handle_reply(client_id,reply,from,broadcast,crypt_level)



is called by disp_rr_simple to handle an incoming reply to a port
search query.



   int  ps_handle_auth_request(request,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an incoming request for
authentication of a receiver or owner.



   int ps_handle_auth_reply(client_id,reply,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an incoming reply to a
request for authentication of a receiver or owner.



				  26



10.   Key Management



10.1.   Description



The key management module maintains a table which maps remote hosts to
keys.  When it has to send a message securely over the network, the
IPC module checks that the key management module has a key for the
message's destination.  The actual encryption is done at the transport
level when the message data has been placed in packets.


If the key management module has no key for a particular remote host,
or the key that it possesses is obsolete, then it must call upon the
local KDS (Key Distribution Server) to do a key exchange.  The local
KDS uses a central KDS to perform the key exchange.  After the key
exchange is complete, the key management module should retry the
suspended IPC message.



10.2.   Interface



   boolean_t  km_init()



initializes the key management module.



   typedef  struct  {...}  key_t,  *key_ptr_t;



is used to hold an encryption or decryption key.



   boolean_t  km_get_key(host_id,  key_ptr)
   netaddr_t                         host_id;
   key_ptr_t                         key_ptr;



looks up the key for the host_id.  If there is a key it returns TRUE
and places the key in key_ptr.



   boolean_t  km_get_ikey(host_id,  ikey_ptr)
   netaddr_t                         host_id;
   key_ptr_t                         key_iptr;



looks up the inverse key for the host_id.  If there is a key returns
TRUE and places the key in ikey_ptr.



   km_do_key_exchange(client_id,  client_retry,  host_id)
   int                                   client_id;
   int                                   (*client_retry)();
   netaddr_t                         host_id;



is called by a client module to get a key exchange done for host_id.
When the key exchange succeeds, the key management module calls the
function client_retry with the parameter client_id to inform the
client that there is now a key for the host.



				  27



km_kds_connect(server_port, kds_port)
port_t                              server_port;
port_t                              kds_port;



is called by the local KDS to register its port (kds_port) with the
network server.



   km_use_key_for_host(server_port,  host_id,  key)
   port_t                              server_port;
   netaddr_t                         host_id;
   key_t                               key;



is called by the local KDS to tell the network server to use key for
all future communication with host_id.


In the above two calls the server_port should always be a special port
which is known only to the network server and the local KDS.  The
network server is responsible for starting the KDS and passing send
rights to this special port to the KDS.



11.   Crypt



The crypt module is responsible for the actual encryption and
decryption of packets that are to be sent out over the network and
received over the network.



11.1.   Interface



   typedef  struct  {...}  netipc_t,  *netipc_ptr_t;



points to an Internet packet encapsulated in a MACH IPC message.



   int  crypt_encrypt_packet(packet_ptr,  crypt_level)
   netipc_ptr_t                    packet_ptr;
   int                                   crypt_level;



encrypts the packet pointed to by packet_ptr at the encryption level
given by crypt_level.  Returns either CRYPT_SUCCESS or CRYPT_FAILURE
if there is no key for the remote host.



   crypt_decrypt_packet(packet_ptr, crypt_level)
   netipc_ptr_t                    packet_ptr;
   int                                   crypt_level;



decrypts the packet pointed to by packet_ptr at the encryption level
given by crypt_level.  Returns either CRYPT_SUCCESS, CRYPT_FAILURE if
there is no key for the remote host or CRYPT_CHECKSUM_FAILURE if the
decrypted checksum is incorrect.



				  28



12.   Network Name Service



12.1.   Description



The network name service module provides a simple name service that is
sufficient to boot-strap a higher-level name service that will provide
a distributed and replicated user-level name service.  The network
name service is host-directed; that is requests for name look ups are
sent to specific hosts and are not broadcast.



12.2.   Interface



   boolean_t  netname_init()



initializes the network name module.



   nn_remove_entries(port_id)
   port_t                              port_id;



removes all entries for the local port port_id from the local name
table.



   typedef  char  netname_name_t[80]



   kern_return_t  netname_check_in(ServPort,port_name,signature,port_id)
   vport_t                            ServPort;
   netname_name_t                port_name;
   port_t                              signature;
   port_t                              port_id;



checks in the port port_id under the name port_name protected by
signature.



   kern_return_t  netname_look_up(ServPort,host_name,port_name,port_id)
   port_t                              ServPort;
   netname_name_t                host_name;
   netname_name_t                port_name;
   port_t                              *port_id;



looks up port_name at host given by host_name.  Returns in port_id the
port found.



   kern_return_t  netname_check_out(ServPort,port_name,signature,port_id)
   port_t                              ServPort;
   netname_name_t                port_name;
   port_t                              signature;



checks out the port checked in under port_name.  The signature must
match the signature supplied to the netname_check_in call.



				  29



   kern_return_t  netname_version(ServPort,version)
   port_t                              ServPort;
   netname_name_t                version;



returns in version some version identification for the network server.



   int  nn_handle_request(request,from,broadcast,crypt_level)



is called by disp_indata_simple to handle an incoming request for a
network name look up.



   int  nn_handle_reply(client_id,reply,from,broadcast,crypt_level)



is called by disp_rr_simple to handle an incoming response to a
request for a network name look up.



13.   Memory Management



13.1.   Operation



The memory management module is responsible for allocating and
deallocating various objects used by the different modules, such as
port and message records, buffers, and so on.  It attempts to use
knowledge of the types of objects required to achieve good
performance.  It tries to reduce the load placed on the MACH virtual
memory system.



13.2.   Interface



   boolean_t  mem_init()



initializes the memory management module.



  int  mem_clean()



attempts to free as much unused space as possible to reduce the paging
load on the operating system; it is potentially slow.



   pointer_t  mem_allocobj(objtype)
   int                                   objtype;



allocates one instance of an object of the given objtype and returns
its address, or 0 in case of failure.



   void  mem_deallocobj(ptr,objtype)
   pointer_t                         ptr;
   int                                   objtype;


				  30



deallocates an object of objtype previously allocated using
mem_allocobj.



   pointer_t  mem_alloc(size,aligned)
   int                                   size;
   boolean_t                         aligned;



allocates a memory area of arbitrary size; it returns 0 in case of
failure.



   void  mem_dealloc(ptr,size)
   pointer_t                         ptr;
   int                                   size;



deallocates memory previously allocated by mem_dealloc.



14.   Read/Write Locks



The read/write locks module provides locks which can have multiple
readers and signals threads waiting for a lock when it becomes free.



14.1.   Interface



   typedef  enum  {PERM_READ,  PERM_READWRITE}  rw_perm_t;
   typedef  enum  {NOBLOCK  =  0,  BLOCK  =  1}  rw_block_t;
   typedef  struct  lock  {...}  *lock_t;


   lock_t  lk_alloc()



allocates a read/write lock.



   void  lk_free(lock)



   frees a read/write lock.



   int  lk_lock(lock,  perm,  block)
   lock_t                              lock;
   rw_perm_t                         perm;
   rw_block_t                       block;



locks the lock for type perm.  If block is true, then this calls
blocks waiting until the lock can be obtained, otherwise the function
returns 0 if the lock cannot be obtained.



   void  lk_unlock(lock)
   lock_t                              lock;



unlocks the lock.


				  31



15.   Locked Queue Module



The locked queue module provides functions to manipulate items on
queues.  When a queue is accessed it is always locked before being
manipulated.



15.1.   Interface



   typedef  struct  {...}  *lock_queue_t;
   typedef  struct  queue_item  {struct  queue_item  *next}  *queue_item_t;



   lock_queue_t  lq_alloc()



allocates and initializes a new locked queue.



   void  lq_init_queue(queue)
   lock_queue_t                    queue;



re-initializes the already allocated queue.



   void  lq_prequeue(queue,  item)
   lock_queue_t                    queue;
   queue_item_t                    item;



inserts item at the head of queue.



   void  lq_insert_in_queue(queue,  test,  item,  args)
   lock_queue_t                    queue;
   int                                   (*test)();
   queue_item_t                    item;
   int                                   arg;



inserts item in the ``correct'' position on queue.  The correct
position is determined by calling the user-supplied function test on
item, arg and the members of queue until it returns TRUE.



   boolean_t  lq_remove_from_queue(queue,  item)
   lock_queue_t                    queue;
   queue_item_t                    item;



removes item from queue if item is present on the queue.  Returns TRUE
is item was deleted from queue, FALSE otherwise.



   boolean_t  lq_cond_delete_from_queue(queue,  test,  item)
   lock_queue_t                    queue;
   int                                   (*test)();
   queue_item_t                    item;
   int                                   arg;


				  32



performs the user-supplied function test on item, arg and on
successive elements of queue.  If it returns TRUE, then the current
element of the queue is deleted.



   boolean_t  lq_on_queue(queue,  item)
   lock_queue_t                    queue;
   queue_item_t                    item;



checks to see if the item is on queue.



   queue_item_t  lq_dequeue(queue)
   lock_queue_t                    queue;



if queue is not empty remove and return the queue item which is at the
head of it.



   queue_item_t  lq_blocking_dequeue(queue)
   lock_queue_t                    queue;



if queue is empty, a wait is done until it is non-empty.  Removes and
returns the queue item which is at the head of queue.



   void  lq_enqueue(queue,  item);
   lock_queue_t                    queue;
   queue_item_t                    item;



inserts item at the tail of queue.



   queue_item_t  lq_find_in_queue(queue,  fn,  args)
   lock_queue_t                    queue;
   int                                   (*fn)();
   int                                   arg;



returns a queue_item_t which is found by applying the user-supplied
function fn to successive elements of queue and arg until fn returns
TRUE.



   void  lq_map_queue(queue,  fn,  args);
   lock_queue_t                    queue;
   int                                   (*fn)();
    int                                   arg;



applies the user-supplied function fn to each successive item of queue
and arg.


In addition to the above routines, a number of equivalent routines are
provided that do not acquire or release the queue lock when invoked,
to be used in situations where global lock management is needed to
avoid deadlock.  Those routines are prefixed with lqn_ instead of lq_.


Finally, the network server also uses doubly-linked lists for some
queues.  using the same macros used in the Mach kernel for that
purpose.


				  33



16.   Timer Module



The timer module accepts requests from other modules for events to be
scheduled at some time in the future.  When the event's deadline
expires the timer module calls the user-supplied function associated
with the timer.



16.1.   Interface



   boolean_t  timer_init()



initializes the timer module.



   struct  timer  {...}  *timer_t;


   timer_t timer_alloc()



returns a new timer.



   void  timer_start(timer)
   timer_t                            timer;



starts up timer.



   void  timer_stop(timer)
   timer_t                            timer;



stops timer.



17.   Miscellaneous



17.1.   Unique Identifer Generator



Simply generates locally unique identifiers (UIDs).  The identifiers
generated are unique with high probability.



17.1.1.   Interface



   void  uid_init()



initializes the UID module.



   long  uid_get_new_uid()



returns a new UID.


				  34



17.2.   Sbuf



The sbuf module provides macros that manipulate sbufs.



17.2.1.   Interface



   void  sbuf_printf(where,  sb_ptr)
   FILE                                 *where;
   sbuf_ptr_t                       sb_ptr;



is the only exported function of the sbuf module.  It prints out the
contents of the sbuf pointed to by sb_ptr.



17.3.   Network Interfaces



Under Mach the interface to the network is an IPC interface with a
filter inside the kernel determining which network packets are to be
received by the network server.  Currently, many transport modules
still use BSD Unix sockets to access network protocol implementations
in the kernel.



17.3.1.   Interface



   int  netipc_receive(pkt_ptr)
   netipc_ptr_t                    pkt_ptr;



waits to receive a packet from the kernel.  Checks the packet's UDP
checksum before returning to the caller.



   int  netipc_send(pkt_ptr)
   netipc_ptr_t                    pkt_ptr;



calculates the UDP checksum for the packet and then sends it to the
kernel for transmission over the network.



17.4.   IPC Message Receive



17.5.   Interface



   int  netmsg_receive(msg_ptr)
   msg_header_t                    *msg_ptr;



does a non-blocking receive for a local IPC message.



				  35



17.6.   Debugging



The network server keeps a log in memory of various events happening
during its operation.  This log, along with statistics on various
operations, can be obtained via the logstat service exported by the
network server.  In addition, many operating parameters, including the
level of debugging information written to the log, can be set using
this same service.



17.6.1.   Interface



Macros and procedures called within the network server



   DEBUGn(condition,print_level,code,arg1,...,argn)



is a macro to be used to write a record containing the code and all
the integer args into the log.  n is a number between 0 and 6,
indicating how many integers must be copied into the log.  A log entry
is only made if condition evaluates to TRUE.  In addition, if
print_level is greater or equal to the global debug.print_level, a
message is printed on stderr.



   DEBUG_STRING(cond,level,string)
   DEBUG_NPORT(cond,level,nport)
   DEBUG_NETADDR(cond,level,netaddr)
   DEBUG_KEY(cond,level,key)
   DEBUG_SBUF(cond,level,sbuf)



are similar to the DEBUGn macros, but are used to enter a string, a
network port identifier, a network address, an encryption key or an
sbuf into the log.


The DEBUG macros can be made to expand to nothing via a compile-time
switch to avoid overheads at execution time.  Each of those macros has
an equivalent LOG macro that can be enabled or disabled independently;
those LOG macros are intended for events that should always be entered
in the log and are infrequent enough that the overhead involved is
negligible.



   ERROR((msg,format,args...))



is used to print out a message on stderr an make an entry in the log.
The argument should be a valid set of arguments for sprintf, with the
message string msg.



   void  panic(error_msg)
   char                                 *error_msg;



is called if something catastrophic happens.  Prints out the
error_msg, dumps the log and terminates the network server.



   void  ipaddr_to_string(output_string,  input_address)
   char                                 *output_string;
   netaddr_t                         input_address;



				  36



Translates the input_address IP address into a printable
representation in output_string.



Procedures exported outside the network server: The following
procedures can be called remotely by sending requests on a port
checked-in as NM_LOGSTAT in the network server.



   kern_return_t  ls_sendlog(ServPort,old_log_ptr,old_log_size,
                                           cur_log_ptr,cur_log_size)
   port_t                ServPort;
   log_ptr_t           *old_log_ptr;
   unsigned  int      *old_log_size;
   log_ptr_t           *cur_log_ptr;
   unsigned  int      *cur_log_size;



is used to obtain both network server logs in the response message.
The old and new logs correspond to the two alternating logs used to
record events.



   kern_return_t  ls_resetlog(ServPort)
   port_t                ServPort;



resets the log to zero size.



   kern_return_t  ls_writelog(ServPort)
   port_t                ServPort;



causes the network server to write its log in a file NMLOG in its
current working directory.



   kern_return_t  ls_sendstat(ServPort,stat_ptr,stat_size)
   port_t                ServPort;
   stat_ptr_t          *stat_ptr;
   unsigned  int      *stat_size;



is used to obtain a record with the vital network server statistics in
the response.



   kern_return_t  ls_resetstat(ServPort)
   port_t                ServPort;



resets all statistics counters to zero.



   kern_return_t  ls_senddebug(ServPort,debug_ptr,debug_size)
   port_t                ServPort;
   debug_ptr_t        *debug_ptr;
   unsigned  int      *debug_size;



is used to obtain a record with all the debugging flags used to
control the operation of the DEBUG macros.


				  37\



   kern_return_t  ls_setdebug(ServPort,debug_ptr,debug_size)
   port_t                ServPort;
   debug_ptr_t        *debug_ptr;
   unsigned  int      *debug_size;



is used to replace the record with all the debugging flags used to
control the operation of the DEBUG macros.



   kern_return_t  ls_sendparam(ServPort,param_ptr,param_size)
   port_t                ServPort;
   param_ptr_t        *param_ptr;
   unsigned  int      *param_size;



is used to obtain a record with the network server control parameters.



   kern_return_t  ls_setparam(ServPort,param_ptr,param_size)
   port_t                ServPort;
   param_ptr_t        *param_ptr;
   unsigned  int      *param_size;



is used to replace the record with the network server control
parameters.



   kern_return_t  ls_sendportstat(ServPort,port_stat_ptr,port_stat_size)
   port_t                ServPort;
   port_stat_ptr_t  *port_stat_ptr;
   unsigned  int      *port_stat_size;



is used to obtain a record with the port record statistics.



17.7.   Camelot Support



The Camelot Distributed Transaction Facility [3 ] requires special
handling for IPC messages used in Camelot transactions.  This handling
is performed in a special Camelot module, not described, here, that
behaves as an extra step in the translation process for incoming and
outgoing IPC messages.


In addition, Camelot also requires some specialized name servers, also
implemented in the Camelot module.



17.8.   Kernel Netport Support



Certain Mach kernels provide an experimental feature, called Netport
or MACH_NP with which Kernel port records may be flagged as
corresponding to local representatives for remote network ports.
Under certain very restricted conditions, the kernel may, upon
processing a message destined for one of these ports, send the message
directly to the remote node instead of handing it to the network
server.  This scheme results in improved performance by avoiding the
overhead of invoking the network servers on both ends of the
communication.  Correctness is assured by having the kernel abort its
transmission and


				  38



reflect the message back to the network server as soon as a situation
arises that is too complex for the Netport code to handle.


When enabled, all modules in the network server that modify network
port records enter the correct information in the kernel port records
to allow the Netport code to function.



17.9.   Initialization



The network server initialization sequence takes care of detecting
modules that require kernel support not present on the current node,
and of setting the working parameters accordingly.  These include:



    o Access to a network interface.  If there is no network, the
      network server degenerates into a simple local Name Server, as
      specified by the conf_network parameter.

    o Netport support: controlled by the conf_netport parameter.

    o VMTP support.  The transport_default parameter is set to the
      index of the best transport protocol available.



17.9.1.   Interface



   boolean_t  nm_init()



initializes the network server by calling and checking the error
returns for all the module initialization functions.




Appendix



A   Compiling a Network Server



The various configuration options for the Network Server are all
defined in the file config.h, which should simply be edited before
compiling the system.  The option settings in the file as distributed
are suitable for a normal generic configuration.


The configuration options are:



NET_LOG enable the LOGn macros.

NET_DEBUG enable the DEBUGn macros.

NET_TRACE enable tracing of procedure calls, under control of a
	command line switch.

NET_PRINT enable printing from the LOG and DEBUG macros.

LOCK_THREADS do not allow more than one thread to run at any one time.
	To use only for debugging.

NM_STATISTICS enable normal statistics gathering.

NETPORT enable entering information in the kernel port records for use
	by the Netport option.

PORTSTAT enable port statistics gathering.


				  39



RPCMOD 	enable the RPC optimization, and the request-response
	transport
	interface.  Should always be on.

COMPAT 	enable special operating mode for compatibility with the
	previous implementation (Mach 1.0 and 2.0) of the Network Server.

NOTIFY	explicitly allocate a notify port, which is not created by
	default in newer versions of the Mach kernel.

CAMELOT	include the Camelot module in the network server.

NM_USE_KDS use an external Key Distribution Server.

USE_VMTP include the VMTP transport module in the network server.

USE_DELTAT include the Delta-t transport module in the network server.

USE_CRYPT include the Crypt module in the network server.

USE_DES include the DES encryption module in the network server.

USE_MULTPERM include the ``multiple permutations'' encryption module
	in the network server.

USE_NEWDES include the ``new'' DES encryption module in the network
	server.

USE_XOR include the ``exclusive or'' encryption module in the network
	server.

USE_KEYMAN include the keymanager module in the network server.

USE_TCP	include the TCP transport module in the network server.

USE_DATAGRAM include the DATAGRAM transport module in the network
	server.

USE_SRR include the SRR transport module in the network server.



Both USE_VMTP and NETPORT require kernel support that is not normally
present.  Normally, USE_TCP, USE_SRR and USE_DATAGRAM should always be
enabled for the system to work.


In addition to the configuration options, the file config.h also
contains all the definitions needed to compile the network server on
various architectures.  It is the only file that should be modified
when porting the network server to a new architecture.



References


[1] Cheriton, D.  VMTP: A Transport Protocol for the Next Generation of
    Communication Systems.  In: Proceedings of the ACM SIGCOMM 86
    Symposium on Communications Architectures and Protocols.  ACM, 1986,
    pp. 406-415.
      
[2] Sansom, R. D., Julin, D. P., and Rashid, R. F. Extending a
    Capability Based System into a Network Environment.  In: SIGCOMM
    '86 Symposium: Communications Architectures & Protocols, ACM
    SIGCOMM.  1986.  Also available as Technical Report CMU-CS-86-115.

[3] Spector, A. Z., Bloch, J. J., Daniels, D. S., Draves, R. P.,
    Duchamp, D., Eppinger, J. L., Menees, S. G., and Thompson, D. S.
    The Camelot Project.  Database Engineering, vol. 9 (1986).  Also
    available as Technical Report CMU-CS-86-166, Carnegie-Mellon
    University, November 1986.