## Slide 1
Randal E. Bryant
Carnegie Mellon University
CS:APP3e
CS:APP Chapter 4
Computer Architecture
Pipelined
Implementation
Part I
http://csapp.cs.cmu.edu

## Slide 2: Overview
General Principles of Pipelining
  Goal
  Difficulties
Creating a Pipelined Y86-64 Processor
  Rearranging SEQ
  Inserting pipeline registers
  Problems with data and control hazards

## Slide 3: Real-World Pipelines: Car Washes
Idea
  Divide process into independent stages
  Move objects through stages in sequence
  At any given times, multiple objects being processed
Sequential
Parallel
Pipelined

## Slide 4: Computational Example
System
  Computation requires total of 300 picoseconds
  Additional 20 picoseconds to save result in register
  Must have clock cycle of at least 320 ps
Combinational
logic
R
e
g
300 ps
20 ps
Clock
Delay = 320 ps
Throughput = 3.12 GIPS

## Slide 5: 3-Way Pipelined Version
System
  Divide combinational logic into 3 blocks of 100 ps each
  Can begin new operation as soon as previous one passes through stage A.
    Begin new operation every 120 ps
  Overall latency increases
    360 ps from start to finish
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Delay = 360 ps
Throughput = 8.33 GIPS

## Slide 6: Pipeline Diagrams
Unpipelined
  Cannot start new operation until previous one completes
3-Way Pipelined
  Up to 3 operations in process simultaneously
Time
OP1
OP2
OP3
Time
A
B
C
A
B
C
A
B
C
OP1
OP2
OP3

## Slide 7: Operating a Pipeline
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
0
120
240
360
480
640
Clock
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
239
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
241
R
e
g
R
e
g
R
e
g
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Comb.
logic
A
Comb.
logic
B
Comb.
logic
C
Clock
300
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
359

## Slide 8: Limitations: Nonuniform Delays
  Throughput limited by slowest stage
  Other stages sit idle for much of the time
  Challenging to partition system into balanced stages
R
e
g
Clock
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
50 ps
20 ps
150 ps
20 ps
100 ps
20 ps
Delay = 510 ps
Throughput = 5.88 GIPS
Comb.
logic
A
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C

## Slide 9: Limitations: Register Overhead
  As try to deepen pipeline, overhead of loading registers becomes more significant
  Percentage of clock cycle spent loading register:
    1-stage pipeline: 6.25%
    3-stage pipeline: 16.67%
    6-stage pipeline: 28.57%
  High speeds of modern processor designs obtained through very deep pipelining
Delay = 420 ps, Throughput = 14.29 GIPS
Clock
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps

## Slide 10: Data Dependencies
System
  Each operation depends on result from preceding one
Clock
Combinational
logic
R
e
g
Time
OP1
OP2
OP3

## Slide 11: Data Hazards
  Result does not feed back around in time for next operation
  Pipelining has changed behavior of system
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
OP4
A
B
C

## Slide 12: Data Dependencies in Processors
  Result from one instruction used as operand for another
    Read-after-write (RAW) dependency
  Very common in actual programs
  Must make sure our pipeline handles these properly
    Get correct results
    Minimize performance impact
1 irmovq $50, %rax
2 addq %rax , %rbx
3 mrmovq 100( %rbx ), %rdx

## Slide 13: SEQ Hardware
  Stages occur in sequence
  One operation in process at a time

## Slide 14: SEQ+ Hardware
  Still sequential implementation
  Reorder PC stage to put at beginning
PC Stage
  Task is to select PC for current instruction
  Based on results computed by previous instruction
Processor State
  PC is no longer stored in register
  But, can determine PC based on other stored information

## Slide 15: Adding Pipeline Registers
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 16: Pipeline Stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Read program registers
Execute
  Operate ALU
Memory
  Read or write data memory
Write Back
  Update register file

## Slide 17: PIPE- Hardware
  Pipeline registers hold intermediate values from instruction execution
Forward (Upward) Paths
  Values passed from one stage to next
  Cannot jump past stages
    e.g., valC passes through decode

## Slide 18: Signal Naming Conventions
S_Field
  Value of Field held in stage S pipeline register
s_Field
  Value of Field computed in stage S

## Slide 19: Feedback Paths
Predicted PC
  Guess value of next PC
Branch information
  Jump taken/not-taken
  Fall-through or target address
Return point
  Read from memory
Register updates
  To register file write ports

## Slide 20: Predicting the PC
  Start fetch of new instruction after current one has completed fetch stage
    Not enough time to reliably determine next instruction
  Guess which instruction will follow
    Recover if prediction was incorrect

## Slide 21: Our Prediction Strategy
Instructions that Don’t Transfer Control
  Predict next PC to be valP
  Always reliable
Call and Unconditional Jumps
  Predict next PC to be valC (destination)
  Always reliable
Conditional Jumps
  Predict next PC to be valC (destination)
  Only correct if branch is taken
    Typically right 60% of time
Return Instruction
  Don’t try to predict

## Slide 22: Recovering from PC Misprediction
  Mispredicted Jump
    Will see branch condition flag once instruction reaches memory stage
    Can get fall-through PC from valA (value M_valA)
  Return Instruction
    Will get return PC when ret reaches write-back stage (W_valM)

## Slide 23: Pipeline Demonstration
File: demo-basic.ys
irmovq $1,%rax #I1
1
2
3
4
5
6
7
8
9
F
D
E
M
W
irmovq $2,%rcx #I2
F
D
E
M
W
irmovq $3,%rdx #I3
F
D
E
M
W
irmovq $4,%rbx #I4
F
D
E
M
W
halt #I5
F
D
E
M
W
Cycle 5
W
I1
M
I2
E
I3
D
I4
F
I5

## Slide 24: Data Dependencies: 3 Nop’s
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
nop
F
D
E
M
W
F
D
E
M
W
0x016:
nop
F
D
E
M
W
F
D
E
M
W
0x017:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
10
W
R[
%
rax
]
f
3
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
3
# demo-h3.ys
Cycle 6
11
0x019: halt
F
D
E
M
W
F
D
E
M
W
Cycle 7

## Slide 25: Data Dependencies: 2 Nop’s
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
nop
F
D
E
M
W
F
D
E
M
W
0x016:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
0x018: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
•
•
•
W
R[
%
rax
]
f
3
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
•
•
•
Cycle 6
Error

## Slide 26: Data Dependencies: 1 Nop
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
0x017: halt
F
D
E
M
W
F
D
E
M
W
# demo-h1.ys
W
R[
%
rdx
]
f
10
W
R[
%
rdx
]
f
10
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
•
•
•
Cycle 5
Error
M
M_
valE
= 3
M_
dstE
=
%
rax

## Slide 27: Data Dependencies: No Nop
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
addq
%
rdx
,%
rax
F
D
E
M
W
0x016: halt
# demo-h0.ys
E
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
Cycle 4
Error
M
M_
valE
= 10
M_
dstE
=
%
rdx
e_
valE
f
0 + 3 = 3
E_
dstE
=
%
rax

## Slide 28: Branch Misprediction Example
  Should only execute first 8 instructions
0x000: xorq %rax,%rax
0x002: jne t # Not taken
0x00b: irmovq $1, %rax # Fall through
0x015: nop
0x016: nop
0x017: nop
0x018: halt
0x019: t: irmovq $3, %rdx # Target (Should not execute)
0x023: irmovq $4, %rcx # Should not execute
0x02d: irmovq $5, %rdx # Should not execute
demo-j.ys

## Slide 29: Branch Misprediction Trace
  Incorrectly execute two instructions at branch target
0x000:
xorq
%
rax
,%
rax
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x002:
jne
t # Not taken
F
D
E
M
W
0x019: t:
irmovq
$3, %
rdx
# Target
F
D
E
M
W
0x023:
irmovq
$4, %
rcx
# Target+1
F
D
E
M
W
0x00b:
irmovq
$1, %
rax
# Fall Through
F
D
E
M
W
# demo
-
j
F
D
E
M
W
Cycle 5
E
valE
f
3
dstE
=
%
rdx
E
valE
f
3
dstE
=
%
rdx
M
M_Cnd =
0
M_
valA
= 0x007
D
valC
=
4
dstE
=
%
ecx
D
valC
=
4
dstE
=
%
rcx
F
valC
f
1
rB
f
%
rax
F
valC
f
1
rB
f
%
rax

## Slide 30: Return Example
0x000: irmovq Stack,%rsp # Intialize stack pointer
0x00a: nop # Avoid hazard on %rsp
0x00b: nop
0x00c: nop
0x00d: call p # Procedure call
0x016: irmovq $5,%rsi # Return point
0x020: halt
0x020: .pos 0x20
0x020: p: nop # procedure
0x021: nop
0x022: nop
0x023: ret
0x024: irmovq $1,%rax # Should not be executed
0x02e: irmovq $2,%rcx # Should not be executed
0x038: irmovq $3,%rdx # Should not be executed
0x042: irmovq $4,%rbx # Should not be executed
0x100: .pos 0x100
0x100: Stack: # Initial stack pointer
  Require lots of nops to avoid data hazards
demo-ret.ys

## Slide 31: Incorrect Return Example
  Incorrectly execute 3 instructions following ret

## Slide 32: Pipeline Summary
Concept
  Break instruction execution into 5 stages
  Run instructions through in pipelined mode
Limitations
  Can’t handle dependencies between instructions when instructions follow too closely
  Data dependencies
    One instruction writes register, later one reads it
  Control dependency
    Instruction sets PC in way that pipeline did not predict correctly
    Mispredicted branch and return
Fixing the Pipeline
  We’ll do that next time