## Slide 1
14-513
18-613

## Slide 2: Code Optimization 18-213/18-613: Introduction to Computer Systems 9th Lecture, May 30th, 2024

## Slide 3: Performance Realities
There’s more to performance than asymptotic complexity
Constant factors matter too!
  Easily see 10:1 performance range depending on how code is written
  Must optimize at multiple levels:
    algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs are compiled and executed
  How modern processors + memory systems operate
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 4: Optimizing Compilers
Provide efficient mapping of program to machine
  register allocation
  code selection and ordering (scheduling)
  dead code elimination
  eliminating minor inefficiencies
Don’t (usually) improve asymptotic efficiency
  up to programmer to select best overall algorithm
  big-O savings are (often) more important than constant factors
    but constant factors also matter
Have difficulty overcoming “optimization blockers”
  potential procedure side-effects
  potential memory aliasing

## Slide 5: Today
Generally Useful Optimizations CSAPP 5.1
  Code motion/precomputation
  Strength reduction
  Sharing of common subexpressions
  Example: Bubblesort
Optimization Blockers CSAPP 5.1
  Procedure calls
  Memory aliasing
Exploiting Instruction-Level Parallelism CSAPP 5.2-5.10
Dealing with Conditionals CSAPP 5.11

## Slide 6
Rear Admiral Grace Hopper (1906-1992)
  Invented first compiler in 1951 (technically it was a linker)
  Coined “compiler” (and “bug”)
  Compiled for Harvard Mark I
  Eventually led to COBOL (which ran the world for years)
  “I decided data processors ought to be able to write their programs in English, and the computers would translate them into machine code”

## Slide 7: Generally Useful Optimizations
Optimizations that you or the compiler should do regardless of processor / compiler
Code Motion
  Reduce frequency with which computation performed
    If it will always produce same result
    Especially moving code out of loop
long j;
int ni = n*i;
for (j = 0; j < n; j++)
a[ni+j] = b[j];
void set_row(double *a, double *b,
long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}

## Slide 8: Compiler-Generated Code Motion (-O1)
set_row:
testq %rcx, %rcx # Test n
jle .L1 # If <= 0, goto done
imulq %rcx, %rdx # ni = n*i
leaq (%rdi,%rdx,8), %rdx # rowp = A + ni*8
movl $0, %eax # j = 0
.L3: # loop:
movsd (%rsi,%rax,8), %xmm0 # t = b[j]
movsd %xmm0, (%rdx,%rax,8) # M[A+ni*8 + j*8] = t
addq $1, %rax # j++
cmpq %rcx, %rax # j:n
jne .L3 # if !=, goto loop
.L1: # done:
rep ; ret
long j;
long ni = n*i;
double *rowp = a+ni;
for (j = 0; j < n; j++)
*rowp++ = b[j];
void set_row(double *a, double *b,
long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}
Notes: Note that the compiler did more than just pull n*i out of the loop

## Slide 9: Strength Reduction
  Replace costly operation with simpler one
  Shift, add instead of multiply or divide
    16*x x << 4
    Utility is machine dependent
    Depends on cost of multiply or divide instruction
      Intel Nehalem: integer multiply takes 3 CPU cycles, add is 1 cycle1
  Recognize sequence of products
for (i = 0; i < n; i++) {
int ni = n*i;
for (j = 0; j < n; j++)
a[ni + j] = b[j];
}
int ni = 0;
for (i = 0; i < n; i++) {
for (j = 0; j < n; j++)
a[ni + j] = b[j];
ni += n;
}
1https://www.agner.org/optimize/instruction_tables.pdf

## Slide 10: Share Common Subexpressions
  Reuse portions of expressions
  GCC will do this with –O1
/* Sum neighbors of i,j */
up = val[(i-1)*n + j ];
down = val[(i+1)*n + j ];
left = val[i*n + j-1];
right = val[i*n + j+1];
sum = up + down + left + right;
long inj = i*n + j;
up = val[inj - n];
down = val[inj + n];
left = val[inj - 1];
right = val[inj + 1];
sum = up + down + left + right;
3 multiplications: i*n, (i–1)*n, (i+1)*n
1 multiplication: i*n
leaq 1(%rsi), %rax # i+1
leaq -1(%rsi), %r8 # i-1
imulq %rcx, %rsi # i*n
imulq %rcx, %rax # (i+1)*n
imulq %rcx, %r8 # (i-1)*n
addq %rdx, %rsi # i*n+j
addq %rdx, %rax # (i+1)*n+j
addq %rdx, %r8 # (i-1)*n+j
...
imulq %rcx, %rsi # i*n
addq %rdx, %rsi # i*n+j
movq %rsi, %rax # i*n+j
subq %rcx, %rax # i*n+j-n
leaq (%rsi,%rcx), %rcx # i*n+j+n
...

## Slide 11: Optimization Example: Bubblesort
Bubblesort program that sorts an array A that is allocated in static storage:
  an element of A requires four bytes
  elements of A are numbered 1 through n (n is a variable)
  A[j] is in location &A+4*(j-1)
for (i = n-1; i >= 1; i--) {
for (j = 1; j <= i; j++)
if (A[j] > A[j+1]) {
temp = A[j];
A[j] = A[j+1];
A[j+1] = temp;
}
}

## Slide 12: Translated (Pseudo) Code
i := n-1
L5: if i<1 goto L1
j := 1
L4: if j>i goto L2
t1 := j-1
t2 := 4*t1
t3 := A[t2] // A[j]
t4 := j+1 t5 := t4-1
t6 := 4*t5
t7 := A[t6] // A[j+1]
if t3<=t7 goto L3
t8 := j-1
t9 := 4*t8
temp := A[t9] // temp:=A[j]
t10 := j+1
t11:= t10-1
t12 := 4*t11
t13 := A[t12] // A[j+1]
t14 := j-1
t15 := 4*t14
A[t15] := t13 // A[j]:=A[j+1]
t16 := j+1
t17 := t16-1
t18 := 4*t17
A[t18]:=temp // A[j+1]:=temp
L3: j := j+1
goto L4
L2: i := i-1
goto L5
L1:
for (i = n-1; i >= 1; i--) {
for (j = 1; j <= i; j++)
if (A[j] > A[j+1]) {
temp = A[j];
A[j] = A[j+1];
A[j+1] = temp;
}
}
Instructions
29 in outer loop
25 in inner loop

## Slide 13: Redundancy in Address Calculation
i := n-1
L5: if i<1 goto L1
j := 1
L4: if j>i goto L2
t1 := j-1
t2 := 4*t1
t3 := A[t2] // A[j]
t4 := j+1 t5 := t4-1
t6 := 4*t5
t7 := A[t6] // A[j+1]
if t3<=t7 goto L3
t8 :=j-1
t9 := 4*t8
temp := A[t9] // temp:=A[j]
t10 := j+1
t11:= t10-1
t12 := 4*t11
t13 := A[t12] // A[j+1]
t14 := j-1
t15 := 4*t14
A[t15] := t13 // A[j]:=A[j+1]
t16 := j+1
t17 := t16-1
t18 := 4*t17
A[t18]:=temp // A[j+1]:=temp
L3: j := j+1
goto L4
L2: i := i-1
goto L5
L1:
Notes: t4 & t5 add 1 and then subtract 1. Same for t10 & t11.
t18 is same as t12.
t9 is (j-1)*4  reuse t9 to avoid recomputing in t15.

## Slide 14: Redundancy Removed
i := n-1
L5: if i<1 goto L1
j := 1
L4: if j>i goto L2
t1 := j-1
t2 := 4*t1
t3 := A[t2] // A[j]
t6 := 4*j
t7 := A[t6] // A[j+1]
if t3<=t7 goto L3
t8 :=j-1
t9 := 4*t8
temp := A[t9] // temp:=A[j]
t12 := 4*j
t13 := A[t12] // A[j+1]
A[t9]:= t13 // A[j]:=A[j+1]
A[t12]:=temp // A[j+1]:=temp
L3: j := j+1
goto L4
L2: i := i-1
goto L5
L1:
Instructions
20 in outer loop
16 in inner loop

## Slide 15: More Redundancy
i := n-1
L5: if i<1 goto L1
j := 1
L4: if j>i goto L2
t1 := j-1
t2 := 4*t1
t3 := A[t2] // A[j]
t6 := 4*j
t7 := A[t6] // A[j+1]
if t3<=t7 goto L3
t8 :=j-1
t9 := 4*t8
temp := A[t9] // temp:=A[j]
t12 := 4*j
t13 := A[t12] // A[j+1]
A[t9]:= t13 // A[j]:=A[j+1]
A[t12]:=temp // A[j+1]:=temp
L3: j := j+1
goto L4
L2: i := i-1
goto L5
L1:
Notes: Notice: t3 is old value of A[j].
Notice: t7 is unmodified A[j+1]
Notice: t2 is offset for j, t6 is offset for j+1
Reuse these values!

## Slide 16: Redundancy Removed
A[t2] := t7 // A[j]:=A[j+1]
A[t6] := t3 // A[j+1]:=old_A[j]
L3: j := j+1
goto L4
L2: i := i-1
goto L5
L1:
i := n-1
L5: if i<1 goto L1
j := 1
L4: if j>i goto L2
t1 := j-1
t2 := 4*t1
t3 := A[t2] // old_A[j]
t6 := 4*j
t7 := A[t6] // A[j+1]
if t3<=t7 goto L3
Instructions
15 in outer loop
11 in inner loop
Notes: t2 is offset for j
t6 is offset for j+1
t7 is A[j + 1]
t3 is old A[j]

## Slide 17: Redundancy in Loops
A[t2] := t7
A[t6] := t3
L3: j := j+1
goto L4
L2: i := i-1
goto L5
L1:
i := n-1
L5: if i<1 goto L1
j := 1
L4: if j>i goto L2
t1 := j-1
t2 := 4*t1
t3 := A[t2] // A[j]
t6 := 4*j
t7 := A[t6] // A[j+1]
if t3<=t7 goto L3

## Slide 18: Redundancy Eliminated
i := n-1
L5: if i<1 goto L1
t2 := 0
t6 := 4
t19 := 4*i
L4: if t6>t19 goto L2
t3 := A[t2]
t7 := A[t6]
if t3<=t7 goto L3
A[t2] := t7
A[t6] := t3
L3: t2 := t2+4
t6 := t6+4
goto L4
L2: i := i-1
goto L5
L1:
A[t2] := t7
A[t6] := t3
L3: j := j+1
goto L4
L2: i := i-1
goto L5
L1:
i := n-1
L5: if i<1 goto L1
j := 1
L4: if j>i goto L2
t1 := j-1
t2 := 4*t1
t3 := A[t2] // A[j]
t6 := 4*j
t7 := A[t6] // A[j+1]
if t3<=t7 goto L3
Notes: Put array indices in registers and increment by 4 on each loop iteration
Avoids redundant refetching j and recomputing indices (in t2 and t6)

## Slide 19: Final Pseudo Code (after strength reduction)
A[t2] := t7
A[t6] := t3
L3: t2 := t2+4
t6 := t6+4
goto L4
L2: i := i-1
goto L5
L1:
i := n-1
L5: if i<1 goto L1
t2 := 0
t6 := 4
t19 := i << 2
L4: if t6>t19 goto L2
t3 := A[t2]
t7 := A[t6]
if t3<=t7 goto L3
These were Machine-Independent Optimizations.
Will be followed by Machine-Dependent Optimizations, including allocating temporaries to registers, converting to assembly code
Instructions
Before Optimizations
29 in outer loop
25 in inner loop
Instructions
After Optimizations
15 in outer loop
9 in inner loop

## Slide 20: Today
Generally Useful Optimizations
  Code motion/precomputation
  Strength reduction
  Sharing of common subexpressions
  Example: Bubblesort
Optimization Blockers
  Procedure calls
  Memory aliasing
Exploiting Instruction-Level Parallelism
Dealing with Conditionals

## Slide 21
John Backus (1924-2007)
  Led team at IBM invented the first commercially available compiler in 1957
  Compiled FORTRAN code for the IBM 704 computer
  FORTRAN still in use today for high performance code
  “Much of my work has come from being lazy. I didn't like writing programs, and so, when I was working on the IBM 701, I started work on a programming system to make it easier to write programs”

## Slide 22: Limitations of Optimizing Compilers
Operate under fundamental constraint
  Must not cause any change in program behavior
  Often prevents optimizations that affect only “edge case” behavior
Behavior obvious to the programmer is not obvious to compiler
  e.g., Data range may be more limited than types suggest (short vs. int)
Most analysis is only within a procedure
  Whole-program analysis is usually too expensive
  Sometimes compiler does interprocedural analysis within a file (new GCC)
Most analysis is based only on static information
  Compiler has difficulty anticipating run-time inputs
When in doubt, the compiler must be conservative

## Slide 23: Optimization Blocker #1: Procedure Calls
Procedure to Convert String to Lower Case
  Extracted from 213 lab submissions
void lower1(char *s)
{
size_t i;
for (i = 0; i < strlen(s); i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}

## Slide 24: Lower Case Conversion Performance
  Time quadruples when double string length
  Quadratic performance
Chart: String length
| 0 | 20000 | 40000 | 60000 | 80000 | 100000 | 120000 | 140000 | 160000 | 180000 | 200000 | 220000 | 240000 | 260000 | 280000 | 300000 | 320000 | 340000 | 360000 | 380000 | 400000 | 420000 | 440000 | 460000 | 480000 | 500000
lower1 | 0 | 0.38248 | 1.529 | 3.4395 | 6.1139 | 9.5526 | 13.7543 | 18.7211 | 24.4512 | 30.9457 | 38.2044 | 46.2266 | 55.0139 | 64.565 | 74.88 | 85.968 | 97.8095 | 110.4161 | 123.7965 | 137.9369 | 152.8305 | 168.486 | 184.9165 | 202.1147 | 220.0625 | 238.8073
lower1

## Slide 25: Calling Strlen
Strlen performance
  Only way to determine length of string is to scan its entire length, looking for null character.
Overall performance, string of length N
  N calls to strlen (called every time through the loop)
  Require times N, N-1, N-2, …, 1
  Overall O(N2) performance
/* My version of strlen */
size_t strlen(const char *s)
{
size_t length = 0;
while (*s != '\0') {
s++;
length++;
}
return length;
}
void lower1(char *s)
{
size_t i;
for (i = 0; i < strlen(s); i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}

## Slide 26: Improving Performance
  Move call to strlen outside of loop
  Legal since result does not change from one iteration to another
  Form of code motion
void lower2(char *s)
{
size_t i;
size_t len = strlen(s);
for (i = 0; i < len; i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}

## Slide 27: Lower Case Conversion Performance
  Time doubles when double string length
  Linear performance of lower2
Chart: String length
| 0 | 20000 | 40000 | 60000 | 80000 | 100000 | 120000 | 140000 | 160000 | 180000 | 200000 | 220000 | 240000 | 260000 | 280000 | 300000 | 320000 | 340000 | 360000 | 380000 | 400000 | 420000 | 440000 | 460000 | 480000 | 500000
lower1 | 0 | 0.38248 | 1.529 | 3.4395 | 6.1139 | 9.5526 | 13.7543 | 18.7211 | 24.4512 | 30.9457 | 38.2044 | 46.2266 | 55.0139 | 64.565 | 74.88 | 85.968 | 97.8095 | 110.4161 | 123.7965 | 137.9369 | 152.8305 | 168.486 | 184.9165 | 202.1147 | 220.0625 | 238.8073
lower2 | 0 | 3.8e-05 | 7.7e-05 | 0.000115 | 0.000153 | 0.000191 | 0.000229 | 0.000267 | 0.000306 | 0.000344 | 0.000382 | 0.00042 | 0.000458 | 0.000497 | 0.000535 | 0.000573 | 0.000611 | 0.000649 | 0.000687 | 0.000726 | 0.000764 | 0.000802 | 0.00084 | 0.000878 | 0.000917 | 0.000955
lower1
lower2

## Slide 28: Optimization Blocker: Procedure Calls
Why couldn’t compiler move strlen out of inner loop?
  Procedure may have side effects
    Alters global state each time called
  Function may not return same value for given arguments
    Depends on other parts of global state
    Procedure lower1 could interact with strlen
Warning:
  Compiler may treat procedure call as a black box
  Weak optimizations near them
Remedies:
  Use of inline functions
    GCC does this with –O1
      Within single file
  Do your own code motion
/* Alternative strlen */ size_t lencnt = 0;
size_t strlen(const char *s)
{
size_t length = 0;
while (*s != '\0') {
s++; length++;
}
lencnt += length;
return length;
}
Notes: Side effect of this version of strlen: updates global lencnt

## Slide 29: Optimization Blocker #2: Memory Aliasing
  Code updates b[i] on every iteration
  Why couldn’t compiler optimize this away?
# sum_rows1 inner loop
.L4:
movsd (%rsi,%rax,8), %xmm0 # FP load
addsd (%rdi), %xmm0 # FP add
movsd %xmm0, (%rsi,%rax,8) # FP store
addq $8, %rdi
cmpq %rcx, %rdi
jne .L4
/* Sum rows of n X n matrix a
and store in vector b */
void sum_rows1(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}

## Slide 30: Memory Aliasing
  Code updates b[i] on every iteration
  Must consider possibility that these updates will affect program behavior
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows1(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}
double A[9] =
{ 0, 1, 2,
4, 8, 16,
32, 64, 128};
double B[3] = A+3;
sum_rows1(A, B, 3);
i = 0: [3, 8, 16]
init: [4, 8, 16]
i = 1: [3, 22, 16]
i = 2: [3, 22, 224]
Value of B:
double A[9] =
{ 0, 1, 2,
0, 8, 16},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
0, 8, 16},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
1, 8, 16},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 8, 16},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 0, 16},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 3, 16},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 6, 16},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 22, 16},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 22, 0},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 22, 32},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 22, 96},
32, 64, 128};
double A[9] =
{ 0, 1, 2,
3, 22, 224,
32, 64, 128};

## Slide 31: Removing Aliasing
  No need to store intermediate results
# sum_rows2 inner loop
.L10:
addsd (%rdi), %xmm0 # FP load + add
addq $8, %rdi
cmpq %rax, %rdi
jne .L10
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows2(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
double val = 0;
for (j = 0; j < n; j++)
val += a[i*n + j];
b[i] = val;
}
}

## Slide 32: Optimization Blocker: Memory Aliasing
Aliasing
  Two different memory references specify single location
  Easy to have happen in C
    Since allowed to do address arithmetic
    Direct access to storage structures
  Get in habit of introducing local variables
    Accumulating within loops
    Your way of telling compiler not to check for aliasing

## Slide 33: Today
Generally Useful Optimizations
  Code motion/precomputation
  Strength reduction
  Sharing of common subexpressions
  Example: Bubblesort
Optimization Blockers
  Procedure calls
  Memory aliasing
Exploiting Instruction-Level Parallelism
Dealing with Conditionals

## Slide 34
Fran Allen (1932-2020)
  Pioneer of many optimizing compilation techniques
  Wrote a paper simply called “Program Optimization” in 1966
  “This paper introduced the use of graph-theoretic structures to encode program content in order to automatically and efficiently derive relationships and identify opportunities for optimization”
  First woman to win the ACM Turing Award (the “Nobel Prize of Computer Science”), in 2006

## Slide 35: Exploiting Instruction-Level Parallelism
Need general understanding of modern processor design
  Hardware can execute multiple instructions in parallel
Performance limited by data dependencies
Simple transformations can cause big speedups
  Compilers often cannot make these transformations
  Lack of associativity and distributivity in floating-point arithmetic

## Slide 36: Benchmark Example: Data Type for Vectors
/* data structure for vectors */
typedef struct{
size_t len;
data_t *data;
} vec;
/* retrieve vector element
and store at val */
int get_vec_element
(*vec v, size_t idx, data_t *val)
{
if (idx >= v->len)
return 0;
*val = v->data[idx];
return 1;
}
len
data
0
1
len-1
Data Types
  Use different declarations for data_t
  int
  long
  float
  double

## Slide 37: Benchmark Computation
Data Types
  Use different declarations for data_t
  int
  long
  float
  double
Operations
  Use different definitions of OP and IDENT
  + / 0
  * / 1
void combine1(vec_ptr v, data_t *dest)
{
long int i;
*dest = IDENT;
for (i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
Compute sum or product of vector elements

## Slide 38: Cycles Per Element (CPE)
Convenient way to express performance of program that operates on vectors or lists
Length = n
In our case: CPE = cycles per OP
Cycles = CPE*n + Overhead
  CPE is slope of line
Chart: Elements
| 0 | 193 | 120 | 91 | 95 | 196 | 97 | 181 | 91 | 83 | 43 | 183 | 140 | 146 | 94 | 134 | 163 | 131 | 110 | 182 | 189 | 112 | 141 | 185 | 188 | 47 | 130 | 102 | 59 | 174
psum1 | 2112.6 | 1451.1 | 1188.6 | 1218 | 2131.5 | 1247.4 | 2003.4 | 1190.7 | 1117.2 | 758.1 | 2020.2 | 1629.6 | 1686.3 | 1211.7 | 1568.7 | 1841.7 | 1543.5 | 1358.7 | 2011.8 | 2066.4 | 1373.4 | 1635.9 | 2032.8 | 2058 | 787.5 | 1539.3 | 1285.2 | 905.1 | 1938.3
psum1i | 367.79 | 2107.43 | 1449.43 | 1188.03 | 1224.09 | 2134.47 | 1242.12 | 1999.27 | 1188.03 | 1115.92 | 755.38 | 2017.29 | 1629.7 | 1683.79 | 1215.07 | 1575.62 | 1837.02 | 1548.58 | 1359.29 | 2008.28 | 2071.37 | 1377.32 | 1638.72 | 2035.32 | 2062.36 | 791.43 | 1539.57 | 1287.18 | 899.6 | 1936.17
psum2 | 1535.1 | 1100.4 | 921.9 | 940.8 | 1545.6 | 949.2 | 1455.3 | 917.7 | 865.2 | 623.7 | 1467.9 | 1209.6 | 1253.7 | 936.6 | 1173.9 | 1352.4 | 1150.8 | 1029 | 1461.6 | 1509.9 | 1039.5 | 1215.9 | 1478.4 | 1505.7 | 642.6 | 1152.9 | 987 | 732.9 | 1419.6
psum2i | 367.66 | 1531.11 | 1091.05 | 916.23 | 940.34 | 1549.2 | 952.4 | 1458.77 | 916.23 | 868.01 | 626.87 | 1470.83 | 1211.62 | 1247.79 | 934.32 | 1175.45 | 1350.27 | 1157.36 | 1030.77 | 1464.8 | 1507 | 1042.82 | 1217.64 | 1482.89 | 1500.97 | 650.99 | 1151.33 | 982.54 | 723.33 | 1416.58
psum1
Slope = 9.0
psum2
Slope = 6.0

## Slide 39: Benchmark Performance
void combine1(vec_ptr v, data_t *dest)
{
long int i;
*dest = IDENT;
for (i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
Compute sum or product of vector elements
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine1 unoptimized | 22.68 | 20.02 | 19.98 | 20.18
Combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14
Combine1 –O3 | 4.5 | 4.5 | 6 | 7.8
Results in CPE (cycles per element)

## Slide 40: Basic Optimizations
Move vec_length out of loop
Avoid bounds check on each cycle
Accumulate in temporary
void combine4(vec_ptr v, data_t *dest)
{
long i;
long length = vec_length(v);
data_t *d = get_vec_start(v);
data_t t = IDENT;
for (i = 0; i < length; i++)
t = t OP d[i];
*dest = t;
}

## Slide 41: Effect of Basic Optimizations
Eliminates sources of overhead in loop
void combine4(vec_ptr v, data_t *dest)
{
long i;
long length = vec_length(v);
data_t *d = get_vec_start(v);
data_t t = IDENT;
for (i = 0; i < length; i++)
t = t OP d[i];
*dest = t;
}
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14
Combine4 | 1.27 | 3.01 | 3.01 | 5.01

## Slide 42: Modern CPU Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates

## Slide 43: Superscalar Processor
Definition: A superscalar processor can issue and execute multiple instructions in one cycle. The instructions are retrieved from a sequential instruction stream and are usually scheduled dynamically.
Benefit: without programming effort, superscalar processor can take advantage of the instruction level parallelism that most programs have.
Most CPUs are superscalar.
  Intel: since Pentium (1993)

## Slide 44: Pipelined Functional Units
Stage 1
Stage 2
Stage 3
long mult_eg(long a, long b, long c) {
long p1 = a*b; long p2 = a*c; long p3 = p1 * p2;
return p3; }
  Divide computation into stages
  Pass partial computations from stage to stage
  Stage i can start on new computation once values passed to i+1
  E.g., complete 3 multiplications in 7 cycles, even though each requires 3 cycles
 | Time |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Stage 1 | a*b | a*c |  |  | p1*p2 |  | 
Stage 2 |  | a*b | a*c |  |  | p1*p2 | 
Stage 3 |  |  | a*b | a*c |  |  | p1*p2

## Slide 45: Haswell CPU
8 Total Functional Units
Multiple instructions can execute in parallel
  2 load, with address computation
  1 store, with address computation
  4 integer
  2 FP multiply
  1 FP add
  1 FP divide
Some instructions take > 1 cycle, but can be pipelined
  Instruction Latency Cycles/Issue
  Load / Store 4 1
  Integer Multiply 3 1
  Integer/Long Divide 3-30 3-30
  Single/Double FP Multiply 5 1
  Single/Double FP Add 3 1
  Single/Double FP Divide 3-15 3-15

## Slide 46: x86-64 Compilation of Combine4
Inner Loop (Case: Integer Multiply)
.L519: # Loop:
imull (%rax,%rdx,4), %ecx # t = t * d[i]
addq $1, %rdx # i++
cmpq %rdx, %rbp # Compare length:i
jg .L519 # If >, goto Loop
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 47: Combine4 = Serial Computation (OP = *)
Computation (length=8)
  ((((((((1 * d[0]) * d[1]) * d[2]) * d[3]) * d[4]) * d[5]) * d[6]) * d[7])
Sequential dependence
  Performance: determined by latency of OP
*
*
1
d0
d1
*
d2
*
d3
*
d4
*
d5
*
d6
*
d7

## Slide 48: Loop Unrolling (2x1)
Perform 2x more useful work per loop iteration
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = (x OP d[i]) OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}

## Slide 49: Effect of Loop Unrolling
Helps integer add
  Achieves latency bound
Others don’t improve. Why?
  Still sequential dependency
x = (x OP d[i]) OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Notes: Add – body of loop close to cost of loop overhead. Need more work in loop to amortize loop overhead.

## Slide 50: Loop Unrolling with Separate Accumulators (2x2)
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x0 = IDENT;
data_t x1 = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x0 = x0 OP d[i];
}
*dest = x0 OP x1;
}
Can this change the result of the computation?
Yes, for FP. Why?

## Slide 51: Effect of Separate Accumulators
Nearly 2x speedup for Int *, FP +, FP *
  Reason: Breaks sequential dependency
  Why is that? (next slide)
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x2 | 0.81 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
2 func. units for FP *,
2 func. units for load
5-stage pipelined FP *
4 func. units for int +,
2 func. units for load
Why Not .25?
1 func. unit for FP +
3-stage pipelined FP +
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
Notes: Why not .25 for Integer Add throughput? Limited by having only 2 load units.
Why 0.5 for FP Mult? 5cycles, fully pipelined (ergo 1 cycle) divided by 2 units => 0.5

## Slide 52: Separate Accumulators
*
*
1
d1
d3
*
d5
*
d7
*
*
*
1
d0
d2
*
d4
*
d6
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
What changed:
  Two independent “streams” of operations
Overall Performance
  N elements, D cycles latency/op
  Should be (N/2+1)*D cycles: CPE = D/2
  CPE matches prediction!
What Now?

## Slide 53: Unrolling & Accumulating
Idea: Can choose L Unrolling Factor and K Accumulators
  L must be a multiple of K
Case: Double *
  Latency bound: 5.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 
2 |  | 2.51 |  | 2.51 |  | 2.51 |  | 
3 |  |  | 1.67 |  |  |  |  | 
4 |  |  |  | 1.25 |  | 1.26 |  | 
6 |  |  |  |  | 0.84 |  |  | 0.88
8 |  |  |  |  |  | 0.63 |  | 
10 |  |  |  |  |  |  | 0.51 | 
12 |  |  |  |  |  |  |  | 0.52
Accumulators
Notes: Diminishing returns: can’t go beyond throughput limitations of execution units.
Large overhead for short lengths, because finish off iterations sequentially.

## Slide 54: Achievable Performance
Limited only by throughput of functional units
Up to 42X improvement over original, unoptimized code
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Best | 0.54 | 1.01 | 1.01 | 0.52
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
Can we do even better?

## Slide 55: Programming with AVX2
YMM Registers
  16 total, each 32 bytes
  32 single-byte integers
  16 16-bit integers
  8 32-bit integers
  8 single-precision floats
  4 double-precision floats
  1 single-precision float
  1 double-precision float

## Slide 56: SIMD Operations
  SIMD Operations: Single Precision
  SIMD Operations: Double Precision
+
+
+
+
%ymm0
%ymm1
vaddpd %ymm0, %ymm1, %ymm1
%ymm0
%ymm1
vaddps %ymm0, %ymm1, %ymm1
+
+
+
+
+
+
+
+

## Slide 57: Using Vector Instructions
Make use of AVX Instructions
  Parallel operations on multiple data elements
  See Web Aside OPT:SIMD on CS:APP web page
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Scalar Best | 0.54 | 1.01 | 1.01 | 0.52
Vector Best | 0.06 | 0.24 | 0.25 | 0.16
Latency Bound | 0.50 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
Vec Throughput Bound | 0.06 | 0.12 | 0.25 | 0.12

## Slide 58: Today
Generally Useful Optimizations
  Code motion/precomputation
  Strength reduction
  Sharing of common subexpressions
  Example: Bubblesort
Optimization Blockers
  Procedure calls
  Memory aliasing
Exploiting Instruction-Level Parallelism
Dealing with Conditionals

## Slide 59: What About Branches?
Challenge
  Instruction Control Unit must work well ahead of Execution Unit to generate enough operations to keep EU busy
  When encounters conditional branch, cannot reliably determine where to continue fetching
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq
Executing
How to continue?

## Slide 60: Modern CPU Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates

## Slide 61: Branch Outcomes
  When encounter conditional branch, cannot determine where to continue fetching
    Branch Taken: Transfer control to branch target
    Branch Not-Taken: Continue with next instruction in sequence
  Cannot resolve until outcome determined by branch/integer unit
Branch Taken
Branch Not-Taken
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq

## Slide 62: Branch Prediction
Idea
  Guess which way branch will go
  Begin executing instructions at predicted position
    But don’t actually modify register or memory data
Predict Taken
Begin
Execution
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq

## Slide 63: Branch Prediction Through Loop
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Read invalid location
Executed
Fetched

## Slide 64: Branch Misprediction Invalidation
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Invalidate

## Slide 65: Branch Misprediction Recovery
Performance Cost
  Multiple clock cycles on modern processor
  Can be a major performance limiter
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401036: jmp 401040
. . .
401040: vmovsd %xmm0,(%r12)
i = 99
Definitely not taken
Reload
Pipeline

## Slide 66: Branch Prediction Numbers
Default behavior:
  Backwards branches are often loops so predict taken
  Forwards branches are often if so predict not taken
Predictors average better than 95% accuracy
  Most branches are already predictable.
Annual branch predictor contests at top Computer Architecture conferences (2010-2016)
  Metrics: Size of branch predictor tables Mispredictions per kilo-instruction (MPKI)
  2016 Winners (https://www.jilp.org/cbp2016/)
    Size 8KB: MPKI=4.1
    Size 64KB: MPKI=3.3

## Slide 67: Summary: Getting High Performance
Good compiler and flags
Don’t do anything sub-optimal
  Watch out for hidden algorithmic inefficiencies
  Write compiler-friendly code
    Watch out for optimization blockers: procedure calls & memory references
  Look carefully at innermost loops (where most work is done)
Tune code for machine
  Exploit instruction-level parallelism
  Avoid unpredictable branches
  Make code cache friendly

## Slide 68: Additional Slides

## Slide 69: Loop Unrolling with Reassociation (2x1a)
Can this change the result of the computation?
Yes, for FP. Why?
void unroll2aa_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = x OP (d[i] OP d[i+1]);
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}
x = (x OP d[i]) OP d[i+1];
Compare to before
Notes: But for more expensive ops, don’t always have an OP unit available

## Slide 70: Effect of Reassociation
Nearly 2x speedup for Int *, FP +, FP *
  Reason: Breaks sequential dependency
  Why is that? (next slide)
x = x OP (d[i] OP d[i+1]);
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
2 func. units for FP *,
2 func. units for load
5-stage pipelined FP *
4 func. units for int +,
2 func. units for load
Why Not .25?
1 func. unit for FP +
3-stage pipelined FP +
Notes: Why not .25 for Integer Add throughput? Limited by having only 2 load units.
Why 0.5 for FP Mult? 5cycles, fully pipelined (ergo 1 cycle) divided by 2 units => 0.5

## Slide 71: Reassociated Computation
What changed:
  Ops in the next iteration can be started early (no dependency)
Overall Performance
  N elements, D cycles latency/op
  (N/2+1)*D cycles: CPE = D/2
*
*
1
*
*
*
d1
d0
*
d3
d2
*
d5
d4
*
d7
d6
x = x OP (d[i] OP d[i+1]);

## Slide 72: Unrolling & Accumulating: Int +
Case
  Intel Haswell
  Integer addition
  Latency bound: 1.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 1.27 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 
2 |  | 0.81 |  | 0.69 |  | 0.54 |  | 
3 |  |  | 0.74 |  |  |  |  | 
4 |  |  |  | 0.69 |  | 1.24 |  | 
6 |  |  |  |  | 0.56 |  |  | 0.56
8 |  |  |  |  |  | 0.54 |  | 
10 |  |  |  |  |  |  | 0.54 | 
12 |  |  |  |  |  |  |  | 0.56
Accumulators