## Slide 1
14-513
18-613

## Slide 2: Cache Memories 18-213/18-613: Introduction to Computer Systems 10th Lecture, February 16, 2023

## Slide 3: Reminder: AIV Policy
No unauthorized use of information
  Borrowing code: by copying, retyping, looking at a file
  Describing: verbal description of code from one person to another
  Searching the Web for solutions
  Copying code from a previous course or online solution
  Reusing your code from a previous semester (here or elsewhere)
No unauthorized supplying of information
  Providing copy: Giving a copy of a file to someone
  Providing access:
    Putting material in unprotected directory
    Putting material in unprotected code repository (e.g., Github)
No collaborations beyond high-level, strategic advice
  Anything more than block diagram or a few words
Start early. Make frequent github commits. Plan for stumbling blocks. Use available help. Don’t panic: Far better to turn in 25% correct solution than get an AIV.
http://www.cs.cmu.edu/~18213/academicintegrity.html

## Slide 4: Today
Cache memory organization and operation CSAPP 6.4-6.5
Performance impact of caches
  The memory mountain CSAPP 6.6.1
  Rearranging loops to improve spatial locality CSAPP 6.6.2
  Using blocking to improve temporal locality CSAPP 6.6.3

## Slide 5: Recall: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4

## Slide 6: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 7: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 8: Working Set, Locality, and Caches
Working Set: The set of data a program is currently “working on”
  Definition of “currently” depends on context, e.g., in this loop
  Includes accesses to data and instructions
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
  Nearby addresses: Spatial Locality
  Equal addresses: Temporal locality
Caches take advantage of temporal locality by storing recently used data, and spatial locality by copying data in block-sized transfer units
  Locality reduces working set sizes
  Caches are most effective when the working set fits in the cache

## Slide 9: Recall: 3 Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache starts empty and this is the first reference to the block.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.
Conflict miss
  Occurs when the cache is large enough, but too many data objects all map (by the placement policy) to the same limited set of blocks
    E.g., if the placement policy maps both 0 and 8 to the same block, then referencing 0, 8, 0, 8, 0, 8, ... would miss every time.

## Slide 10: CPU Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
CPU looks first for data in cache
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory

## Slide 11: What it Really Looks Like
Bus interface
ALU
Register file
CPU chip
Cache
memory
Core i7-3960X
AMD FX 8150
Nehalem

## Slide 12: What it Really Looks Like (Cont.)
Intel Alder Lake (2021)
8 P-cores + 8 E-cores
L1 caches per P-core: 32KB Instruction & 48KB Data
L1 caches per E-core: 64KB Instruction & 32KB Data
L2 caches: 1.25MB per P-core, 2MB per four E-cores
L3 cache: 30MB shared among all cores
Notes: Intel processor, launched in 2021, with 8 Golden Cove high-performance cores (P-cores) and 8 Gracemont power-efficient cores (E-cores)

## Slide 13: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size
= S x E x B data bytes
valid bit

## Slide 14: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 15: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 16: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes (= hit)
valid? +
block offset
tag

## Slide 17: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes (= hit)
valid? +
int (4 Bytes) is here
block offset
If tag doesn’t match (= miss): old line is evicted and replaced

## Slide 18: Direct-Mapped Cache Simulation
4-bit addresses (address space size M=16 bytes)
S=4 sets, E=1 Blocks/set, B=2 bytes/block
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
v
Tag
Block
0
0
0
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
0
M[0-1]
Set 0
Set 1
Set 2
Set 3
(cold)
(cold)
(cold)
(conflict)
Notes: Pause at the end of this slide to consider that M[0] and M[8] have nothing to do with one another, but that they interfere with one anothers’ existences in the cache.

## Slide 19: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
2 lines per set
S sets

## Slide 20: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes (= hit)
block offset
tag

## Slide 21: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes (= hit)
block offset
tag
5
4
short int (2 Bytes) is here
No match or not valid (= miss):
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 22: 2-Way Set Associative Cache Simulation
4-bit addresses (M=16 bytes)
S=2 sets, E=2 blocks/set, B=2 bytes/block
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1
Notes: For the same trace as before, we get a hit for the second 0 with a 2-way set associative cache (instead of a miss with a direct-mapped cache).

## Slide 23: What about writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Each cache line needs a dirty bit (set if data differs from memory)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location will follow
  No-write-allocate (writes straight to memory, does not load into cache)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate
0
1
2
B-1
tag
d
B = 2b bytes
dirty bit
v
valid bit

## Slide 24: Why Index Using Middle Bits?
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
t bits
0…01
100
Address of int:
find set
Standard Method:
Middle bits indexing
t bits
1…11
100
Address of int:
find set
Alternative Method:
High bits indexing

## Slide 25: Illustration of Indexing Approaches
64-byte memory
  6-bit addresses
16 byte, direct-mapped cache
Block size = 4. (Thus, 4 sets; why?)
2 bits tag, 2 bits index, 2 bits offset
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx
Notes: 16byte direct mapped $, 4B blocks -> must be 4 sets to account for all 16B of cache

## Slide 26: Middle Bits Indexing
Addresses of form TTSSBB
  TT Tag bits
  SS Set index bits
  BB Offset bits
Makes good use of spatial locality
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx

## Slide 27: High Bits Indexing
Addresses of form SSTTBB
  SS Set index bits
  TT Tag bits
  BB Offset bits
Program with high spatial locality would generate lots of conflicts
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx
Notes: Go from block with set index bits 00 to 01, displace the line sitting in set 0 from the block with set index 00.

## Slide 28: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 29: Example: Core i7 L1 Data Cache
B =
S = , s =
E = , e =
C =
Block offset: . bits
Set index: . bits
Tag: . bits
Stack Address: 0x00007f7262a1e010
Block offset: 0x??
Set index: 0x??
Tag: 0x??
32 KB 8-way set associative
64 bytes/block
47 bit address range
Notes: B = 64 (2^6)
E = 8 (2^3)
S = 64 (2^6) [need to infer from B, E, and Cache Size]
Cache Size = 2^15 (32768)

## Slide 30: Example: Core i7 L1 Data Cache
B = 64
S = 64, s = 6
E = 8, e = 3
C = 64 x 64 x 8 = 32,768
Block offset: 6 bits
Set index: 6 bits
Tag: 35 bits
Stack Address: 0x00007f7262a1e010
Block offset: 0x??
Set index: 0x??
Tag: 0x??
32 kB 8-way set associative 64 bytes/block
47 bit address range

## Slide 31: Example: Core i7 L1 Data Cache
B = 64
S = 64, s = 6
E = 8, e = 3
C = 64 x 64 x 8 = 32,768
Block offset: 6 bits
Set index: 6 bits
Tag: 35 bits
Stack Address: 0x00007f7262a1e010
Block offset: 0x10
Set index: 0x0
Tag: 0x7f7262a1e
32 kB 8-way set associative 64 bytes/block
47 bit address range
0000 0001 0000
Notes: 0x010 => 0000 0001 0000, say that it awkwardly segments the bits, but that’s ok

## Slide 32: Cache Performance Metrics
Miss Rate
  Fraction of memory accesses not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (as %):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a cached block to the processor
    includes time to determine whether line is in cache
  Typical numbers:
    4 clock cycle for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 33: How Bad Can a Few Cache Misses Be?
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider this simplified example: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 x 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 x 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 34: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories

## Slide 35: Quiz Time!
Canvas Quiz: Day 10 – Cache Memories

## Slide 36: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 37: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 38: Memory Mountain Test Function
long data[MAXELEMS]; /* Global array to traverse */
/* test - Iterate over first "elems" elements of
* array "data" with stride of "stride“,
* using 4x4 loop unrolling.
*/
int test(int elems, int stride) {
long i, sx2=stride*2, sx3=stride*3, sx4=stride*4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems, limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+stride];
acc2 = acc2 + data[i+sx2];
acc3 = acc3 + data[i+sx3];
}
/* Finish any remaining elements */
for (; i < length; i++) {
acc0 = acc0 + data[i];
}
return ((acc0 + acc1) + (acc2 + acc3));
}
Call test() with many combinations of elems
and stride.
For each elems and stride:
1. Call test() once to warm up the caches.
2. Call test() again and measure the read throughput(MB/s)
mountain/mountain.c

## Slide 39: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Notes: Slopes of spatial locality – increase stride, degrade throughput because burn through blocks faster
Ridges of temporal – As increase size, can’t fit in level of cache any more, drop to next one down. Data in cache because of warm up before test run.
Prefetching – do better than we expect.

## Slide 40: Closer Look at Stride Effects
Chart: Stride
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
8 elems per cache block
128K
Chart: Throughput for size = 128K
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
Measured | 30896 | 25024 | 24135 | 20391 | 17199 | 14634 | 12670 | 11274 | 11248 | 11262 | 11294 | 11251
Miss rate = stride/8
Miss rate = 1.0
stride

## Slide 41: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 42: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  Matrix elements are doubles (8 bytes)
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
matmult/mm.c

## Slide 43: Miss Rate Analysis for Matrix Multiply
Assume:
  Block size = 32B (big enough for four doubles)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x

## Slide 44: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > sizeof(aij) bytes, exploit spatial locality
    miss rate = sizeof(aij) / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    miss rate = 1 (i.e. 100%)

## Slide 45: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.25 1.0 0.0
matmult/mm.c
Block size = 32B (four doubles)

## Slide 46: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c
Block size = 32B (four doubles)
Same analysis as ijk
Notes: Can go quickly through this slide. Only point is that the outer loop order doesn’t change the analysis

## Slide 47: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.0
matmult/mm.c
Block size = 32B (four doubles)
0.25
0.25

## Slide 48: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.0
matmult/mm.c
Block size = 32B (four doubles)
1.0
1.0

## Slide 49: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  avg misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  avg misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  avg misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 50: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700
jki | 4.8 | 4.68 | 4.65 | 4.8 | 6.84 | 15.03 | 22.78 | 29.39 | 40.39 | 57.06 | 60.54 | 63.33 | 65.61 | 67.49
kji | 4.83 | 4.72 | 4.64 | 4.69 | 6.83 | 15.1 | 22.68 | 29.18 | 40.26 | 57.02 | 60.53 | 63.34 | 65.62 | 67.53
ijk | 3.75 | 4.08 | 4.33 | 4.45 | 4.45 | 4.45 | 4.45 | 4.47 | 7.73 | 18.77 | 20.36 | 21.67 | 22.76 | 23.71
jik | 3.93 | 4.14 | 4.36 | 4.47 | 4.52 | 4.56 | 4.57 | 4.6 | 7.96 | 19.05 | 20.59 | 21.86 | 22.92 | 23.82
kij | 1.86 | 1.78 | 2.14 | 2.3 | 2.23 | 2.18 | 2.14 | 2.12 | 2.12 | 2.13 | 2.13 | 2.14 | 2.16 | 2.22
ikj | 1.78 | 1.8 | 2.12 | 2.03 | 1.96 | 1.92 | 1.89 | 1.86 | 1.86 | 1.88 | 1.89 | 1.9 | 1.91 | 1.95
ijk / jik (1.25)
jki / kji (2.0)
kij / ikj (0.5)
Cycles per inner loop iteration

## Slide 51: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 52: Example: Matrix Multiplication
a
b
i
j
x
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n + j] += a[i*n + k] * b[k*n + j];
}

## Slide 53: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache line = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
x
=
n
x
=
8 wide
Notes: n/8 – comes from taking n and doing it in chunks of 8 that fit in a cache line, with perfect stride 1 accesses across the row
N – comes from missing on everything but the 1 double needed going down a column

## Slide 54: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache line = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 n2 = (9/8) n3
n
x
=
8 wide

## Slide 55: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=L)
for (j = 0; j < n; j+=L)
for (k = 0; k < n; k+=L)
/* L x L mini matrix multiplications */
for (i1 = i; i1 < i+L; i1++)
for (j1 = j; j1 < j+L; j1++)
for (k1 = k; k1 < k+L; k1++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
x
c
=
c
+
Block size L x L
matmult/bmm.c

## Slide 56: Cache Miss Analysis
Assume:
  Cache line = 8 doubles. Blocking size L ≥ 8
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3L2 < C
First (block) iteration:
  Misses per block: L2/8
  Blocks per Iteration: 2n/L
  (omitting matrix c)
  Misses per Iteration:
  2n/L x L2/8 = nL/4
  Afterwards in cache (schematic)
x
=
x
=
Block size L x L
n/L blocks
Notes: L^2 / 8 comes from taking L^2 bytes per block and perfectly caching them 8 doubles at a time.
2n/L comes from doing n/L blocks of size L^2 in each source matrix

## Slide 57: Cache Miss Analysis
Assume:
  Cache line = 8 doubles. Blocking size L ≥ 8
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3L2 < C
Second (block) iteration:
  Same misses as
  first iteration
  2n/L x L2/8 = nL/4
Total misses:
  nL/4 misses per iteration x (n/L)2 iterations = n3/(4L) misses
x
=
Block size L x L
n/L blocks
Notes: n/L is the dimension of the matrix in blocks. (n/L)^2 is the number of iterations.
nL/4 is the misses per iteration. N^3/4L is the total miss count.

## Slide 58: Blocking Summary
No blocking: (9/8) n3 misses
Blocking: (1/(4L)) n3 misses
Use largest block size L, such that L satisfies 3L2 < C
  Fit three blocks in cache! Two input, one output.
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly
Notes: 3L^2 to accommodate M3 = M1 x M2, with M1,2,3 all supplying blocks of dim L^2

## Slide 59: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!
  Focus on the inner loops, where bulk of computations and memory accesses occur.
  Try to maximize spatial locality by reading data objects sequentially with stride 1.
  Try to maximize temporal locality by using a data object as often as possible once it’s read from memory.

## Slide 60: Supplemental slides

## Slide 61: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
128m | 16636 | 8966 | 5846 | 4298 | 3403 | 2789 | 2348 | 2055 | 1904 | 1786 | 1693 | 1607
64m | 16925 | 9080 | 5860 | 4307 | 3408 | 2795 | 2352 | 2058 | 1912 | 1791 | 1695 | 1608
32m | 17168 | 9212 | 5897 | 4331 | 3431 | 2822 | 2375 | 2078 | 1924 | 1809 | 1713 | 1628
16m | 17405 | 9559 | 6027 | 4458 | 3520 | 2899 | 2465 | 2179 | 2049 | 1952 | 1883 | 1825
8m | 19339 | 11837 | 8045 | 6079 | 4927 | 4246 | 3745 | 3289 | 3131 | 3026 | 2899 | 2924
4m | 20728 | 16852 | 13212 | 10371 | 8542 | 7259 | 6345 | 5627 | 5396 | 5228 | 5090 | 4977
2m | 29025 | 19350 | 13735 | 10550 | 8610 | 7308 | 6361 | 5648 | 5417 | 5241 | 5094 | 4978
1024k | 29291 | 19543 | 13689 | 10508 | 8597 | 7281 | 6354 | 5628 | 5388 | 5218 | 5071 | 4956
512k | 29290 | 19411 | 13779 | 10594 | 8667 | 7390 | 6438 | 5684 | 5453 | 5325 | 5213 | 5128
256k | 29762 | 21456 | 16905 | 13504 | 11044 | 9359 | 8175 | 7240 | 7082 | 6889 | 6858 | 6835
128k | 30042 | 23953 | 22661 | 18952 | 15706 | 13602 | 11761 | 10409 | 10184 | 10137 | 10158 | 9875
64k | 29468 | 23044 | 21501 | 19208 | 15955 | 13551 | 11784 | 10516 | 10364 | 10320 | 10262 | 10132
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Core i5 Haswell
3.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size

## Slide 62: Cache Capacity Effects from Memory Mountain
Chart: Working set size (bytes)
| 128m | 64m | 32m | 16m | 8m | 4m | 2m | 1024k | 512k | 256k | 128k | 64k | 32k | 16k
s8 | 2055 | 2058 | 2078 | 2179 | 3289 | 5627 | 5648 | 5628 | 5684 | 7240 | 10409 | 10516 | 26110 | 27746
Core i7 Haswell
3.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slice through memory mountain with stride=8
L1
L2
L3
Main Memory

## Slide 63: Modeling Block Size Effects from Memory Mountain
Chart: Throughput for size = 128K
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
Measured | 30896 | 25024 | 24135 | 20391 | 17199 | 14634 | 12670 | 11274 | 11248 | 11262 | 11294 | 11251
Model | 30896 | 24743.7642 | 20634.8109 | 17696.1805 | 15490.2007 | 13773.2479 | 12398.9348 | 11274 | 11274 | 11274 | 11274 | 11274
Core i7 Haswell
2.26 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Stride s

## Slide 64: 2008 Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
128m | 5427 | 2757 | 1939 | 1455 | 1151 | 951 | 803 | 701 | 672 | 646 | 626 | 610
64m | 5496 | 2760 | 1936 | 1459 | 1149 | 949 | 803 | 703 | 666 | 644 | 621 | 610
32m | 5498 | 2758 | 1938 | 1454 | 1151 | 934 | 811 | 704 | 671 | 645 | 625 | 611
16m | 5506 | 2769 | 1941 | 1460 | 1153 | 953 | 811 | 705 | 672 | 646 | 626 | 614
8m | 5657 | 2977 | 2090 | 1586 | 1251 | 1035 | 882 | 766 | 777 | 836 | 1018 | 1365
4m | 10401 | 8422 | 7522 | 6468 | 5469 | 4809 | 4284 | 3894 | 3900 | 3899 | 3898 | 3897
2m | 10401 | 8418 | 7517 | 6468 | 5465 | 4804 | 4284 | 3898 | 3896 | 3897 | 3893 | 3897
1024k | 10479 | 8469 | 7578 | 6508 | 5510 | 4854 | 4326 | 3935 | 3939 | 3945 | 3951 | 3963
512k | 10486 | 8465 | 7578 | 6508 | 5514 | 4854 | 4330 | 3938 | 3945 | 3952 | 3956 | 3969
256k | 10479 | 8456 | 7578 | 6503 | 5510 | 4850 | 4322 | 3931 | 3935 | 3938 | 3944 | 3958
128k | 10473 | 8443 | 7552 | 6488 | 5496 | 4833 | 4307 | 3920 | 3912 | 3922 | 3923 | 3938
64k | 10460 | 8414 | 7537 | 6463 | 5474 | 4817 | 4295 | 3902 | 3897 | 3899 | 3893 | 3905
No prefetching
Core 2 Duo
2.4 GHz
32 KB L1 d-cache
6MB L2 cache
64 B block size

## Slide 65: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c
Block size = 32B (four doubles)

## Slide 66: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c
Block size = 32B (four doubles)

## Slide 67: Recap: Stack and instruction pointers
The stack pointer (%rsp) points to the top of the stack
The instruction pointer (%rip) points to the next instruction to be executed
They are independent
  But linked by call and ret instructions
Stack
Text
Data
Heap
Shared
Libraries
rsp
rip

## Slide 68: Recap: stack operations
push %rax =
more stuff
rsp

## Slide 69: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
more stuff
rax
rsp

## Slide 70: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
more stuff
rax
rsp

## Slide 71: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
more stuff
rax
rip
rsp

## Slide 72: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
ret =
more stuff
rax
rip
rsp

## Slide 73: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
ret =
  mov (%rsp), %rip
  add %rsp, 8
more stuff
rax
rsp

## Slide 74: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
ret =
  mov (%rsp), %rip
  add %rsp, 8
pop %rax =
more stuff
rax
rsp

## Slide 75: Recap: stack operations
push %rax =
  sub %rsp, 8
  mov %rax, (%rsp)
call func =
  sub %rsp, 8
  mov %rip, (%rsp)
  jmp func
ret =
  mov (%rsp), %rip
  add %rsp, 8
pop %rax =
  mov (%rsp), %rax
  add %rsp, 8
more stuff
rsp