## Slide 1
14-513
18-613

## Slide 2: Virtual Memory: Concepts 18-213/18-613: Introduction to Computer Systems 12th Lecture, October 6, 2022

## Slide 3: Announcements
Homework #5 due today
No new HW released this week
Low-stakes Midterm Review in Small Groups Mon Feb 27
Lab 4 (cachelab) due Thurs Feb 16
Homework #6/#7 (low-stakes take-home midterm) goes out Mon Feb 27 at 10 pm ET, due Fri Mar 3 at 11:59 pm
  80 minutes self-timed. Covers through 2/20 lecture. Questions similar to homeworks, but only one attempt. Open book.
  Tests what you’ve learned, as in a real midterm (and as in the Final).
  Low-stakes: Only 4% of grade (could even be “half dropped”).

## Slide 4: Hmmm, How Does This Work?!
Process 1
Process 2
Process n
Solution: Virtual Memory (today and next lecture)

## Slide 5: Today
Address spaces CSAPP 9.1-9.2
VM as a tool for caching CSAPP 9.3
VM as a tool for memory management CSAPP 9.4
VM as a tool for memory protection CSAPP 9.5
Address translation CSAPP 9.6

## Slide 6: A System Using Physical Addressing
Used in “simple” systems like embedded microcontrollers in devices like elevators and digital picture frames
0:
1:
M-1:
Main memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4

## Slide 7: A System Using Virtual Addressing
Used in all modern servers, laptops, and smart phones
One of the great ideas in computer science
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100

## Slide 8: Address Spaces
Linear address space: Ordered set of contiguous non-negative integer addresses: {0, 1, 2, 3 … }
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
Physical address space: Set of M = 2m physical addresses {0, 1, 2, 3, …, M-1}

## Slide 9: Why Virtual Memory (VM)?
Uses main memory efficiently
  Use DRAM as a cache for parts of a virtual address space
Simplifies memory management
  Each process gets the same uniform linear address space
Isolates address spaces
  One process can’t interfere with another’s memory
  User program cannot access privileged kernel information and code

## Slide 10: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 11: VM as a Tool for Caching
Conceptually, virtual memory is an array of N contiguous bytes stored on disk.
The contents of the array on disk are cached in physical memory (DRAM cache)
  These cache blocks are called pages (size is P = 2p bytes)
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
stored on disk
Physical pages (PPs)
cached in DRAM

## Slide 12: DRAM Cache Organization
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
  Time to load block from disk > 1ms (> 1 million clock cycles)
    CPU can do a lot of computation during that time
Consequences
  Large page (block) size: typically 4 KB
    Linux “huge pages” are 2 MB (default) to 1 GB
  Fully associative. Why?
    Any VP can be placed in any PP
    Requires a “large” mapping function – different from cache memories
  Highly sophisticated, expensive replacement algorithms. Why?
    Too complicated and open-ended to be implemented in hardware
  Write-back rather than write-through. Why?
Notes: Minimizing cache misses is paramount. Fully associative avoids conflict misses, and likely no worse on capacity misses.
Sophisticated replacement algorithms likely better than simpler ones at minimizing misses.
Write-through would slow computation down to speed of the disk.

## Slide 13: Enabling Data Structure: Page Table
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
  Per-process kernel data structure in DRAM
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3

## Slide 14: Page Hit
Page hit: reference to VM word that is in physical memory (DRAM cache hit)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 15: Page Fault
Page fault: reference to VM word that is not in physical memory (DRAM cache miss)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 16: Triggering a Page Fault
User writes to memory location
That portion (page) of user’s memory is currently on disk
MMU triggers page fault exception
  (More details in later lecture)
  Raise privilege level to supervisor mode
  Causes procedure call to software page fault handler
int a[1000];
main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10
User code
Kernel code
Exception: page fault
Execute page fault handler
movl

## Slide 17: Handling Page Fault
Page miss causes page fault (an exception)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 18: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 19: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 20: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
Key point: Waiting until the miss to copy the page to DRAM is known as demand paging

## Slide 21: Completing page fault
Page fault handler executes return from interrupt (iret) instruction
  Like ret instruction, but also restores privilege level
  Return to instruction that caused fault
  But, this time there is no page fault
int a[1000];
main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10
User code
Kernel code
Exception: page fault
Copy page from disk to memory
Return and reexecute movl
movl

## Slide 22: Allocating Pages
Allocating a new page (VP 5) of virtual memory.
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VP 5
null

## Slide 23: Allocating Pages
Allocating a new page (VP 5) of virtual memory.
Subsequent miss will bring it into memory
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VP 5
Notes: Note that valid bit is 0 until the subsequent miss

## Slide 24: Locality to the Rescue Again!
Virtual memory seems terribly inefficient, but it works because of locality.
At any point in time, programs tend to access a set of active virtual pages called the working set
  Programs with better temporal locality will have smaller working sets
If (working set size < main memory size)
  Good performance for one process (after cold misses)
If (working set size > main memory size )
  Thrashing: Performance meltdown where pages are swapped (copied) in and out continuously
  If multiple processes run at the same time, thrashing occurs if their total working set size > main memory size

## Slide 25: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 26
Key idea: each process has its own virtual address space
  It can view memory as a simple linear array
  Mapping function scatters addresses through physical memory
    Well-chosen mappings can improve locality
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation
VM as a Tool for Memory Management

## Slide 27
Simplifying memory allocation
  Each virtual page can be mapped to any physical page
  A virtual page can be stored in different physical pages at different times
  Can allocate the same virtual addresses on the heap for multiple processes
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation
VM as a Tool for Memory Management

## Slide 28
Sharing code and data among processes
  Map virtual pages to the same physical page (here: PP 6)
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation
VM as a Tool for Memory Management

## Slide 29: Simplifying Linking and Loading
Linking
  Each program has similar virtual address space
  Code, data, and heap always start at the same addresses.
Loading
  execve allocates virtual pages for .text and .data sections & creates PTEs marked as invalid
  The .text and .data sections are copied, page by page, on demand by the virtual memory system
Discussed later in lecture on Linking and Loading
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%rsp
(stack
pointer)
Memory
invisible to
user code
brk
0x400000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Loaded
from
the
executable
file

## Slide 30: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 31: VM as a Tool for Memory Protection
Extend page table entries (PTEs) with permission bits
MMU checks these bits on each access
Process i:
Address
READ
WRITE
PP 6
Yes
No
PP 4
Yes
Yes
PP 2
Yes
VP 0:
VP 1:
VP 2:
•
•
•
Process j:
Yes
SUP
No
No
Yes
Address
READ
WRITE
PP 9
Yes
No
PP 6
Yes
Yes
PP 11
Yes
Yes
SUP
No
Yes
No
VP 0:
VP 1:
VP 2:
Physical
Address Space
PP 2
PP 4
PP 6
PP 8
PP 9
PP 11
EXEC
Yes
EXEC
Yes
Yes
Yes
Yes
No
SUP: requires kernel mode

## Slide 32: Quiz Time!
Canvas Quiz: Day 12 – VM Concepts

## Slide 33: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 34: VM Address Translation
Virtual Address Space
  V = {0, 1, …, N–1}
Physical Address Space
  P = {0, 1, …, M–1}
Address Translation
  MAP: V  P U {}
  For virtual address a:
    MAP(a) = a’ if data at virtual address a is at physical address a’ in P
    MAP(a) =  if data at virtual address a is not in physical memory
      Either invalid or stored on disk

## Slide 35: Summary of Address Translation Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number

## Slide 36: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table base register (PTBR)
(CR3 in x86)
Page table
Physical page table
address for the current
process
Valid bit = 0:
Page not in memory
(page fault)
0
p-1
p
n-1
0
p-1
p
m-1
Valid bit = 1

## Slide 37: Address Translation: Page Hit
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5

## Slide 38: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim to page out (if dirty, writes pages to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7

## Slide 39: Integrating VM and Cache
VA
CPU
MMU
PTEA
PTE
PA
Data
Memory
PA
PA
miss
PTEA
PTEA
miss
PTEA
hit
PA
hit
Data
PTE
L1
cache
CPU Chip
VA: virtual address, PA: physical address, PTE: page table entry, PTEA = PTE address

## Slide 40: Speeding up Translation with a TLB
Page table entries (PTEs) are cached in L1 like any other memory word
  PTEs may be evicted by other data references
  PTE hit still requires a small L1 delay
Solution: Translation Lookaside Buffer (TLB)
  Small set-associative hardware cache in MMU
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages

## Slide 41: Summary of Address Translation Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number

## Slide 42: Accessing the TLB
MMU uses the VPN portion of the virtual address to access the TLB:
TLB tag (TLBT)
TLB index (TLBI)
0
p-1
p
n-1
VPO
VPN
p+t-1
p+t
PTE
tag
v
…
PTE
tag
v
Set 0
PTE
tag
v
PTE
tag
v
Set 1
PTE
tag
v
PTE
tag
v
Set T-1
T = 2t sets
TLBI selects the set
TLBT matches tag of line within set

## Slide 43: TLB Hit
MMU
Cache/
Memory
CPU
CPU Chip
VA
1
PA
4
Data
5
A TLB hit eliminates a cache/memory access
TLB
2
VPN
PTE
3

## Slide 44: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs an additional cache/memory access (the PTE) Fortunately, TLB misses are rare. Why?
Notes: Locality of reference. Each PTE corresponds to a 4KB page of memory (or larger, with huge pages)

## Slide 45: Multi-Level Page Tables
Suppose:
  4KB (212) page size, 48-bit address space, 8-byte PTE
Problem:
  Would need a 512 GB page table!
    248 * 2-12 * 23 = 239 bytes
Common solution: Multi-level page table
Example: 2-level page table
  Level 1 table: each PTE points to a page table (always memory resident)
  Level 2 table: each PTE points to a page (paged in and out like any other data)
Level 1
Table
...
Level 2
Tables
...

## Slide 46: A Two-Level Page Table Hierarchy
Level 1
page table
...
Level 2
page tables
VP 0
...
VP 1023
VP 1024
...
VP 2047
Gap
0
PTE 0
...
PTE 1023
PTE 0
...
PTE 1023
1023 null
PTEs
PTE 1023
1023
unallocated
pages
VP 9215
Virtual
memory
(1K - 9)
null PTEs
PTE 0
PTE 1
PTE 2 (null)
PTE 3 (null)
PTE 4 (null)
PTE 5 (null)
PTE 6 (null)
PTE 7 (null)
PTE 8
2K allocated VM pages
for code and data
6K unallocated VM pages
1023 unallocated pages
1 allocated VM page
for the stack
64 bit addresses, 8KB pages, 8-byte PTEs
Here, addresses increase from top to bottom
Notes: Not the usual layout for our address space figures, since addresses increase top-to-bottom instead of decrease.

## Slide 47: Translating with a k-level Page Table
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
the Level 1
page table
a Level 2
page table
a Level k
page table

## Slide 48: Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and programming
  Simplifies protection by providing a convenient interpositioning point to check permissions
Implemented via combination of hardware & software
  MMU, TLB, exception handling mechanisms part of hardware
  Page fault handlers, TLB management performed in software