## Slide 1: Bits, Bytes and Integers – Part 1 15-213/15-513: Introduction to Computer Systems 2nd Lecture, May 18, 2022
Instructors:
Zack Weinberg

## Slide 2: Waitlist questions
All waitlist questions should go to Amy Weis alweis@andrew.cmu.edu
Please don’t contact the instructors with waitlist questions.

## Slide 3: Reminder about in-person attendance
This room is full.
In-person classes are primarily for undergraduate students who are enrolled in 15-213.
If I told you in email to enroll in 513 for a reason other than “you’re a graduate student,” you are also entitled to be in this room.
If you’re enrolled in 15-513 because you are a graduate student, however, you may attend only if there is space.

## Slide 4: Roadmap – Inside a Computer
You may have seen this block diagram, or one like it, before.
CPU
RAM
GPU
Display
GPU
RAM
Network Adapter
Hard
Disk
Controller
The Internet
Disks
…
Bus

## Slide 5: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 6: Everything is bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.2V
0.9V
1.1V
0
1
0

## Slide 7: For example, can count in binary
Base 2 Number Representation
  Represent 1521310 as 111011011011012
  Represent 1.2010 as 1.0011001100110011[0011]…2
  Represent 1.5213 X 104 as 1.11011011011012 X 213

## Slide 8: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary
15213: 0011 1011 0110 1101
3
B
6
D

## Slide 9: Activity: binary, hexadecimal, twos complement
https://www.cs.cmu.edu/afs/cs/academic/class/15213-m22/www/activities/213_lecture2.pdf

## Slide 10: Preview: Combining bytes…
C Data Type | Typical 32-bit | Typical 64-bit
char | 1 | 1
short | 2 | 2
int | 4 | 4
long | 4 | 8
float | 8 | 8
double | 8 | 8
pointer | 4 | 8

## Slide 11: Preview: … to make integers
UMax = where w is the number of bits (“word size”)
UMin = 0
TMax =
TMin =
  Asymmetric!
  Because of zero