## Slide 1: Machine-Level Programming I: Basics 15-213/18-213: Introduction to Computer Systems 5th Lecture, May 25, 2022
Instructor:
Kyle Liang

## Slide 2: Announcements
Lab 2 (bomb lab) will be available via Autolab on May 27
  Due Friday June 3
Lab 1 is due Friday June 3 (handin via Autolab)
Written Assignment 1 is due Wednesday June 1
GDB bootcamp will be this Friday, May 27
  Exceptionally useful for labs–you’ll really want it for Lab 2.

## Slide 3: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 4: Intel x86 Processors
Dominate laptop/desktop/server market
  ARM architecture is a promising newcomer
Evolutionary design
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time goes on
    Now 3 volumes, about 5,000 pages of documentation
Complex instruction set computer (CISC)
  Many different instructions with many different formats
    But, only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But, Intel has done just that!
    In terms of speed. Less so for low power.

## Slide 5: Intel x86 Evolution: Milestones
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit Intel processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32 bit Intel processor , referred to as IA32
  Added “flat addressing”, capable of running Unix
Pentium 4E 2004 125M 2800-3800
  First 64-bit Intel x86 processor, referred to as x86-64
Core 2 2006 291M 1060-3333
  First multi-core Intel processor
Core i7 2008 731M 1600-4400
  Four cores (our shark machines)

## Slide 6: Intel x86 Processors, cont.
Machine Evolution
  386 1985 0.3M
  Pentium 1993 3.1M
  Pentium/MMX 1997 4.5M
  PentiumPro 1995 6.5M
  Pentium III 1999 8.2M
  Pentium 4 2000 42M
  Core 2 Duo 2006 291M
  Core i7 2008 731M
  Core i7 Skylake 2015 1.9B
Added Features
  Instructions to support multimedia operations
  Instructions to enable more efficient conditional operations
  Transition from 32 bits to 64 bits
  More cores

## Slide 7: Intel x86 Processors, cont.
Past Generations
  1st Pentium Pro 1995 600 nm
  1st Pentium III 1999 250 nm
  1st Pentium 4 2000 180 nm
  1st Core 2 Duo 2006 65 nm
Recent & Upcoming Generations
  Nehalem 2008 45 nm
  Sandy Bridge 2011 32 nm
  Ivy Bridge 2012 22 nm
  Haswell 2013 22 nm
  Broadwell 2014 14 nm
  Skylake 2015 14 nm
  Kaby Lake 2016 14 nm
  Coffee Lake 2017 14 nm
  Cannon Lake 2018 10 nm
  Ice Lake 2019 10 nm
  Tiger Lake 2020 10 nm
  Alder Lake 2022 “intel 7” (10nm+++)
Process technology
Process technology dimension = width of narrowest wires
(10 nm ≈ 100 atoms wide)
(But this is changing now.)

## Slide 8: 2018 State of the Art: Coffee Lake
Mobile Model: Core i7
  2.2-3.2 GHz
  45 W
Server Model: Xeon E
  Integrated graphics
  Multi-socket enabled
  3.3-3.8 GHz
  80-95 W
Desktop Model: Core i7
  Integrated graphics
  2.4-4.0 GHz
  35-95 W

## Slide 9: x86 Clones: Advanced Micro Devices (AMD)
Historically
  AMD has followed just behind Intel
  A little bit slower, a lot cheaper
Then
  Recruited top circuit designers from Digital Equipment Corp. and other downward trending companies
  Built Opteron: tough competitor to Pentium 4
  Developed x86-64, their own extension to 64 bits
Recent Years
  Intel got its act together
    1995-2011: Lead semiconductor “fab” in world
    2018: #2 largest by $$ (#1 is Samsung)
    2019: reclaimed #1
  AMD fell behind: Spun off GlobalFoundaries
  2019-20: Pulled ahead! Used TSMC for part of fab
  2022: Intel re-took the lead

## Slide 10: Intel’s 64-Bit History
2001: Intel Attempts Radical Shift from IA32 to IA64
  Totally different architecture (Itanium)
  Executes IA32 code only as legacy
  Performance disappointing
2003: AMD Steps in with Evolutionary Solution
  x86-64 (now called “AMD64”)
Intel Felt Obligated to Focus on IA64
  Hard to admit mistake or that AMD is better
2004: Intel Announces EM64T extension to IA32
  Extended Memory 64-bit Technology
  Almost identical to x86-64!
All but low-end x86 processors support x86-64
  But, lots of code still runs in 32-bit mode

## Slide 11: Our Coverage
IA32
  The traditional x86
  For 15/18-213: RIP, Summer 2015
x86-64
  The standard
  shark> gcc hello.c
  shark> gcc –m64 hello.c
Presentation
  Book covers x86-64
  Web aside on IA32
  We will only cover x86-64

## Slide 12: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 13: How Does a Computer Understand Code?
Short answer: Bits!
Not the complete picture, let’s take it bit by bit

## Slide 14: How Does a Person Understand English?
Let’s see how humans understand English
  English uses an alphabet
    A, B, C …
  Examine a sentence:
    Subject: (I) core noun of the sentence
    Object: (15213) supporting noun
    Verbs: (love) actions associating subject and object
I love 15213!

## Slide 15: How Does a CPU Understand Code (cont)?
What’s the language of the CPU?
  Basic building block is bits
  A sentence in English is like a program
  Subject and Object?
    Data Types: Integers, Floats, …
  Verb?
    Arithmetic Operations: +, -, /, *, <<, >>, …
CPU: Take data, apply action, use result
  Let’s encode: 1 + 2
    (+, 1, 2)
1 + 2
Notes: Ask students on verbs.

## Slide 16: Generalize Our Encoding
1 + 2 -> (+, 1, 2)
3 + 4 -> (+, 3, 4)
Let’s make specialized hardware in our CPU for +, -, …
Separate operations from data
  p = 1
  q = 2
  (+, p, q)
1 + 2
p
q
+

## Slide 17: Generalize Our Data Pipeline
CPU needs to supply p, q to our arithmetic unit
CPU uses registers to store information for the ALU
  (+, %p, %q)
But where do the registers get information?
  From the program, and in memory
    (Load, 0x1, %p)
    (Load, &0x7FFFF7AFCBA0, %q)
p
q
+

## Slide 18: Levels of Abstraction
C programmer
Assembly programmer
Computer Designer
#include <stdio.h>
int main(){
int i, n = 10, t1 = 0, t2 = 1, nxt;
for (i = 1; i <= n; ++i){
printf("%d, ", t1);
nxt = t1 + t2;
t1 = t2;
t2 = nxt; }
return 0; }
Gates, clocks, circuit layout, …

## Slide 19: Definitions
Architecture: (also ISA: instruction set architecture) The parts of a processor design that one needs to understand for writing assembly/machine code.
  Examples: instruction set specification, registers
Microarchitecture: Implementation of the architecture
  Examples: cache sizes and core frequency
Code Forms:
  Machine Code: The byte-level programs that a processor executes
  Assembly Code: A text representation of machine code
Example ISAs:
  Intel: x86, IA32, Itanium, x86-64
  ARM: Used in almost all mobile phones
  RISC V: New open-source ISA

## Slide 20: Assembly/Machine Code View
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
CPU
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte addressable array
    Code and user data
    Stack to support procedures
Rest in
Instruction Pointer
Notes: IP: instruction pointer

## Slide 21: Assembly Characteristics: Data Types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
Code: Byte sequences encoding series of instructions
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory
Notes: 10 bytes: extended precision, allows better calculation of double-precision

## Slide 22: Class Activity
Form teams of 2
One person should take notes / advise / etc
One person should ssh to a shark machine
  wget http://www.cs.cmu.edu/~213/activities/lec5.tar
  tar xf lec5.tar
  cd lec5
  ./act1

## Slide 23: x86-64 Integer Registers
%rsp
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
  Not part of memory (or cache)
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 24: Some History: IA32 Registers
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source
index
destination
index
stack
pointer
base
pointer
Origin
(mostly obsolete)

## Slide 25: Assembly Characteristics: Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches
  Indirect branches

## Slide 26: Moving Data
Moving Data
  movq Source, Dest
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “addressing modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN
Warning: Intel docs use mov Dest, Source

## Slide 27: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest

## Slide 28: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 29: Example of Simple Addressing Modes
whatAmI:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret
void
whatAmI(<type> a, <type> b)
{
????
}
%rdi
%rsi

## Slide 30: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 31: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 32: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 33: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 34: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 35: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 36: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 37: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 38: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]
Notes: Scale by byte, short, int, or long

## Slide 39: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 40: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 41: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 42: Address Computation Instruction
leaq Src, Dst
  Src is address mode expression
  Set Dst to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t = x+2*x
salq $2, %rax # return t<<2
Converted to ASM by compiler:

## Slide 43: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src Also called shlq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order! Src,Dest (Warning: Intel docs use “op Dest,Src”)
No distinction between signed and unsigned int (why?)

## Slide 44: Some Arithmetic Operations
One Operand Instructions
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
    notq Dest Dest = ~Dest
See book for more instructions

## Slide 45: Arithmetic Expression Example
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But, only used once
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret

## Slide 46: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z, t4
%rax | t1, t2, rval
%rcx | t5

## Slide 47: Recap: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Rounding, addition, multiplication
Example and properties
Floating point in C
Summary

## Slide 48: Recap: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac
  Example: 1521310 = (-1)0 x 1.11011011011012 x 213
Notes: M stands for mantissa

## Slide 49: Floating Point Operations: Basic Idea
x +f y = Round(x + y)
x ×f y = Round(x × y)
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into frac

## Slide 50: Rounding
Rounding Modes (illustrate with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
  Towards zero $1 $1 $1 $2 –$1
  Round down (−∞) $1 $1 $1 $2 –$2
  Round up (+∞) $2 $2 $2 $3 –$1
  Nearest Even (default) $1 $2 $2 $2 –$2

## Slide 51: Closer Look at Round-To-Even
Default Rounding Mode
  Hard to get any other kind without dropping into assembly
  C99 has support for rounding mode management
  All others are statistically biased
    Sum of set of positive numbers will consistently be over- or under- estimated
Applying to Other Decimal Places / Bit Positions
  When exactly halfway between two possible values
    Round so that least significant digit is even
  E.g., round to nearest hundredth
    7.8949999 7.89 (Less than half way)
    7.8950001 7.90 (Greater than half way)
    7.8950000 7.90 (Half way—round up)
    7.8850000 7.88 (Half way—round down)

## Slide 52: Rounding Binary Numbers
Binary Fractional Numbers
  “Even” when least significant bit is 0
  “Half way” when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
  Value Binary Rounded Action Rounded Value
  2 3/32 10.000112 10.002 (<1/2—down) 2
  2 3/16 10.001102 10.012 (>1/2—up) 2 1/4
  2 7/8 10.111002 11.002 ( 1/2—up) 3
  2 5/8 10.101002 10.102 ( 1/2—down) 2 1/2

## Slide 53: FP Multiplication
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands
4 bit mantissa: 1.010*22 x 1.110*23 = 10.0011*25
= 1.00011*26 = 1.001*26

## Slide 54: Floating Point Addition
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up
1.010*22 + 1.110*23 = (1.010 + 11.100)*22
= 100.110 * 22 = 1.0011 * 24 = 1.010 * 24

## Slide 55: Mathematical Properties of FP Add
Compare to those of Abelian Group
  Closed under addition?
    But may generate infinity or NaN
  Commutative?
  Associative?
    Overflow and inexactness of rounding
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
  0 is additive identity?
  Every element has additive inverse?
    Yes, except for infinities & NaNs
Monotonicity
  a ≥ b ⇒ a+c ≥ b+c?
    Except for infinities & NaNs
Yes
Yes
Yes
No
Almost
Almost

## Slide 56: Mathematical Properties of FP Mult
Compare to Commutative Ring
  Closed under multiplication?
    But may generate infinity or NaN
  Multiplication Commutative?
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
    Ex: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  1 is multiplicative identity?
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
Monotonicity
  a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    Except for infinities & NaNs
Yes
Yes
No
Yes
No
Almost

## Slide 57: Recap: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Rounding, addition, multiplication
Example and properties
Floating point in C
Summary

## Slide 58: Tiny Floating Point Example
8-bit Floating Point Representation
  the sign bit is in the most significant bit
  the next four bits are the exponent, with a bias of 7
  the last three bits are the frac
Same general form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s | exp | frac
1 | 4-bits | 3-bits

## Slide 59: Dynamic Range (Positive Only)
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias
(-1)0(0+1/4)*2-6
(-1)0(1+1/8)*2-6

## Slide 60: Distribution of Values
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
Notice how the distribution gets denser toward zero.
8 values
s | exp | frac
1 | 3-bits | 2-bits

## Slide 61: Distribution of Values (close-up view)
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 3
s | exp | frac
1 | 3-bits | 2-bits

## Slide 62: Special Properties of the IEEE Encoding
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider −0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield? The answer is complicated.
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity

## Slide 63: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Rounding, addition, multiplication
Example and properties
Floating point in C
Summary

## Slide 64: Floating Point in C
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode

## Slide 65: Floating Point Puzzles
For each of the following C expressions, either:
  Argue that it is true for all argument values
  Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (double)(float) d
f == -(-f);
2/3 == 2/3.0
d < 0.0 ⇒ ((d*2) < 0.0)
d > f ⇒ -f > -d
d * d >= 0.0
(d+f)-d == f
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NaN
Notes: Floats cannot represent all ints: only 25 bits in the

## Slide 66: Summary
IEEE Floating Point has clear mathematical properties
Represents numbers of form M x 2E
One can reason about operations independent of implementation
  As if computed with perfect precision and then rounded
Not the same as real arithmetic
  Violates associativity/distributivity
  Makes life difficult for compilers & serious numerical applications programmers

## Slide 67: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 68: Turning C into Object Code
text
text
binary
binary
Compiler (gcc –Og -S)
Assembler (gcc –c or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –Og p1.c p2.c -o p
    Use debugging-friendly optimizations (-Og)
    Put resulting binary in file p

## Slide 69: Compiling Into Assembly
C Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Obtain (on shark machine) with command
  gcc –Og –S sum.c
Produces file sum.s
Warning: Will get very different results on non-Shark machines (Andrew Linux, Mac OS-X, …) due to different versions of gcc and different compiler settings.

## Slide 70: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore

## Slide 71: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore
Things that look weird and are preceded by a ‘.’ are generally directives.
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Notes: Directives are notes to the assembler. They do not represent instructions are not translated to machine code.

## Slide 72: Object Code
Code for sumstore
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 14 bytes
  Each instruction 1, 3, or 5 bytes
  Starts at address 0x0400595
Notes: Object code is almost executable but lacks certain references across files. Linker resolves this.

## Slide 73: Machine Instruction Example
C Code
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Object Code
  3-byte instruction
  Stored at address 0x40059e
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 74: Disassembling Object Code
Disassembled
Disassembler
  objdump –d sum
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
0000000000400595 <sumstore>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 75: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore

## Slide 76: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore
  Examine the 14 bytes starting at sumstore
  x/14xb sumstore
Object Code
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3

## Slide 77: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91
Reverse engineering forbidden by
Microsoft End User License Agreement
Notes: EULA’s are particularly harmful: disassembly is a US federal right for educational purposes.

## Slide 78: Machine Programming I: Summary
History of Intel processors and architectures
  Evolutionary design leads to many quirks and artifacts
C, assembly, machine code
  New forms of visible state: program counter, registers, ...
  Compiler must transform statements, expressions, procedures into low-level instruction sequences
Assembly Basics: Registers, operands, move
  The x86-64 move instructions cover wide range of data movement forms
Arithmetic
  C compiler will figure out different instruction combinations to carry out computation