## Slide 1: Compressive sensing Motivation, theory, recovery
Linear inverse problems
Compressive sensing
  Theory
  Hallmark
  Recovery algorithms
Examples

## Slide 2: Linear inverse problems
Many classic problems in computer can be posed as linear inverse problems
Notation
  Signal of interest
  Observations
  Measurement model
Problem definition: given , recover
measurement noise
measurement matrix

## Slide 3: Linear inverse problems
Problem definition: given , recover
Scenario 1
We can invert the
system of equations

## Slide 4: Linear inverse problems
Problem definition: given , recover
Scenario 2

## Slide 5
Credit: Rob Fergus and Antonio Torralba

## Slide 6
Credit: Rob Fergus and Antonio Torralba

## Slide 7: Linear inverse problems
Problem definition: given , recover
Scenario 2
Measurement matrix has a
(N-M) dimensional null-space
Solution is no longer unique
Many interesting vision problem fall under this scenario

## Slide 8: Image super-resolution
Low resolution input/observation
128x128 pixels

## Slide 9: Image super-resolution
2x super-resolution

## Slide 10: Image super-resolution
4x super-resolution

## Slide 11: Image super-resolution
Super-resolution factor D
Under-sampling factor M/N = 1/D2
General rule:
The smaller the under-sampling, the more the unknowns and hence, the harder the super-resolution problem

## Slide 12: Many other vision problems…
Affine rank minimizaiton, Matrix completion, deconvolution, Robust PCA
Image synthesis
  Infilling, denoising, etc.
Light transport
  Reflectance fields, BRDFs, Direct global separation, Light transport matrices
Sensing

## Slide 13: Compressive sensing

## Slide 14: Sense by Sampling
sample
Notes: Example: Large Hadron Collider will produce 10 peta bytes of data per second; need to triage that down to 100/sec “potentially interesting events” in real time

## Slide 15: Sense by Sampling
sample
too
much
data!
Notes: Example: Large Hadron Collider will produce 10 peta bytes of data per second; need to triage that down to 100/sec “potentially interesting events” in real time

## Slide 16: Sense then Compress
compress
decompress
sample
JPEG
JPEG2000
…

## Slide 17: Sparsity
pixels
large wavelet coefficients
(blue = 0)

## Slide 18: Sparsity
pixels
large wavelet coefficients
(blue = 0)
wideband signal samples
large Gabor (TF) coefficients
time
frequency

## Slide 19: Concise Signal Structure
Sparse signal: only K out of N coordinates nonzero
sorted index

## Slide 20: Concise Signal Structure
Sparse signal: only K out of N coordinates nonzero
  model: union of K-dimensional subspaces aligned w/ coordinate axes
sorted index

## Slide 21: Concise Signal Structure
Sparse signal: only K out of N coordinates nonzero
  model: union of K-dimensional subspaces
Compressible signal: sorted coordinates decay rapidly with power-law
sorted index
power-law decay

## Slide 22: Concise Signal Structure
Sparse signal: only K out of N coordinates nonzero
  model: union of K-dimensional subspaces
Compressible signal: sorted coordinates decay rapidly with power-law
  model: ball:
sorted index
power-law decay

## Slide 23: What’s Wrong with this Picture?
Why go to all the work to acquire N samples only to discard all but K pieces of data?
compress
decompress
sample

## Slide 24: What’s Wrong with this Picture?
  linear processing
  linear signal model
  (bandlimited subspace)
compress
decompress
sample
  nonlinear processing
  nonlinear signal model
  (union of subspaces)

## Slide 25: Compressive Sensing
Directly acquire “compressed” data via dimensionality reduction
Replace samples by more general “measurements”
compressive sensing
recover

## Slide 26: Sampling
Signal is -sparse in basis/dictionary
  WLOG assume sparse in space domain
Sampling
sparse signal
nonzero entries
measurements

## Slide 27: Compressive Sampling
When data is sparse/compressible, can directly acquire a condensed representation with no/little information loss through linear dimensionality reduction
measurements
sparse signal
nonzero
entries

## Slide 28: How Can It Work?
Projection not full rank… … and so loses information in general
Ex: Infinitely many ’s map to the same (null space)

## Slide 29: How Can It Work?
Projection not full rank… … and so loses information in general
But we are only interested in sparse vectors
columns

## Slide 30: How Can It Work?
Projection not full rank… … and so loses information in general
But we are only interested in sparse vectors
is effectively MxK
columns

## Slide 31: Criterion for no information loss
No two points can map to the same point under action of
K-dim subspaces
Notes: 31

## Slide 32: Restricted Isometry Property (RIP)
“Stable embedding”
RIP of order 2K implies: for all K-sparse x1 and x2
K-dim subspaces

## Slide 33: RIP = Stable Embedding
An information preserving projection preserves the geometry of the set of sparse signals
RIP ensures that
Notes: 33

## Slide 34: How Can It Work?
Projection not full rank… … and so loses information in general
Design so that each of its Mx2K submatrices are full rank (RIP)
Unfortunately, a combinatorial, NP-complete design problem
columns

## Slide 35: Insight from the 70’s [Kashin, Gluskin]
Draw at random
  iid Gaussian
  iid Bernoulli
  …
Then has the RIP with high probability provided
columns

## Slide 36: Randomized Sensing
Measurements = random linear combinations of the entries of the signal
No information loss for sparse vectors whp
measurements
sparse signal
nonzero
entries

## Slide 37: CS Signal Recovery
Goal: Recover signal from measurements
Problem: Random projection not full rank (ill-posed inverse problem)
Solution: Exploit the sparse/compressible geometry of acquired signal

## Slide 38: CS Signal Recovery
Random projection not full rank
Recovery problem: given find
Null space
Search in null space for the “best” according to some criterion
  ex: least squares
(N-M)-dim hyperplane at random angle

## Slide 39: Signal Recovery
Recovery: given (ill-posed inverse problem) find (sparse)
Optimization:
Closed-form solution:

## Slide 40: Signal Recovery
Recovery: given (ill-posed inverse problem) find (sparse)
Optimization:
Closed-form solution:
Wrong answer!
Notes: 40

## Slide 41: Signal Recovery
Recovery: given (ill-posed inverse problem) find (sparse)
Optimization:
Closed-form solution:
Wrong answer!
Notes: 41

## Slide 42: Signal Recovery
Recovery: given (ill-posed inverse problem) find (sparse)
Optimization:
“find sparsest vector in translated nullspace”
Notes: 42

## Slide 43: Signal Recovery
Recovery: given (ill-posed inverse problem) find (sparse)
Optimization:
Correct!
But NP-Complete alg
“find sparsest vector in translated nullspace”
Notes: 43

## Slide 44: Signal Recovery
Recovery: given (ill-posed inverse problem) find (sparse)
Optimization:
Convexify the optimization
Candes Romberg Tao
Donoho
Notes: 44

## Slide 45: Signal Recovery
Recovery: given (ill-posed inverse problem) find (sparse)
Optimization:
Convexify the optimization
Correct!
Polynomial time alg (linear programming)
Notes: 45

## Slide 46: Compressive Sensing
Signal recovery via optimization [Candes, Romberg, Tao; Donoho]
random measurements
sparse signal
nonzero
entries
Notes: 46

## Slide 47: Compressive Sensing
Signal recovery via iterative greedy algorithm
  (orthogonal) matching pursuit [Gilbert, Tropp]
  iterated thresholding [Nowak, Figueiredo; Kingsbury, Reeves; Daubechies, Defrise, De Mol; Blumensath, Davies; …]
  CoSaMP [Needell and Tropp]
random measurements
sparse signal
nonzero
entries
Notes: 47

## Slide 48: CS Hallmarks
Stable
  acquisition/recovery process is numerically stable
Asymmetrical (most processing at decoder)
  conventional: smart encoder, dumb decoder
  CS: dumb encoder, smart decoder
Democratic
  each measurement carries the same amount of information
  robust to measurement loss and quantization
  “digital fountain” property
Random measurements encrypted
Universal
  same random projections / hardware can be used for any sparse signal class (generic)
Notes: 48

## Slide 49: Universality
Random measurements can be used for signals sparse in any basis

## Slide 50: Universality
Random measurements can be used for signals sparse in any basis

## Slide 51: Universality
Random measurements can be used for signals sparse in any basis
sparse coefficient
vector
nonzero
entries

## Slide 52: Examples

## Slide 53: Case Study 1: Periodic signals
Bottling line
Toothbrush
Credit: Veeraraghavan et al, 2011

## Slide 54: High-speed Camera
0
fMax
- fMax
Periodic signal has regularly spaced, sparse Fourier coefficients.
Is it necessary to use a high-speed video camera? Why waste bandwidth?
fP=1/P
2fP
-fP
-2fP
-4fP
-3fP
4fP
3fP
Nyquist Sampling of x(t) – When each period of x has high frequency variations, Nyquist sampling rate is high.
P = 10ms
Ts = 1/(2 fMax)

## Slide 55: Solving for the video
y
Camera observations at a pixel
A
x
=
Coded Strobing
Frame 1
Frame M
Frame Integration Period TS
N unknowns
t

## Slide 56: Solving for the video
Non-zero elements
Fourier Basis
Basis Coeff
x = F s
b1
b2
bN
t

## Slide 57: Solving for the video
y
F
s
=
A

## Slide 58: Implementation
PGR Dragonfly2
(25 fps)
FLC Shutter
Can flutter at 250us

## Slide 59: Toothbrush (simulation)
1000fps hi-speed camera
20fps normal camera
20fps coded strobing camera
Reconstructed frames

## Slide 60: Mill Tool
Normal Video: 25fps
Reconstructed Video at 2000fps
Mill tool rotating at 50Hz
Coded Strobing Video: 25fps
Mill tool rotating at 50Hz
Mill tool rotating at 50Hz

## Slide 61: Case Study 2: Spatial Multiplexing
Digital
micro-mirror device
Photo-detector

## Slide 62: Signal model
Motion flow
Credit: Ce Liu
Optical flow from I1 to I2
Two images I1 and I2

## Slide 63: Results
Final estimate (6 different videos)
Initial estimate (6 different videos) *animated gifs*
Single pixel camera with short-wave infrared detector
Sampling rate: 10,000 Hz
Number of compressive measurements: 65536
Total duration of data acquisition: 6 seconds
Reconstructed video resolution: 128x128x256

## Slide 64: Example 3: MRI
Lustig et al., 2008
MRI obtains samples in Fourier space
Taking lesser samples == higher speed of operation, less time etc.

## Slide 65: MRI
Least squares recovery
From 10 times lesser number of measurements
Lustig et al., 2008

## Slide 66: MRI
l1-recovery
From 10 times lesser number of measurements
The recovery is exact, provided some conditions are satisfied
Lustig et al., 2008

## Slide 67: Summary: CS
Compressive sensing
  randomized dimensionality reduction
  exploits signal sparsity information
  integrates sensing, compression, processing
Why it works: with high probability, random projections preserve information in signals with concise geometric structures
  sparse signals
  compressible signals

## Slide 68: Summary: CS
Encoding: = random linear combinations of the entries of
Decoding: Recover from via optimization
measurements
sparse signal
nonzero
entries
Notes: 68