signals

---
examples of signals
length of column of mercury in a thermometer
angles of hands on a clock
or needle of automobile speedometer
intensity and frequency of sound when a tool removes metal from stock turning in a lathe
electrical signals: voltage ~ power collected by antenna, current ~ light intensity, etc
digital signals: ADC + microprocessor convert electrical signal to message in some protocol

---
and unwanted signals (== noise)
light leaks thru a crack in your camera’s body
people talk at the table next to yours
strong radio station near weak one you want
observation-to-observation variation
measurand fluctuates (slouch or stand straight)
instrument fluctuates (meter stick trembles)
fundamental natural sources of fluctuation:
thermal motion (“Johnson” or “Nyquist” noise)
interval-to-interval statistical count variations (shot noise)
“chaos”, “uncertainty principle”, etc (1/f noise)

---
transduction

---
transduction (between modalities)
conversion of an environmental parameter into a signal is what we call sensing
temperature  length of mercury column
force  resistance of (stretched) length of wire
conversion of a signal into an environmental change is what we call actuation
finger pushes  lever moves  toilet flushes
signal  power amplifier  current through a resistor  heating of the environment
signal  power amplifier  robot arm motor  motion
the signal is almost always electrical ...
... in modern times; it wasn’t always so!

---
electrical signals
before ~1960s almost all signals were effectively length measurements:
temperature  length of column of mercury
 voltage  position of meter needle along arc
and occasionally some digital counting
e.g., geiger tube + electrical or electronic counter
by the 1980s almost all signals were electrical quantities represented digitally:
 voltage  light frequency (color) on sensor
 current  light intensity (power) on sensor
 parameters: resistance = voltage / current

---
review of elementary electricity & electronics

---
basic electrical concepts
charge: number of electrons, protons, etc
(each carrying a fundamental unit of charge)
current: charge per unit time flowing through an imagined surface that cuts a wire,
or flowing into or out of a device terminal
voltage: potential energy per unit charge,
“pressure” in response to which current flows
 general rule of transport:
measure of x {energy} per unit y {charge}
measure of y {charge} per unit time
rate {power} = (x/y) {voltage} * (y/t) {current}

---
basic electrical devices
resistor R (or, generally, impedance): current I that flows thru it ~ voltage V applied across it
capacitor C: time derivative of voltage applied across it ~ current that flows into or out of it
inductor L: time integral of voltage applied across it ~ current that flows through it
     I = {V/R, C dV/dt, ∫ V dt/L}
     V = {R I, ∫ I dt/C, L dI/dt}  most usual form
        = {R dQ/dt, Q/C, L d2Q/dt2}
 Q = {∫Vdt/R, CV, ∫ ∫ V dt dt’/L}

---
electrical & electronic sensors

---
basic electrical sensors
many are sources of voltage, current, or charge
CCD pixel voltage ~ integrated light intensity
Ionscan signal current ~ explosive vapor concentration
Geiger tube charge pulse ~ incident ionizing radiation particle energy
many others are “parametric”
strain gauge resistance ~ stretching of wire
humidity sensor capacitance ~ relative humidity
proximity sensor inductance ~ nearby metal

---
From which you should be able to
convince yourself
that in series resistances, inductances, and reciprocal capacitances add,
whereas in parallel
reciprocal resistances,
reciprocal inductances,
and capacitances add
(with the proviso, for inductors, that they are really independent, i.e.,
they do not share each others magnetic fields)

---
We will see
later, when
we discuss
AC signals
and their
decomposition
into Fourier
frequency
components,
that “dot” or “d/dt”
is usefully written
j2f
and
“integral dt”
is usefully written
1/ j2f

---
basic principle is often concealed!