data acquisition

---
read …
Fraden Chapter 5,
Interface Electronic Circuits
for some additional details and an alternative perspective to mine

---
topics ...
data acquisition
sensor-to-signal interface
usually means convert some interesting environmental parameter to a signal voltage
“signal conditioning”
convert analog signal to digital format (ADC)
communicate signal to computer

---
data acquisition (& control)

---
sensor-to-signal interface
action of environment on sensor causes
it to generate an electrical signal directly
voltage source (V)
current (I) or charge (Q) source
action of environment on sensor changes an electrical parameter that we can measure
resistance changes: V ~ I
capacitance changes: V ~ ∫ I dt, I ~ dV/dt
inductance changes: V ~ dI/dt, I ~ ∫ V dt

---
example:
current-to-voltage conversion
simple: I = Vmeasured / Rknown
better: use an “op amp”

---
signal conditioning
filter for expected frequency regime
subtract DC offset (“zeroing”)
amplify or attenuate signal (“scaling”)
linearize relationship between measurand and observed electrical parameter
now usually done in software after ADC
etc ...

---
example: AD594/595

---
analog-to-digital converter (ADC)
many different principles
often integrated with microcontrollers
in some types, e.g., “successive approximation”, the CPU to participates in the conversion
guess what the digital output should be
feed it to a digital-to-analog converter
compare analog input & output and iterate
all involve trade-offs of speed (conversion time), resolution (number of bits), and cost
“flash converter” is fastest, lowest resolution, highest cost: required for video digitization

---
flash converter (video applications)
data acquisition

---
 Σ-Δ converter (“one-bit” audio)
data acquisition

---
communication with computer
dedicated: DAQ/C (data acquisition & control) system with embedded processors
tightly integrated: card resides in PC slot
a little less tight: bus extender “boxes”
“box” connected to parallel/serial/USB port
or just a “dongle” plugged into the port
IEEE-4888 instrumentation bus: parallel address, control, and data lines
networked: instrument assigned IP address

---
example: USB DAQ/C for $129
data acquisition

---
DAQ/C software
low level:
software “pokes” setup into input registers
software “peeks” data stashed in output registers
high level:
set-up and acquire data
set-up and provide system control signals
analyze data (Fourier transforms, statistics, etc)
interactive graphic visualization (“presentation”)
archiving data
formatting as required by target journal
etc

---
example: LabVIEW

---
assignment
(24) There are many articles on the statistics of the time differences between successive drops from a dripping faucet. Design a data acquisition & control system for this problem: identify suitable commercial hardware (and optionally software), and show the control program’s logic. Avoid hardware “overkill”, i.e., features and ranges that you don’t need, as these add expense and complexity.

---
next topic … sensors!
light sensors
basic principles of image sensors