## Slide 1: Machine-Level Programming IV: Data 15-213: Introduction to Computer Systems 7th Lecture, September 20, 2022
Instructors:
Dave Andersen (15-213)
Zack Weinberg (15-213)
Brian Railing (15-513)
David Varodayan (14-513)

## Slide 2: Today
Partial recap: Integers
  Word size
  Addresses
One-Dimensional Arrays
Structs
  Alignment
  Arrays of Structs
Multi-Dimensional Arrays
  Nested (Arrays of Arrays)
  (Arrays of) Pointers to Arrays
If we have time:
  Endianness
  Machine Instructions

## Slide 3: Byte-Oriented Memory Organization
Programs refer to data by address
  Imagine all of RAM as an enormous array of bytes
  An address is an index into that array
    A pointer variable stores an address
System provides a private address space to each “process”
  A process is an instance of a program, being executed
  An address space is one of those enormous arrays of bytes
  Each program can see only its own code and data within its enormous array
  We’ll come back to this later (“virtual memory” classes)
• • •
00•••0
FF•••F

## Slide 4: Machine Words
Any given computer has a “Word Size”
  Nominal size of integer-valued data
    and of addresses
  Until recently, most machines used 32 bits (4 bytes) as word size
    Limits addresses to 4GB (232 bytes)
  Increasingly, machines have 64-bit word size
    Potentially, could have 16 EB (exabytes) of addressable memory
    That’s bytes
  Machines still support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 5: Addresses Always Specify Byte Locations
Address of a word is address of the first byte in the word
Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 6: Today
Partial recap: Integers
  Word size
  Addresses
One-Dimensional Arrays
Structs
  Alignment
  Arrays of Structs
Multi-Dimensional Arrays
  Nested (Arrays of Arrays)
  (Arrays of) Pointers to Arrays
If we have time:
  Endianness
  Machine Instructions
Activity break: pick a partner (just one other student this time),
open activity (https://canvas.cmu.edu/courses/30386/assignments/528617), do parts 1 and 2

## Slide 7: Array Allocation
Basic Principle
  T A[L];
  Array of data type T and length L
  Contiguously allocated region of L * sizeof(T) bytes in memory
char string[12];
x
x + 12
int val[5];
x
x + 4
x + 8
x + 12
x + 16
x + 20
double a[3];
x + 24
x
x + 8
x + 16
char *p[3];
x
x + 8
x + 16
x + 24

## Slide 8: Array Access
Basic Principle
  T A[L];
  Array of data type T and length L
  Identifier A can be used as a pointer to array element 0: Type T*
Reference Type Value
  val[4] int 3
  val int * x
  val+1 int * x + 4
  &val[2] int * x + 8
  val[5] int ??
  *(val+1) int 5 //val[1]
  val + i int * x + 4 * i //&val[i]
int val[5];
1
5
2
1
3
x
x + 4
x + 8
x + 12
x + 16
x + 20

## Slide 9: Array Example
Declaration “zip_dig cmu” equivalent to “int cmu[5]”
Example arrays were allocated in successive 20 byte blocks
  Not guaranteed to happen in general
#define ZLEN 5
typedef int zip_dig[ZLEN];
zip_dig cmu = { 1, 5, 2, 1, 3 };
zip_dig mit = { 0, 2, 1, 3, 9 };
zip_dig ucb = { 9, 4, 7, 2, 0 };
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36
zip_dig mit;
0
2
1
3
9
36
40
44
48
52
56
zip_dig ucb;
9
4
7
2
0
56
60
64
68
72
76

## Slide 10: Array Accessing Example
Register %rdi contains starting address of array
Register %rsi contains array index
Desired digit at %rdi + 4*%rsi
Use memory reference (%rdi,%rsi,4)
int get_digit
(zip_dig z, int digit)
{
return z[digit];
}
# %rdi = z
# %rsi = digit
movl (%rdi,%rsi,4), %eax # z[digit]
x86-64
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36

## Slide 11: Array Loop Example
# %rdi = z
movl $0, %eax # i = 0
jmp .L3 # goto middle
.L4: # loop:
addl $1, (%rdi,%rax,4) # z[i]++
addq $1, %rax # i++
.L3: # middle
cmpq $4, %rax # i:4
jbe .L4 # if <=, goto loop
rep; ret

## Slide 12: Array Loop Example
# %rdi = z
movl $0, %eax # i = 0
jmp .L3 # goto middle
.L4: # loop:
addl $1, (%rdi,%rax,4) # z[i]++
addq $1, %rax # i++
.L3: # middle
cmpq $4, %rax # i:4
jbe .L4 # if <=, goto loop
rep; ret
void zincr(zip_dig z) {
size_t i;
for (i = 0; i < ZLEN; i++)
z[i]++;
}

## Slide 13: Understanding Pointers & Arrays #1
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3] |  |  |  |  |  | 
int *A2 |  |  |  |  |  | 

## Slide 14: Understanding Pointers & Arrays #1
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3] | Y | N | 12 | Y | N | 4
int *A2 | Y | N | 8 | Y | Y | 4
A1
A2
Allocated int
Unallocated pointer
Allocated pointer
Unallocated int

## Slide 15: Understanding Pointers & Arrays #2
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  |  | **An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3] |  |  |  |  |  |  |  |  | 
int *A2[3] |  |  |  |  |  |  |  |  | 
int (*A3)[3] |  |  |  |  |  |  |  |  | 
int (*A4[3]) |  |  |  |  |  |  |  |  | 

## Slide 16: Understanding Pointers & Arrays #2
Decl | An |  |  | *An |  |  | **An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3] | Y | N | 12 | Y | N | 4 | N | - | -
int *A2[3] | Y | N | 24 | Y | N | 8 | Y | Y | 4
int (*A3)[3] | Y | N | 8 | Y | Y | 12 | Y | Y | 4
int (*A4[3]) | Y | N | 24 | Y | N | 8 | Y | Y | 4
A1
A2/A4
Allocated int
Unallocated pointer
Allocated pointer
Unallocated int
A3

## Slide 17: Today
Partial recap: Integers
  Word size
  Addresses
One-Dimensional Arrays
Structs
  Alignment
  Arrays of Structs
Multi-Dimensional Arrays
  Nested (Arrays of Arrays)
  (Arrays of) Pointers to Arrays
If we have time:
  Endianness
  Machine Instructions
Activity break: do parts 3 and 4 now

## Slide 18: Structure Representation
Structure represented as block of memory
  Big enough to hold all of the fields
Fields ordered according to declaration
  Even if another ordering could yield a more compact representation
Compiler determines overall size + positions of fields
  Machine-level program has no understanding of the structures in the source code
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};

## Slide 19: Generating Pointer to Structure Member
# r in %rdi, idx in %rsi
leaq (%rdi,%rsi,4), %rax
ret
int *get_ap
(struct rec *r, size_t idx)
{
return &r->a[idx];
}
Generating Pointer to Array Element
  Offset of each structure member determined at compile time
  Compute as r + 4*idx
r+4*idx
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};

## Slide 20: Following Linked List
.L11: # loop:
movslq 16(%rdi), %rax # i = M[r+16]
movl %esi, (%rdi,%rax,4) # M[r+4*i] = val
movq 24(%rdi), %rdi # r = M[r+24]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
C Code
Register | Value
%rdi | r
%rsi | val
struct rec {
int a[4];
int i;
struct rec *next;
};
Element i
r
i
next
0
16
24
32
a

## Slide 21: Structures & Alignment
Unaligned Data
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8
c
i[0]
i[1]
v
p
p+1
p+5
p+9
p+17
struct S1 {
char c;
int i[2];
double v;
} *p;

## Slide 22: Alignment Principles
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
  Required on some machines; advised on x86-64
Motivation for Aligning Data
  Memory accessed by (aligned) chunks of 4 or 8 bytes (system dependent)
    Inefficient to load or store datum that spans quad word boundaries
    Virtual memory trickier when datum spans 2 pages
Compiler
  Inserts gaps in structure to ensure correct alignment of fields

## Slide 23: Specific Cases of Alignment (x86-64)
1 byte: char, …
  no restrictions on address
2 bytes: short, …
  lowest 1 bit of address must be 02
4 bytes: int, float, …
  lowest 2 bits of address must be 002
8 bytes: double, long, char *, …
  lowest 3 bits of address must be 0002

## Slide 24: Satisfying Alignment with Structures
struct S1 {
char c;
int i[2];
double v;
} *p;
Within structure:
  Must satisfy each element’s alignment requirement
Overall structure placement
  Each structure has alignment requirement K
    K = Largest alignment of any element
  Initial address & structure length must be multiples of K
Example:
  K = 8, due to double element
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8

## Slide 25: Meeting Overall Alignment Requirement
For largest alignment requirement K
Overall structure must be multiple of K
struct S2 {
double v;
int i[2];
char c;
} *p;
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
p+0 |  |  |  |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  |  |  |  |  | p+24 | 
Multiple of K=8

## Slide 26: Saving Space
Put large data types first
Effect (K=4)
struct S4 {
char c;
int i;
char d;
} *p;
struct S5 {
int i;
char c;
char d;
} *p;
c
i
3 bytes
d
3 bytes
c
i
d
2 bytes

## Slide 27: Arrays of Structures
Overall structure length multiple of K
Satisfy alignment requirement for every element
struct S2 {
double v;
int i[2];
char c;
} a[10];
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
a+24 |  |  |  |  |  |  | a+32 |  |  |  |  |  |  |  | a+40 |  |  |  |  |  |  |  | a+48 | 
 | a[0] |  |  |  |  | a[1] |  |  |  |  | a[2] |  |  |  |  | • • • |  |  |  |  |  | 
a+0 |  |  |  |  | a+24 |  |  |  |  | a+48 |  |  |  |  | a+72 |  |  |  |  |  |  | 

## Slide 28: Accessing Array Elements
Compute array offset 12*idx
  sizeof(S3), including alignment spacers
Element j is at offset 8 within structure
Assembler gives offset a+8
  Resolved during linking
struct S3 {
short i;
float v;
short j;
} a[10];
short get_j(int idx)
{
return a[idx].j;
}
# %rdi = idx
leaq (%rdi,%rdi,2),%rax # 3*idx
movzwl a+8(,%rax,4),%eax
 | a[0] |  |  |  |  | • • • |  |  |  | a[idx] |  |  |  | • • |  |  | • |  |  | 
a+0 |  |  |  |  | a+12 |  |  |  | a+12*idx |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | i | 2 bytes |  | v |  |  | j | 2 bytes |  |  | 
 |  |  |  | a+12*idx |  |  |  |  |  | a+12*idx+8 |  |  |  |  | 
Notes: Give the pseudo-code for the assembly, which field / element is being accessed?

## Slide 29: Today
Partial recap: Integers
  Word size
  Addresses
One-Dimensional Arrays
Structs
  Alignment
  Arrays of Structs
Multi-Dimensional Arrays
  Nested (Arrays of Arrays)
  (Arrays of) Pointers to Arrays
If we have time:
  Endianness
  Machine Instructions
Activity break: do part 5 now

## Slide 30: Multidimensional (Nested) Arrays
Declaration
  T A[R][C];
  2D array of data type T
  R rows, C columns
  Type T element requires K bytes
Array Size
  R * C * K bytes
Arrangement
  Row-Major Ordering
A[0][0]
A[0][C-1]
A[R-1][0]
• • •
• • •
A[R-1][C-1]
•
•
•
•
•
•
int A[R][C];
• • •
A
[0]
[0]
A
[0]
[C-1]
• • •
A
[1]
[0]
A
[1]
[C-1]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
• • •
4*R*C Bytes
Notes: Board: show 3D example: a[2][3][2] to illustrate the idea of row major as enumerating indices from right to left

## Slide 31: Nested Array Example
“zip_dig pgh[4]” equivalent to “int pgh[4][5]”
  Variable pgh: array of 4 elements, allocated contiguously
  Each element is an array of 5 int’s, allocated contiguously
“Row-Major” ordering of all elements in memory
#define PCOUNT 4
zip_dig pgh[PCOUNT] =
{{1, 5, 2, 0, 6},
{1, 5, 2, 1, 3 },
{1, 5, 2, 1, 7 },
{1, 5, 2, 2, 1 }};
zip_dig
pgh[4];
76
96
116
136
156
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1

## Slide 32: Nested Array Row Access
• • •
Row Vectors
  A[i] is array of C elements
  Each element of type T requires K bytes
  Starting address A + i * (C * K)
• • •
A
[i]
[0]
A
[i]
[C-1]
A[i]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
A[R-1]
• • •
A
• • •
A
[0]
[0]
A
[0]
[C-1]
A[0]
A+(i*C*4)
A+((R-1)*C*4)
int A[R][C];

## Slide 33: Nested Array Row Access Code
Row Vector
  pgh[index] is array of 5 int’s
  Starting address pgh+20*index
Machine Code
  Computes and returns address
  Compute as pgh + 4*(index+4*index)
int *get_pgh_zip(int index)
{
return pgh[index];
}
# %rdi = index
leaq (%rdi,%rdi,4),%rax # 5 * index
leaq pgh(,%rax,4),%rax # pgh + (20 * index)
pgh
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1
pgh[2]

## Slide 34: Nested Array Element Access
• • •
Array Elements
  A[i][j] is element of type T, which requires K bytes
  Address A + i * (C * K) + j * K = A + (i * C + j) * K
• • • • • •
A
[i]
[j]
A[i]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
A[R-1]
• • •
A
• • •
A
[0]
[0]
A
[0]
[C-1]
A[0]
A+(i*C*4)
A+((R-1)*C*4)
int A[R][C];
A+(i*C*4)+(j*4)

## Slide 35: Nested Array Element Access Code
Array Elements
  pgh[index][dig] is int
  Address: pgh + 20*index + 4*dig
    = pgh + 4*(5*index + dig)
int get_pgh_digit(int index, int dig)
{
return pgh[index][dig];
}
leaq (%rdi,%rdi,4), %rax # 5*index
addl %rax, %rsi # 5*index+dig
movl pgh(,%rsi,4), %eax # M[pgh + 4*(5*index+dig)]
pgh
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1
pgh[1][1]

## Slide 36: Multi-Level Array Example
Variable univ denotes array of 3 elements
Each element is a pointer
  8 bytes
Each pointer points to array of int’s
zip_dig cmu = { 1, 5, 2, 1, 3 };
zip_dig mit = { 0, 2, 1, 3, 9 };
zip_dig ucb = { 9, 4, 7, 2, 0 };
#define UCOUNT 3
int *univ[UCOUNT] = {mit, cmu, ucb};
36
160
16
56
168
176
univ
cmu
mit
ucb
1
5
2
1
3
16
20
24
28
32
36
0
2
1
3
9
36
40
44
48
52
56
9
4
7
2
0
56
60
64
68
72
76

## Slide 37: Element Access in Multi-Level Array
Computation
  Element access Mem[Mem[univ+8*index]+4*digit]
  Must do two memory reads
    First get pointer to row array
    Then access element within array
salq $2, %rsi # 4*digit
addq univ(,%rdi,8), %rsi # p = univ[index] + 4*digit
movl (%rsi), %eax # return *p
ret
int get_univ_digit
(size_t index, size_t digit)
{
return univ[index][digit];
}

## Slide 38: Array Element Accesses
int get_pgh_digit
(size_t index, size_t digit)
{
return pgh[index][digit];
}
int get_univ_digit
(size_t index, size_t digit)
{
return univ[index][digit];
}
Nested array
Multi-level array
Accesses looks similar in C, but address computations very different:
Mem[pgh+20*index+4*digit]
Mem[Mem[univ+8*index]+4*digit]

## Slide 39: N X N Matrix Code
Fixed dimensions
  Know value of N at compile time
Variable dimensions, explicit indexing
  Traditional way to implement dynamic arrays
Variable dimensions, implicit indexing
  “New” feature in C99
#define N 16
typedef int fix_matrix[N][N];
/* Get element A[i][j] */
int fix_ele(fix_matrix A,
size_t i, size_t j)
{
return A[i][j];
}
#define IDX(n, i, j) ((i)*(n)+(j))
/* Get element A[i][j] */
int vec_ele(size_t n, int *A,
size_t i, size_t j)
{
return A[IDX(n,i,j)];
}
/* Get element a[i][j] */
int var_ele(size_t n, int A[n][n],
size_t i, size_t j) {
return A[i][j];
}

## Slide 40: Summary
Arrays
  Elements packed into contiguous region of memory
  Use index arithmetic to locate individual elements
Structures
  Elements packed into single region of memory
  Access using offsets determined by compiler
  Possible require internal and external padding to ensure alignment
Combinations
  Can nest structure and array code arbitrarily

## Slide 41: Today
Partial recap: Integers
  Word size
  Addresses
One-Dimensional Arrays
Structs
  Alignment
  Arrays of Structs
Multi-Dimensional Arrays
  Nested (Arrays of Arrays)
  (Arrays of) Pointers to Arrays
If we have time:
  Endianness
  Machine Instructions
Activity break: do part 6 now

## Slide 42: Byte Ordering
So, how are the bytes within a multi-byte word ordered in memory?
Conventions
  Big Endian: Sun, PPC Mac, network packet headers
    Least significant byte has highest address
  Little Endian: x86, ARM processors running Android, iOS, and Windows
    Least significant byte has lowest address

## Slide 43: Byte Ordering Example
Example
  Variable x has 4-byte value of 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 44: Examining Data Representations
Code to Print Byte Representation of Data
  Casting pointer to unsigned char * allows treatment as a byte array
Printf directives:
%p: Print pointer (must be void *)
%.2x: Print integer in hexadecimal, with at least two digits
void show_bytes(unsigned char *start, size_t len){
size_t i;
for (i = 0; i < len; i++) {
printf("%p\t%.2x\n",
(void *)&start[i], start[i]);
} }

## Slide 45: show_bytes Execution Example
int a = 15213;
printf("int a = %d;\n“, a);
show_bytes((unsigned char *) &a, sizeof(int));
Result (Linux x86-64):
int a = 15213;
0x7fffb7f71dbc 6d
0x7fffb7f71dbd 3b
0x7fffb7f71dbe 00
0x7fffb7f71dbf 00

## Slide 46: Representing Pointers
Different compilers & machines assign different locations to objects
May even get different results each time program is run (ASLR)
int B = -15213;
int *P = &B;
x86-64
Sun
IA32
EF
FF
FB
2C
AC
28
F5
FF
3C
1B
FE
82
FD
7F
00
00

## Slide 47: Representing Strings
char S[6] = "18213";
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
IA32
Sun
31
38
32
31
33
00
31
38
32
31
33
00

## Slide 48: A note about x86 machine code
Address Instruction Code Assembly Rendition
8048365: 5b pop %ebx
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
804836c: 83 bb 28 00 00 00 00 cmpl $0x0,0x28(%ebx)
x86 machine code is a sequence of bytes
  Grouped into variable-length instructions, which look like strings…
  But they contain embedded little-endian numbers…
Example Fragment
Deciphering Numbers
  Value: 0x12ab
  Pad to 32 bits: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse: ab 12 00 00

## Slide 49: A peek at x86 instruction encoding
Operand size = 16 bits
ModRM byte: cx/r9, di, “addressing mode”
REX prefix: adjust sizes and register numbers
Primary opcode: MOV reg → mem + some operand size info
REX becomes a set of primary opcodes
Address size changes to 32 bits
and its long, complex history
Address size changes to 16 bits, register numbering is different
Now means: Operand size = 32 bits
64-bit mode…
88 0f mov %cl, (%rdi)
66 89 0f mov %cx, (%rdi)
89 0f mov %ecx, (%rdi)
48 89 0f mov %rcx, (%rdi)
44 88 0f mov %r9b, (%rdi)
66 44 89 0f mov %r9w, (%rdi)
44 89 0f mov %r9d, (%rdi)
4c 89 0f mov %r9, (%rdi)
Same bytes interpreted in 32-bit mode…
88 0f mov %cl, (%edi)
66 89 0f mov %cx, (%edi)
89 0f mov %ecx, (%edi)
48 dec %eax
44 inc %esp
66 44 inc %sp
4c dec %esp
and 16-bit mode …
88 0f mov %cl, (%bx)
66 89 0f mov %ecx, (%bx)
89 0f mov %cx, (%bx)
44 inc %sp
66 44 inc %esp

## Slide 50: Extra material
None of this will be on the exam, but you might be curious…

## Slide 51: 16 X 16 Matrix Access
/* Get element A[i][j] */
int fix_ele(fix_matrix A, size_t i, size_t j) {
return A[i][j];
}
# A in %rdi, i in %rsi, j in %rdx
salq $6, %rsi # 64*i
addq %rsi, %rdi # A + 64*i
movl (%rdi,%rdx,4), %eax # M[A + 64*i + 4*j]
ret
Array Elements
  int A[16][16];
  Address A + i * (C * K) + j * K
  C = 16, K = 4

## Slide 52: n X n Matrix Access
/* Get element A[i][j] */
int var_ele(size_t n, int A[n][n], size_t i, size_t j) {
return A[i][j];
}
# n in %rdi, A in %rsi, i in %rdx, j in %rcx
imulq %rdx, %rdi # n*i
leaq (%rsi,%rdi,4), %rax # A + 4*n*i
movl (%rax,%rcx,4), %eax # A + 4*n*i + 4*j
ret
Array Elements
  size_t n;
  int A[n][n];
  Address A + i * (C * K) + j * K
  C = n, K = 4
  Must perform integer multiplication
Notes: Why multiply?

## Slide 53: Example: Array Access
#include <stdio.h>
#define ZLEN 5
#define PCOUNT 4
typedef int zip_dig[ZLEN];
int main(int argc, char** argv) {
zip_dig pgh[PCOUNT] =
{{1, 5, 2, 0, 6},
{1, 5, 2, 1, 3 },
{1, 5, 2, 1, 7 },
{1, 5, 2, 2, 1 }};
int *linear_zip = (int *) pgh;
int *zip2 = (int *) pgh[2];
int result =
pgh[0][0] +
linear_zip[7] +
*(linear_zip + 8) +
zip2[1];
printf("result: %d\n", result);
return 0;
}
linux> ./array
result: 9
Notes: Stop and ask students to work out what this might print.

## Slide 54: Example: Array Access
#include <stdio.h>
#define ZLEN 5
#define PCOUNT 4
typedef int zip_dig[ZLEN];
int main(int argc, char** argv) {
zip_dig pgh[PCOUNT] =
{{1, 5, 2, 0, 6},
{1, 5, 2, 1, 3 },
{1, 5, 2, 1, 7 },
{1, 5, 2, 2, 1 }};
int *linear_zip = (int *) pgh;
int *zip2 = (int *) pgh[2];
int result =
pgh[0][0] +
linear_zip[7] +
*(linear_zip + 8) +
zip2[1];
printf("result: %d\n", result);
return 0;
}
linux> ./array
result: 9

## Slide 55: Understanding Pointers & Arrays #3
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  |  | **An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3][5] |  |  |  |  |  |  |  |  | 
int *A2[3][5] |  |  |  |  |  |  |  |  | 
int (*A3)[3][5] |  |  |  |  |  |  |  |  | 
int *(A4[3][5]) |  |  |  |  |  |  |  |  | 
int (*A5[3])[5] |  |  |  |  |  |  |  |  | 
Decl | ***An |  | 
 | Cmp | Bad | Size
int A1[3][5] |  |  | 
int *A2[3][5] |  |  | 
int (*A3)[3][5] |  |  | 
int *(A4[3][5]) |  |  | 
int (*A5[3])[5] |  |  | 

## Slide 56
Declaration
int A1[3][5]
int *A2[3][5]
int (*A3)[3][5]
int *(A4[3][5])
int (*A5[3])[5]
A2/A4
A5
Allocated int
Unallocated pointer
Allocated pointer
Unallocated int
Allocated pointer to unallocated int
A1
A3

## Slide 57: Understanding Pointers & Arrays #3
Cmp: Compiles (Y/N)
Bad: Possible bad pointer reference (Y/N)
Size: Value returned by sizeof
Decl | An |  |  | *An |  |  | **An |  | 
 | Cmp | Bad | Size | Cmp | Bad | Size | Cmp | Bad | Size
int A1[3][5] | Y | N | 60 | Y | N | 20 | Y | N | 4
int *A2[3][5] | Y | N | 120 | Y | N | 40 | Y | N | 8
int (*A3)[3][5] | Y | N | 8 | Y | Y | 60 | Y | Y | 20
int *(A4[3][5]) | Y | N | 120 | Y | N | 40 | Y | N | 8
int (*A5[3])[5] | Y | N | 24 | Y | N | 8 | Y | Y | 20
Decl | ***An |  | 
 | Cmp | Bad | Size
int A1[3][5] | N | - | -
int *A2[3][5] | Y | Y | 4
int (*A3)[3][5] | Y | Y | 4
int *(A4[3][5]) | Y | Y | 4
int (*A5[3])[5] | Y | Y | 4

## Slide 58: Example Struct Exam Question
http://www.cs.cmu.edu/~213/oldexams/exam1-f12.pdf

## Slide 59: Example Struct Exam Question
http://www.cs.cmu.edu/~213/oldexams/exam1-f12.pdf
a
X
X
X
X
X
X
X
b
b
b
b
b
b
b
b
c
c
c
c
d
d
d
X
e
e
e
e
e
e
e
e
f
f
f
f
f
f
f
f

## Slide 60: Example Struct Exam Question (Cont’d)
http://www.cs.cmu.edu/~213/oldexams/exam1-f12.pdf

## Slide 61: Example Struct Exam Question (Cont’d)
a
d
d
d
c
c
c
c
b
b
b
b
b
b
b
b
e
e
e
e
e
e
e
e
f
f
f
f
f
f
f
f
http://www.cs.cmu.edu/~213/oldexams/exam1-f12.pdf

## Slide 62: Background
History
  x87 FP
    Legacy, very ugly
  SSE FP
    Supported by Shark machines
    Special case use of vector instructions
  AVX FP
    Newest version
    Similar to SSE
    Documented in book

## Slide 63: Programming with SSE3
XMM Registers
  16 total, each 16 bytes
  16 single-byte integers
  8 16-bit integers
  4 32-bit integers
  4 single-precision floats
  2 double-precision floats
  1 single-precision float
  1 double-precision float

## Slide 64: Scalar & SIMD Operations
  Scalar Operations: Single Precision
  SIMD Operations: Single Precision
  Scalar Operations: Double Precision
+
%xmm0
%xmm1
addss %xmm0,%xmm1
+
+
+
+
%xmm0
%xmm1
addps %xmm0,%xmm1
+
%xmm0
%xmm1
addsd %xmm0,%xmm1

## Slide 65: FP Basics
Arguments passed in %xmm0, %xmm1, ...
Result returned in %xmm0
All XMM registers caller-saved
float fadd(float x, float y)
{
return x + y;
}
double dadd(double x, double y)
{
return x + y;
}
# x in %xmm0, y in %xmm1
addss %xmm1, %xmm0
ret
# x in %xmm0, y in %xmm1
addsd %xmm1, %xmm0
ret

## Slide 66: FP Memory Referencing
Integer (and pointer) arguments passed in regular registers
FP values passed in XMM registers
Different mov instructions to move between XMM registers, and between memory and XMM registers
double dincr(double *p, double v)
{
double x = *p;
*p = x + v;
return x;
}
# p in %rdi, v in %xmm0
movapd %xmm0, %xmm1 # Copy v
movsd (%rdi), %xmm0 # x = *p
addsd %xmm0, %xmm1 # t = x + v
movsd %xmm1, (%rdi) # *p = t
ret

## Slide 67: Other Aspects of FP Code
Lots of instructions
  Different operations, different formats, ...
Floating-point comparisons
  Instructions ucomiss and ucomisd
  Set condition codes CF, ZF, and PF
Using constant values
  Set XMM0 register to 0 with instruction xorpd %xmm0, %xmm0
  Others loaded from memory