## Slide 1
14-513
18-613

## Slide 3: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 4: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 5: Memory Mountain Test Function
long data[MAXELEMS]; /* Global array to traverse */
/* test - Iterate over first "elems" elements of
* array "data" with stride of "stride“,
* using 4x4 loop unrolling.
*/
int test(int elems, int stride) {
long i, sx2=stride*2, sx3=stride*3, sx4=stride*4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems, limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+stride];
acc2 = acc2 + data[i+sx2];
acc3 = acc3 + data[i+sx3];
}
/* Finish any remaining elements */
for (; i < length; i++) {
acc0 = acc0 + data[i];
}
return ((acc0 + acc1) + (acc2 + acc3));
}
Call test() with many combinations of elems
and stride.
For each elems and stride:
1. Call test() once to warm up the caches.
2. Call test() again and measure the read throughput(MB/s)
mountain/mountain.c

## Slide 6: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Notes: Slopes of spatial locality – increase stride, degrade throughput because burn through blocks faster
Ridges of temporal – As increase size, can’t fit in level of cache any more, drop to next one down. Data in cache because of warm up before test run.
Prefetching – do better than we expect.

## Slide 7: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 8: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  Matrix elements are doubles (8 bytes)
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
matmult/mm.c

## Slide 9: Miss Rate Analysis for Matrix Multiply
Assume:
  Block size = 32B (big enough for four doubles)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x

## Slide 10: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > sizeof(aij) bytes, exploit spatial locality
    miss rate = sizeof(aij) / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    miss rate = 1 (i.e. 100%)

## Slide 11: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.25 1.0 0.0
matmult/mm.c
Block size = 32B (four doubles)

## Slide 12: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.0
matmult/mm.c
Block size = 32B (four doubles)
0.25
0.25

## Slide 13: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Miss rate for inner loop iterations:
  A B C
  0.0
matmult/mm.c
Block size = 32B (four doubles)
1.0
1.0

## Slide 14: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  avg misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  avg misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  avg misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 15: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700
jki | 4.8 | 4.68 | 4.65 | 4.8 | 6.84 | 15.03 | 22.78 | 29.39 | 40.39 | 57.06 | 60.54 | 63.33 | 65.61 | 67.49
kji | 4.83 | 4.72 | 4.64 | 4.69 | 6.83 | 15.1 | 22.68 | 29.18 | 40.26 | 57.02 | 60.53 | 63.34 | 65.62 | 67.53
ijk | 3.75 | 4.08 | 4.33 | 4.45 | 4.45 | 4.45 | 4.45 | 4.47 | 7.73 | 18.77 | 20.36 | 21.67 | 22.76 | 23.71
jik | 3.93 | 4.14 | 4.36 | 4.47 | 4.52 | 4.56 | 4.57 | 4.6 | 7.96 | 19.05 | 20.59 | 21.86 | 22.92 | 23.82
kij | 1.86 | 1.78 | 2.14 | 2.3 | 2.23 | 2.18 | 2.14 | 2.12 | 2.12 | 2.13 | 2.13 | 2.14 | 2.16 | 2.22
ikj | 1.78 | 1.8 | 2.12 | 2.03 | 1.96 | 1.92 | 1.89 | 1.86 | 1.86 | 1.88 | 1.89 | 1.9 | 1.91 | 1.95
ijk / jik (1.25)
jki / kji (2.0)
kij / ikj (0.5)
Cycles per inner loop iteration

## Slide 16: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 17: Example: Matrix Multiplication
a
b
i
j
x
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n + j] += a[i*n + k] * b[k*n + j];
}

## Slide 18: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache line = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
x
=
n
x
=
8 wide
Notes: n/8 – comes from taking n and doing it in chunks of 8 that fit in a cache line, with perfect stride 1 accesses across the row
N – comes from missing on everything but the 1 double needed going down a column

## Slide 19: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache line = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 n2 = (9/8) n3
n
x
=
8 wide

## Slide 20: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=L)
for (j = 0; j < n; j+=L)
for (k = 0; k < n; k+=L)
/* L x L mini matrix multiplications */
for (i1 = i; i1 < i+L; i1++)
for (j1 = j; j1 < j+L; j1++)
for (k1 = k; k1 < k+L; k1++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
x
c
=
c
+
Block size L x L
matmult/bmm.c

## Slide 21: Cache Miss Analysis
Assume:
  Cache line = 8 doubles. Blocking size L ≥ 8
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3L2 < C
First (block) iteration:
  Misses per block: L2/8
  Blocks per Iteration: 2n/L
  (omitting matrix c)
  Misses per Iteration:
  2n/L x L2/8 = nL/4
  Afterwards in cache (schematic)
x
=
x
=
Block size L x L
n/L blocks
Notes: 2n/L comes from doing n/L blocks of size L^2 in each source matrix
L^2 / 8 comes from taking L^2 bytes per block and perfectly caching them 8 doubles at a time.

## Slide 22: Cache Miss Analysis
Assume:
  Cache line = 8 doubles. Blocking size L ≥ 8
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3L2 < C
Second (block) iteration:
  Same misses as
  first iteration
  2n/L x L2/8 = nL/4
Total misses:
  nL/4 misses per iteration x (n/L)2 iterations = n3/(4L) misses
x
=
Block size L x L
n/L blocks
Notes: n/L is the dimension of the matrix in blocks. (n/L)^2 is the number of iterations.
nL/4 is the misses per iteration. N^3/4L is the total miss count.

## Slide 23: Blocking Summary
No blocking: (9/8) n3 misses
Blocking: (1/(4L)) n3 misses
Use largest block size L, such that L satisfies 3L2 < C
  Fit three blocks in cache! Two input, one output.
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly
Notes: 3L^2 to accommodate M3 = M1 x M2, with M1,2,3 all supplying blocks of dim L^2

## Slide 24: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!
  Focus on the inner loops, where bulk of computations and memory accesses occur.
  Try to maximize spatial locality by reading data objects sequentially with stride 1.
  Try to maximize temporal locality by using a data object as often as possible once it’s read from memory.

## Slide 25: Supplemental slides

## Slide 26: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
128m | 16636 | 8966 | 5846 | 4298 | 3403 | 2789 | 2348 | 2055 | 1904 | 1786 | 1693 | 1607
64m | 16925 | 9080 | 5860 | 4307 | 3408 | 2795 | 2352 | 2058 | 1912 | 1791 | 1695 | 1608
32m | 17168 | 9212 | 5897 | 4331 | 3431 | 2822 | 2375 | 2078 | 1924 | 1809 | 1713 | 1628
16m | 17405 | 9559 | 6027 | 4458 | 3520 | 2899 | 2465 | 2179 | 2049 | 1952 | 1883 | 1825
8m | 19339 | 11837 | 8045 | 6079 | 4927 | 4246 | 3745 | 3289 | 3131 | 3026 | 2899 | 2924
4m | 20728 | 16852 | 13212 | 10371 | 8542 | 7259 | 6345 | 5627 | 5396 | 5228 | 5090 | 4977
2m | 29025 | 19350 | 13735 | 10550 | 8610 | 7308 | 6361 | 5648 | 5417 | 5241 | 5094 | 4978
1024k | 29291 | 19543 | 13689 | 10508 | 8597 | 7281 | 6354 | 5628 | 5388 | 5218 | 5071 | 4956
512k | 29290 | 19411 | 13779 | 10594 | 8667 | 7390 | 6438 | 5684 | 5453 | 5325 | 5213 | 5128
256k | 29762 | 21456 | 16905 | 13504 | 11044 | 9359 | 8175 | 7240 | 7082 | 6889 | 6858 | 6835
128k | 30042 | 23953 | 22661 | 18952 | 15706 | 13602 | 11761 | 10409 | 10184 | 10137 | 10158 | 9875
64k | 29468 | 23044 | 21501 | 19208 | 15955 | 13551 | 11784 | 10516 | 10364 | 10320 | 10262 | 10132
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Core i5 Haswell
3.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size

## Slide 27: Cache Capacity Effects from Memory Mountain
Chart: Working set size (bytes)
| 128m | 64m | 32m | 16m | 8m | 4m | 2m | 1024k | 512k | 256k | 128k | 64k | 32k | 16k
s8 | 2055 | 2058 | 2078 | 2179 | 3289 | 5627 | 5648 | 5628 | 5684 | 7240 | 10409 | 10516 | 26110 | 27746
Core i7 Haswell
3.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slice through memory mountain with stride=8
L1
L2
L3
Main Memory

## Slide 28: Cache Block Size Effects from Memory Mountain
Chart: Throughput for size = 128K
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
Measured | 30896 | 25024 | 24135 | 20391 | 17199 | 14634 | 12670 | 11274 | 11248 | 11262 | 11294 | 11251
Core i7 Haswell
2.26 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Miss rate = s/8
Miss rate = 1.0
Stride s

## Slide 29: Modeling Block Size Effects from Memory Mountain
Chart: Throughput for size = 128K
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
Measured | 30896 | 25024 | 24135 | 20391 | 17199 | 14634 | 12670 | 11274 | 11248 | 11262 | 11294 | 11251
Model | 30896 | 24743.7642 | 20634.8109 | 17696.1805 | 15490.2007 | 13773.2479 | 12398.9348 | 11274 | 11274 | 11274 | 11274 | 11274
Core i7 Haswell
2.26 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Stride s

## Slide 30: 2008 Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12
128m | 5427 | 2757 | 1939 | 1455 | 1151 | 951 | 803 | 701 | 672 | 646 | 626 | 610
64m | 5496 | 2760 | 1936 | 1459 | 1149 | 949 | 803 | 703 | 666 | 644 | 621 | 610
32m | 5498 | 2758 | 1938 | 1454 | 1151 | 934 | 811 | 704 | 671 | 645 | 625 | 611
16m | 5506 | 2769 | 1941 | 1460 | 1153 | 953 | 811 | 705 | 672 | 646 | 626 | 614
8m | 5657 | 2977 | 2090 | 1586 | 1251 | 1035 | 882 | 766 | 777 | 836 | 1018 | 1365
4m | 10401 | 8422 | 7522 | 6468 | 5469 | 4809 | 4284 | 3894 | 3900 | 3899 | 3898 | 3897
2m | 10401 | 8418 | 7517 | 6468 | 5465 | 4804 | 4284 | 3898 | 3896 | 3897 | 3893 | 3897
1024k | 10479 | 8469 | 7578 | 6508 | 5510 | 4854 | 4326 | 3935 | 3939 | 3945 | 3951 | 3963
512k | 10486 | 8465 | 7578 | 6508 | 5514 | 4854 | 4330 | 3938 | 3945 | 3952 | 3956 | 3969
256k | 10479 | 8456 | 7578 | 6503 | 5510 | 4850 | 4322 | 3931 | 3935 | 3938 | 3944 | 3958
128k | 10473 | 8443 | 7552 | 6488 | 5496 | 4833 | 4307 | 3920 | 3912 | 3922 | 3923 | 3938
64k | 10460 | 8414 | 7537 | 6463 | 5474 | 4817 | 4295 | 3902 | 3897 | 3899 | 3893 | 3905
No prefetching
Core 2 Duo
2.4 GHz
32 KB L1 d-cache
6MB L2 cache
64 B block size

## Slide 31: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c
Block size = 32B (four doubles)

## Slide 32: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c
Block size = 32B (four doubles)

## Slide 33: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c
Block size = 32B (four doubles)

## Slide 34: Cache and Memory Wrap-Up 15-213/18-213/15-513/18-613: Introduction to Computer Systems 16 March 2021

## Slide 35: Design and Debugging 15-213/18-213/15-513/18-613: Introduction to Computer Systems 16 March 2021

## Slide 36: After this lecture
You will be able to:
  Describe the steps to debug complex code failures
  Identify ways to manage the complexity when programming
  State guidelines for communicating the intention of the code

## Slide 37: Outline
Debugging
  Defects and Failures
  Scientific Debugging
  Tools
Design
  Managing complexity
  Communication
  Naming
  Comments

## Slide 38: Defects and Infections
1. The programmer creates a defect
2. The defect causes an infection
3. The infection propagates
4. The infection causes a failure

## Slide 39: Curse of Debugging
Not every defect causes a failure!
Testing can only show the presence of errors – not their absence. (Dijkstra 1972)

## Slide 40: Defects to Failures
Code with defects will introduce erroneous or “infected” state
  Correct code may propagate this state
  Eventually an erroneous state is observed
Some executions will not trigger the defect
  Others will not propagate “infected” state
Debugging sifts through the code to find the defect

## Slide 41: Explicit Debugging
Stating the problem
  Describe the problem aloud or in writing
    A.k.a. “Rubber duck” or “teddy bear” method
  Often a comprehensive problem description is sufficient to solve the failure
Notes: Explain the problem to your teddy bear

## Slide 42: Scientific Debugging
Hypothesis
Problem Description
Code
Failing Runs
Other Runs
Before debugging, you need to construct a hypothesis as to the defect
  Propose a possible defect and why it explains the failure conditions
Ockham’s Razor – given several hypotheses, pick the simplest / closest to current work

## Slide 43: Scientific Debugging
Prediction
Observation & Conclusion
Hypothesis
Experiment
Make predictions based on your hypothesis
  What do you expect to happen under new conditions
  What data could confirm or refute your hypothesis
How can I collect that data?
  What experiments?
  What collection mechanism?
Does the data refute the hypothesis?
  Refine the hypothesis based on the new inputs

## Slide 44: Scientific Debugging
Conclusion
Diagnosis
Fix
Confirm
A set of experiments has confirmed the hypothesis
  This is the diagnosis of the defect
Develop a fix for the defect
Run experiments to confirm the fix
  Otherwise, how do you know that it is fixed?

## Slide 45: Code with a Bug
int fib(int n)
{
int f, f0 = 1, f1 = 1;
while (n > 1) {
n = n - 1;
f = f0 + f1;
f0 = f1;
f1 = f;
}
return f;
} int main(..) { .. for (i = 9; i > 0; i--) printf(“fib(%d)=%d\n”, i, fib(i));
$ gcc -o fib fib.c fib(9)=55 fib(8)=34 ... fib(2)=2 fib(1)=134513905
A defect has caused a failure.
Notes: Simple example to illustrate techniques.
Students do not need to know the code or find the bug.

## Slide 46: Constructing a Hypothesis
Specification defined the first Fibonacci number as 1
  We have observed working runs (e.g., fib(2))
  We have observed a failing run
  We then read the code
fib(1) failed // Hypothesis
Code | Hypothesis
for (i = 9; …) | Result depends on order of calls
while (n > 1) { | Loop check is incorrect
int f; | f is uninitialized
Notes: What is the input to the hypothesis?
Propose three possible hypotheses from the code.

## Slide 47: Prediction
Propose a new condition or conditions
  What will logically happen if your hypothesis is correct?
  What data can be
fib(1) failed // Hypothesis
  // Result depends on order of calls
    If fib(1) is called first, it will return correctly.
  // Loop check is incorrect
    Change to n >= 1 and run again.
  // f is uninitialized
    Change to int f = 1;

## Slide 48: Experiment
Identical to the conditions of a prior run
  Except with one condition changed
Conditions
  Program input, using a debugger, altering the code
fib(1) failed // Hypothesis
  If fib(1) is called first, it will return correctly.
    Fails.
  Change to n >= 1
    fib(1)=2
    fib(0)=...
  Change to int f = 1;
    Works. Sometimes a prediction can be a fix.

## Slide 49: Observation
What is the observed result?
  Factual observation, such as “Calling fib(1) will return 1.”
  The conclusion will interpret the observation(s)
Don’t interfere.
  printf() can interfere
  Like quantum physics, sometimes observations are part of the experiment
Proceed systematically.
  Update the conditions incrementally so each observation relates to a specific change

## Slide 50: Debugging Tools
Observing program state can require a variety of tools
  Debugger (e.g., gdb)
    What state is in local / global variables (if known)
    What path through the program was taken
  Valgrind
    Does execution depend on uninitialized variables
    Are memory accesses ever out-of-bounds
Notes: Image: https://thumbs.dreamstime.com/m/sherlock-holmes-cartoon-vector-14725610.jpg (from a search for pubic domain images)

## Slide 51: Diagnosis
A scientific hypothesis that explains current observations and makes future predictions becomes a theory
  We’ll call this a diagnosis
Use the diagnosis to develop a fix for the defect
  Avoid “post hoc, ergo propter hoc” fallacy
    Latin for: “After this, therefore because of this”
  Or correlation does not imply causation
Understand why the defect and fix relate
Once there was a program that only worked on Wednesday…
Notes: Fallacy commonly seen in malloc lab. If I add a printf to this code, then it works at –O3. Actual problem is that there is undefined behavior and the printf function call reduced the optimization space.
Story: “Once there was a program that only worked on Wednesday. The spec had declared that days are at most 8 characters long. Wednesday is 9 (+ NULL). The NULL was initializing another field so the program would only then operate correctly.”

## Slide 52: Fix and Confirm
Confirm that the fix resolves the failure
If you fix multiple perceived defects, which fix was for the failure?
  Be systematic

## Slide 53: Learn
Common failures and insights
  Why did the code fail?
  What are my common defects?
Assertions and invariants
  Add checks for expected behavior
  Extend checks to detect the fixed failure
Testing
  Every successful set of conditions is added to the test suite
Notes: - Prof Railing says, “I don’t use certain C syntax in my code as I know I am prone to errors if I do.”
- Are there internal conditions to check for (invariants)? External (tests)?

## Slide 54: Quick and Dirty
Not every problem needs scientific debugging
  Set a time limit: (for example)
    0 – 10 minutes – Informal Debugging
    10 – 60 minutes – Scientific Debugging
    > 60 minutes – Take a break / Ask for help

## Slide 55: Code Smells
Use of uninitialized variables
Unused values
Unreachable code
Duplicated code
Bloated functions/methods
Memory leaks
Interface misuse
Null pointers
Etc
Common ways in which code is likely to have bugs,
either already or in the future
Notes: Common bugs, many of which can be detected by compilers or existing tools.

## Slide 56: Quiz Time!
Check out:
https://canvas.cmu.edu/courses/10968

## Slide 57: Outline
Debugging
  Defects and Failures
  Scientific Debugging
  Tools
Design
  Managing complexity
  Communication
  Naming
  Comments

## Slide 58: Design
A good design needs to achieve many things:
  Performance
  Availability
  Modifiability, portability
  Scalability
  Security
  Testability
  Usability
  Cost to build, cost to operate
Notes: From these many objectives, we will summarize into two points.

## Slide 59: Design
Good Design does:
Complexity Management &
Communication
Notes: If a design does these things and solves the problem, then it can also achieve (or be extended to achieve) the other objectives

## Slide 60: Complexity
There are well known limits to how much complexity a human can manage easily.

## Slide 61: Complexity Management
However, patterns can be very helpful...

## Slide 62: Complexity Management
Many techniques have been developed to help manage complexity:
Separation of concerns
Modularity
Reusability
Extensibility
DRY
Abstraction
Information Hiding
...
Notes: This is a lot and the list is beyond the scope of the course. Next slide is the 200-level suggestion(s)
DRY=Don’t Repeat Yourself. The DRY principle is stated as, "Every piece of knowledge or logic must have a single, unambiguous representation within a system.”

## Slide 63: Managing Complexity
Given the many ways to manage complexity
  Design code to be testable
  Try to reuse testable chunks
Notes: To start managing complexity, split

## Slide 64: Complexity Example
Split a cache access into three+ testable components
  State all of the steps that a cache access requires
  Convert address into tag, set index, block offset
  Look up the set using the set index
  Check if the tag matches any line in the set
  If so, hit
  If not a match, miss, then
  Find the LRU block
  Evict the LRU block
  Read in the new line from memory
  Update LRU
  Update dirty if the access was a store
  Which steps depend on the operation being a load or a store?
Notes: I would have students talk to their neighbors for a few minutes about these steps

## Slide 65: Complexity Example
Split a cache access into three+ testable components
  State all of the steps that a cache access requires
  Convert address into tag, set index, block offset
  Look up the set using the set index
  Check if the tag matches any line in the set
  If so, hit
  If not a match, miss, then
  Find the LRU block
  Evict the LRU block
  Read in the new line from memory
  Update LRU
  Update dirty if the access was a store
  Which steps depend on the operation being a load or a store?
Notes: I would have students talk to their neighbors for a few minutes about these steps
Convert address can also be multiple steps
This is just one example sequence

## Slide 66: Designs need to be testable
Testable design
  Testing versus Contracts
  These are complementary techniques
Testing and Contracts are
  Acts of design more than verification
  Acts of documentation
Notes: Design by contract, also known as contract programming, programming by contract and design-by-contract programming, is an approach for designing software. It prescribes that software designers should define formal, precise and verifiable interface specifications for software components, which extend the ordinary definition of abstract data types with preconditions, postconditions and invariants. These specifications are referred to as "contracts", in accordance with a conceptual metaphor with the conditions and obligations of business contracts.

## Slide 67: Testing Example
For your cache simulator, you can write your own traces
  Write a trace to test for a cache hit
  L 50, 1 L 50, 1
  Write a trace to test dirty bytes in cache
  S 100, 1

## Slide 68: Communication
When writing code, the author is communicating with:
The machine
Other developers of the system
Code reviewers
Their future self
Notes: We communicate with different audiences.

## Slide 69: Communication
There are many techniques that have been developed around code communication:
Tests
Naming
Comments
Commit Messages
Code Review
Design Patterns
...
Notes: We communicate through many means

## Slide 70
Naming

## Slide 71: Avoid deliberately meaningless names:

## Slide 72: Naming is understanding
“If you don’t know what a thing should be called, you cannot know what it is.
If you don’t know what it is, you cannot sit down and write the code.” - Sam Gardiner

## Slide 73: Better naming practices
Start with meaning and intention
Use words with precise meanings (avoid “data”, “info”, “perform”)
Prefer fewer words in names
Avoid abbreviations in names
Use code review to improve names
Read the code out loud to check that it sounds okay
Actually rename things
Notes: Yes, the 213 course-staff is guilty of transgressing many of these suggestions

## Slide 74: Naming guidelines – Use dictionary words
Only use dictionary words and abbreviations that appear in a dictionary.
  For example: FileCpy -> FileCopy
  Avoid vague abbreviations such as acc, mod, auth, etc..

## Slide 75: Avoid using single-letter names
Single letters are unsearchable
  Give no hints as to the variable’s usage
Exceptions are loop counters
  Especially if you know why i, j, etc were originally used
Notes: See https://en.wikibooks.org/wiki/Fortran/Fortran_variables

## Slide 76: Limit name character length
“Good naming limits individual name length, and reduces the need for specialized vocabulary” – Philip Relf

## Slide 77: Limit name word count
Keep names to a four word maximum
Limit names to the number of words that people can read at a glance.
Which of each pair do you prefer?
a1) arraysOfSetsOfLinesOfBlocks
a2) cache
b1) evictedData
b2) evictedDataBytes
Notes: Bpr: “My friend wrote the following line in C++. This data structure tracked the coherence state in a simulator. I still wonder if he could have done better
map<uint, map<ContextId, map<ContextId, map<uint, uint> > > > theDataStructureWhichShallNotBeNamed;”

## Slide 78: Describe Meaning
Use descriptive names.
Avoid names with no meaning: a, foo, blah, tmp, etc
There are reasonable exceptions:
void swap(int* a, int* b) {
int tmp = *a;
*a = *b;
*b = tmp;
}
Notes: Tmp is fine when it really is short-lived and temporary.

## Slide 79: Use a large vocabulary
Be more specific when possible:
  Person -> Employee
What is size in this binaryTree?
struct binaryTree {
int size;
…
};
Notes: Discuss size. Could be height of tree, number of nodes, memory usage, etc.

## Slide 80: Use problem domain terms
Use the correct term in the problem domain’s language.
  Hint: as a student, consider the terms in the assignment
In cachelab, consider the following:
line
element

## Slide 81: Use opposites precisely
Consistently use opposites in standard pairs
  first/end -> first/last

## Slide 82
Comments

## Slide 83: Don’t Comments
Don’t say what the code does
  because the code already says that
Don’t explain awkward logic
  improve the code to make it clear
Don’t add too many comments
  it’s messy, and they get out of date

## Slide 84: Awkward Code
Imagine someone (TA, employer, etc) has to read your code
  Would you rather rewrite or comment the following?
  How about?
  Both lines update program state in the same way.
(*(void **)((*(void **)(bp)) + DSIZE)) = (*(void **)(bp + DSIZE));
bp->prev->next = bp->next;
Notes: Old malloc example, published in SIGCSE by Railing and Bryant.

## Slide 85: Do Comments
Answer the question: why the code exists
When should I use this code?
When shouldn’t I use it?
What are the alternatives to this code?

## Slide 86: Why does this exist?
Explain why a magic number is what it is.
When should this code be used? Is there an alternative?
// Each address is 64-bit, which is 16 + 1 hex characters
const int MAX_ADDRESS_LENGTH = 17;
unsigned power2(unsigned base, unsigned expo){
unsigned i;
unsigned result = 1;
for(i=0;i<expo;i++){
result+=result;
}
return result;
}
Notes: The power2 code is from a student’s submission.

## Slide 87: How to write good comments
Write short comments of what the code will do.
  Single line comments
  Example: Write four one-line comments for quick sort
// Initialize locals
// Pick a pivot value
// Reorder array around the pivot
// Recurse
Notes: Students are notorious for writing comments last, so emphasize that brief comments of the design comes before implementation.

## Slide 88: How to write good comments
Write short comments of what the code will do.
  Single line comments
  Example: Write four one-line comments for quick sort
Write that code.
Revise comments / code
  If the code or comments are awkward or complex
  Join / Split comments as needed
Maintain code and comments

## Slide 89: How to write good comments
Try to write good code first
Try to write a one-sentence comment
Refactor the code until the comment is easy to write
Now write a good comment
Maintain your code AND your comments
Notes: Original good comment strategy

## Slide 90: Commit Messages
Committing code to a source repository is a vital part of development
  Protects against system failures and typos:
    cat foo.c versus cat > foo.c
  The commit messages are your record of your work
    Communicating to your future self
    Describe in one line what you did
  “Parses command line arguments”
  “fix bug in unique tests, race condition not solved”
  “seg list finished, performance is …”
Notes: The cat example will silently truncate the file to be empty.

## Slide 91: Summary
Programs have defects
  Be systematic about finding them
Programs are more complex than humans can manage
  Write code to be manageable
Programming is not solitary, even if you are communicating with a grader or a future self
  Be understandable in your communication

## Slide 92: Acknowledgements
Some debugging content derived from:
  http://www.whyprogramsfail.com/slides.php
Some code examples for design are based on:
  “The Art of Readable Code”. Boswell and Foucher. 2011.
Lecture originally written by
  Michael Hilton and Brian Railing