## Slide 1
14-513
18-613

## Slide 2: Machine-Level Programming II: Control 15-213/15-513: Introduction to Computer Systems 4th Lecture, Jan 25, 2024
Carnegie Mellon

## Slide 3: Announcements
Written 1 out yesterday, due Wed 1/24
GDB & Debugging Bootcamp this Sun 1/28
  Watch for Piazza posting on the details
Lab 1 (datalab) due Fri 2/1
Lab 2 (bomblab) out today, due Thurs 2/8
  Turns in automatically via Autolab

## Slide 4: Recall: Machine Instructions
C
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Machine
  3 bytes at address 0x40059e
  Compact representation of the assembly instruction
  (Relatively) easy for hardware to interpret
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 5: Recall: Move & Arithmetic Operations
Some Two Operand Instructions:
  Format Computation
    movq Src,Dest
    leaq Src,Dest
    addq Src,Dest
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src Also called shlq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Dest = Src (Src can be $const)
Dest = address computed by expression Src
Dest = Dest + Src

## Slide 6: Recall: Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8

## Slide 7: Which numbers are pointers?
They aren’t labeled
You have to figure it out from context
(gdb) info registers
rax 0x40057d 4195709
rbx 0x0 0
rcx 0x4005e0 4195808
rdx 0x7fffffffdc28 140737488346152
rsi 0x7fffffffdc18 140737488346136
rdi 0x1 1
rbp 0x0 0x0
rsp 0x7fffffffdb38 0x7fffffffdb38
r8 0x7ffff7dd5e80 140737351868032
r9 0x0 0
r10 0x7fffffffd7c0 140737488345024
r11 0x7ffff7a2f460 140737348039776
r12 0x400490 4195472
r13 0x7fffffffdc10 140737488346128
r14 0x0 0
r15 0x0 0
rip 0x40057d 0x40057d
Notes: Several people asked this question last time.
The registers don’t have any “this is a pointer” label, just like they don’t have any “this is signed” label. You have to figure it out from context.

## Slide 8: Which numbers are pointers?
They aren’t labeled
You have to figure it out from context
%rsp and %rip always hold pointers
  Register values that are “close” to %rsp or %rip are probably also pointers
(gdb) info registers
rax 0x40057d 4195709
rbx 0x0 0
rcx 0x4005e0 4195808
rdx 0x7fffffffdc28 140737488346152
rsi 0x7fffffffdc18 140737488346136
rdi 0x1 1
rbp 0x0 0x0
rsp 0x7fffffffdb38 0x7fffffffdb38
r8 0x7ffff7dd5e80 140737351868032
r9 0x0 0
r10 0x7fffffffd7c0 140737488345024
r11 0x7ffff7a2f460 140737348039776
r12 0x400490 4195472
r13 0x7fffffffdc10 140737488346128
r14 0x0 0
r15 0x0 0
rip 0x40057d 0x40057d
Notes: How close is close? Hard to say. I’m pretty sure the values in r8 and r11 here are too far away from rsp to be a pointer, but I could be wrong. Actually, my educated guess is that they are pointers, but pointers into a different part of memory than the one rsp and rsi and rdx and r13 are pointing into.

## Slide 9: Which numbers are pointers?
If a register is being used as a pointer…
Dump of assembler code for function main:
=> 0x40057d <+0>: sub $0x8,%rsp
0x400581 <+4>: mov (%rsi),%rsi
0x400584 <+7>: mov $0x400670,%edi
0x400589 <+12>: mov $0x0,%eax
0x40058e <+17>: call 0x400460

## Slide 10: Which numbers are pointers?
If a register is being used as a pointer…
  mov (%rsi), %rsi
  …Then its value is expected to be a pointer.
    There might be a bug that makes its value incorrect.
Not as obvious with complicated address “modes”
  (%rsi, %rbx) – One of these is a pointer, we don’t know which.
  (%rsi, %rbx, 2) – %rsi is a pointer, %rbx isn’t (why?)
  0x400570(, %rbx, 2) – 0x400570 is a pointer, %rbx isn’t (why?)
  lea (anything), %rax – (anything) may or may not be a pointer
Dump of assembler code for function main:
=> 0x40057d <+0>: sub $0x8,%rsp
0x400581 <+4>: mov (%rsi),%rsi
0x400584 <+7>: mov $0x400670,%edi
0x400589 <+12>: mov $0x0,%eax
0x40058e <+17>: call 0x400460

## Slide 11: Today
Control: Condition codes CSAPP 3.6.1 - 3.6.2
Conditional branches CSAPP 3.6.3 - 3.6.6
Loops CSAPP 3.6.7
Switch Statements CSAPP 3.6.8

## Slide 12: Control flow
extern void op1(void);
extern void op2(void);
void decision(int x) {
if (x) {
op1();
} else {
op2();
}
}
decision
x != 0
op2
op1
return
Yes
No

## Slide 13: Control flow in assembly language
extern void op1(void);
extern void op2(void);
void decision(int x) {
if (x) {
op1();
} else {
op2();
}
}
decision:
subq $8, %rsp
testl %edi, %edi
je .L2
call op1
jmp .L1
.L2:
call op2
.L1:
addq $8, %rsp
ret
It’s all done with GOTO!

## Slide 14: Processor State (x86-64, Partial)
Information about currently executing program
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
  Location of current code control point ( %rip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%rip
Registers
Current stack top
Instruction pointer
CF
ZF
SF
OF
Condition codes
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 15: Condition Codes (Implicit Setting)
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
  GDB prints these as one “eflags” register eflags 0x246 [ PF ZF IF ] Z set, CSO clear
Implicitly set (as side effect) of arithmetic operations
  Example: addq Src,Dest ↔ t = a+b
  CF set if carry out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by lea instructions
Notes: You can ignore PF, IF, and any other things that show up in the square brackets that you haven’t heard of. They’re processor state bits that you don’t have to care about unless you’re coding the OS kernel.

## Slide 16: ZF set when
000000000000…00000000000

## Slide 17: SF set when
1xxxxxxxxxxx…xxxxxxxxxxx

## Slide 18: CF set when
1xxxxxxxxxxxx...
1xxxxxxxxxxxx...
+
xxxxxxxxxxxxx...
1
For unsigned arithmetic, this reports overflow
0xxxxxxxxxxxx...
1xxxxxxxxxxxx...
_
1xxxxxxxxxxxx...
1
Carry
Borrow

## Slide 19: OF set when
yxxxxxxxxxxxx...
yxxxxxxxxxxxx...
+
zxxxxxxxxxxxx...
z = ~y
For signed arithmetic, this reports overflow
  (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
a
b
t
yxxxxxxxxxxxx...
zxxxxxxxxxxxx...
_
zxxxxxxxxxxxx...
  (a>0 && b<0 && t<0) || (a<0 && b>0 && t>0)
a
b
t
Positive
Overflow
Negative
Overflow

## Slide 20: Compare Instruction
cmp a, b
  Computes (just like sub)
  Sets condition codes based on result, but…
  Does not change
  Used for if (a < b) { … } whenever isn’t needed for anything else

## Slide 21: Test Instruction
test a, b
  Computes (just like and)
  Sets condition codes (only SF and ZF) based on result, but…
  Does not change
  Most common use: test %rX, %rX to compare %rX to zero
  Second most common use: test %rX, %rY tests if any of the 1-bits in %rY are also 1 in %rX (or vice versa)

## Slide 22: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 23: Jumping
jX Instructions
  Jump to different part of code depending on condition codes
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 24: Reading Condition Codes
SetX Instructions
  Set low-order byte of destination to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 25: x86-64 Integer Registers
%rsp
  SetX argument is always a low byte (%al, %r8b, etc.)
%al
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 26: Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %rax
ret
SetX Instructions:
  Set single byte based on combination of condition codes
One of addressable byte registers
  Does not alter remaining bytes
  Typically use movzbl to finish job
    32-bit instructions also set upper 32 bits to 0
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 27: Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %rax
ret
SetX Instructions:
  Set single byte based on combination of condition codes
One of addressable byte registers
  Does not alter remaining bytes
  Typically use movzbl to finish job
    32-bit instructions also set upper 32 bits to 0
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
Beware weirdness movzbl (and others)
movzbl %al, %eax
%eax
%al
%rax
0x000000
%al
%rax
0x00000000
0x000000
%al
Zapped to all 0’s

## Slide 28: Activity Time!
To obtain a copy of today’s activity, log into a shark machine and do the following:
$ wget http://www.cs.cmu.edu/~213/activities/machine-control.tar
$ tar xf machine-control.tar
$ cd machine-control
Do (only) “3 Basic Control Flow”, problems 1, 2, and 3

## Slide 29: Conditional Branch Example (Old Style)
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
absdiff:
cmpq %rsi, %rdi # x:y
jle .L4
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
Generation
  shark> gcc –Og -S –fno-if-conversion control.c
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
I’ll get to this shortly.

## Slide 30: Expressing with Goto Code
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
C allows goto statement
Jump to position designated by label
long absdiff_j
(long x, long y)
{
long result;
int ntest = (x <= y);
if (ntest) goto Else;
result = x-y;
goto Done;
Else:
result = y-x;
Done:
return result;
}

## Slide 31: General Conditional Expression Translation (Using Branches)
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
ntest = !Test;
if (ntest) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 32: Using Conditional Moves
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
result = Then_Expr;
eval = Else_Expr;
nt = !Test;
if (nt) result = eval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest ← Src
  Supported in post-1995 x86 processors
  GCC tries to use them
    But, only when known to be safe
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional moves do not require control transfer

## Slide 33: Conditional Move Example
absdiff:
movq %rdi, %rax # x
subq %rsi, %rax # result = x-y
movq %rsi, %rdx
subq %rdi, %rdx # eval = y-x
cmpq %rsi, %rdi # x:y
cmovle %rdx, %rax # if <=, result = eval
ret
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
When is
this bad?

## Slide 34: Bad Cases for Conditional Move
Expensive Computations
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;
Bad Performance
Unsafe
Illegal

## Slide 35: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 36: “Do-While” Loop Example
C Code
long pcount_do
(unsigned long x) {
long result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 37: “Do-While” Loop Compilation
Goto Version
movl $0, %eax # result = 0
.L2: # loop:
movq %rdi, %rdx
andl $1, %edx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi # x >>= 1
jne .L2 # if (x) goto loop
rep; ret
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Register | Use(s)
%rdi | Argument x
%rax | result

## Slide 38: Quiz Time!
Canvas Quiz: Day 4 - Machine Control

## Slide 39: General “Do-While” Translation
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 40: General “While” Translation #1
While version
while (Test)
Body
“Jump-to-middle” translation
Used with -Og
Goto Version
goto test;
loop:
Body
test:
if (Test)
goto loop;
done:

## Slide 41: While Loop Example #1
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Jump to Middle Version
long pcount_goto_jtm
(unsigned long x) {
long result = 0;
goto test;
loop:
result += x & 0x1;
x >>= 1;
test:
if(x) goto loop;
return result;
}
Compare to do-while version of function
Initial goto starts loop at test

## Slide 42: General “While” Translation #2
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
“Do-while” conversion
Used with –O1
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 43: While Loop Example #2
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Do-While Version
long pcount_goto_dw
(unsigned long x) {
long result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
done:
return result;
}
Compare to do-while version of function
Initial conditional guards entrance to loop

## Slide 44: “For” Loop  Do-While Loop
For version
Do-While Version
if (!Test)
goto done;
do {
Body
Update
} while(Test);
done:
Goto Version
if (!Test)
goto done;
loop:
Body
Update
if (Test)
goto loop;
done:
for (Init; Test; Update )
Body
Initial test can often be optimized away – why?
Notes: Can optimize initial test away when Test is known to be true first time because of initial condition Init. E.g., for(i=0, i < 8; i++)

## Slide 45: “For” Loop Do-While Conversion
C Code
Initial test can be optimized away
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
Goto Version
long pcount_for_goto_dw
(unsigned long x) {
size_t i;
long result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test

## Slide 46: Activity Time!
Do “6 Loops”, problems 15, 16, and 17

## Slide 47: Today
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 48: Switch Statement Example
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 49: Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
goto *JTab[x];
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Translation (Extended C)
Jump Table
Jump Targets

## Slide 50: Switch Statement Example
long my_switch
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
.L3:
.L5:
.L9:
.L7:
.L8:
my_switch:
cmpq $6, %rdi # x:6
ja .L8 # if x > 6 jump # to default
jmp *.L4(,%rdi,8)

## Slide 51: Assembly Setup Explanation
Table Structure
  Each target requires 8 bytes
  Base address at .L4
Jumping
  Direct: jmp .L8
  Jump target is denoted by label .L8
  Indirect: jmp *.L4(,%rdi,8)
  Start of jump table: .L4
  Must scale by factor of 8 (addresses are 8 bytes)
  Fetch target from effective Address .L4 + x*8
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 52: Code Blocks (x == 1)
.L3:
movq %rsi, %rax # y
imulq %rdx, %rax # y*z
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 53: Handling Fall-Through
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;

## Slide 54: Code Blocks (x == 2, x == 3)
.L5: # Case 2
movq %rsi, %rax
cqto
idivq %rcx # y/z
jmp .L6 # goto merge
.L9: # Case 3
movl $1, %eax # w = 1
.L6: # merge:
addq %rcx, %rax # w += z
ret
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 55: Code Blocks (x == 5, x == 6, default)
.L7: # Case 5,6
movl $1, %eax # w = 1
subq %rdx, %rax # w -= z
ret
.L8: # Default:
movl $2, %eax # 2
ret
switch(x) {
. . .
case 5: // .L7
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 56: Summarizing
C Control
  if-then-else
  do-while
  while, for
  switch
Assembler Control
  Conditional jump
  Conditional move
  Indirect jump (via jump tables)
  Compiler generates code sequence to implement more complex control
Standard Techniques
  Loops converted to do-while or jump-to-middle form
  Large switch statements use jump tables
  Sparse switch statements may use decision trees (if-elseif-elseif-else)

## Slide 57: Exercise
xorq %rax, %rax
subq $1, %rax
cmpq $2, %rax
setl %al
movzbl %al, %eax
%rax | SF | CF | OF | ZF
0x0000 0000 0000 0000 | 0 | 0 | 0 | 1
0xFFFF FFFF FFFF FFFF | 1 | 1 | 0 | 0
0xFFFF FFFF FFFF FFFF | 1 | 0 | 0 | 0
0xFFFF FFFF FFFF FF01 | 1 | 0 | 0 | 0
0x0000 0000 0000 0001 | 1 | 0 | 0 | 0
cmpq b,a like computing a-b w/o setting dest
CF set if carry/borrow out from most significant bit (used for unsigned comparisons)
ZF set if a == b
SF set if (a-b) < 0 (as signed)
OF set if two’s-complement (signed) overflow
Note: setl and movzbl do not modify condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (signed)
setge | ~(SF^OF) | Greater or Equal (signed)
setl | SF^OF | Less (signed)
setle | (SF^OF)¦ZF | Less or Equal (signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 58: Exercise
xorq %rax, %rax
subq $1, %rax
cmpq $2, %rax
setl %al
movzbl %al, %eax
%rax | SF | CF | OF | ZF
0x0000 0000 0000 0000 | 0 | 0 | 0 | 1
0xFFFF FFFF FFFF FFFF | 1 | 1 | 0 | 0
0xFFFF FFFF FFFF FFFF | 1 | 0 | 0 | 0
0xFFFF FFFF FFFF FF01 | 1 | 0 | 0 | 0
0x0000 0000 0000 0001 | 1 | 0 | 0 | 0
cmpq b,a like computing a-b w/o setting dest
CF set if carry/borrow out from most significant bit (used for unsigned comparisons)
ZF set if a == b
SF set if (a-b) < 0 (as signed)
OF set if two’s-complement (signed) overflow
Note: setl and movzbl do not modify condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (signed)
setge | ~(SF^OF) | Greater or Equal (signed)
setl | SF^OF | Less (signed)
setle | (SF^OF)¦ZF | Less or Equal (signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 59: Switch Statement Example
Setup:
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
What range of values takes default?
Note that w not initialized here
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 60: Switch Statement Example
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Setup:
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8 # Use default
jmp *.L4(,%rdi,8) # goto *JTab[x]

## Slide 61: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}

## Slide 62: Finding Jump Table in Binary
00000000004005e0 <switch_eg>:
4005e0: 48 89 d1 mov %rdx,%rcx
4005e3: 48 83 ff 06 cmp $0x6,%rdi
4005e7: 77 2b ja 400614 <switch_eg+0x34>
4005e9: ff 24 fd f0 07 40 00 jmpq *0x4007f0(,%rdi,8)
4005f0: 48 89 f0 mov %rsi,%rax
4005f3: 48 0f af c2 imul %rdx,%rax
4005f7: c3 retq
4005f8: 48 89 f0 mov %rsi,%rax
4005fb: 48 99 cqto
4005fd: 48 f7 f9 idiv %rcx
400600: eb 05 jmp 400607 <switch_eg+0x27>
400602: b8 01 00 00 00 mov $0x1,%eax
400607: 48 01 c8 add %rcx,%rax
40060a: c3 retq
40060b: b8 01 00 00 00 mov $0x1,%eax
400610: 48 29 d0 sub %rdx,%rax
400613: c3 retq
400614: b8 02 00 00 00 mov $0x2,%eax
400619: c3 retq

## Slide 63: Finding Jump Table in Binary (cont.)
00000000004005e0 <switch_eg>:
. . .
4005e9: ff 24 fd f0 07 40 00 jmpq *0x4007f0(,%rdi,8)
. . .
% gdb switch
(gdb) x /8xg 0x4007f0
0x4007f0: 0x0000000000400614 0x00000000004005f0
0x400800: 0x00000000004005f8 0x0000000000400602
0x400810: 0x0000000000400614 0x000000000040060b
0x400820: 0x000000000040060b 0x2c646c25203d2078
(gdb)

## Slide 64: Finding Jump Table in Binary (cont.)
% gdb switch
(gdb) x /8xg 0x4007f0
0x4007f0: 0x0000000000400614 0x00000000004005f0
0x400800: 0x00000000004005f8 0x0000000000400602
0x400810: 0x0000000000400614 0x000000000040060b
0x400820: 0x000000000040060b 0x2c646c25203d2078
. . .
4005f0: 48 89 f0 mov %rsi,%rax
4005f3: 48 0f af c2 imul %rdx,%rax
4005f7: c3 retq
4005f8: 48 89 f0 mov %rsi,%rax
4005fb: 48 99 cqto
4005fd: 48 f7 f9 idiv %rcx
400600: eb 05 jmp 400607 <switch_eg+0x27>
400602: b8 01 00 00 00 mov $0x1,%eax
400607: 48 01 c8 add %rcx,%rax
40060a: c3 retq
40060b: b8 01 00 00 00 mov $0x1,%eax
400610: 48 29 d0 sub %rdx,%rax
400613: c3 retq
400614: b8 02 00 00 00 mov $0x2,%eax
400619: c3 retq

## Slide 65: Reminder: Machine Instructions
C
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Machine
  3 bytes at address 0x40059e
  Compact representation of the assembly instruction
  (Relatively) easy for hardware to interpret
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03
0100 1 0 0 0 10001011 00 000 011
REX W R X B MOV r->x Mod R M
Notes: We’re not going to get into exactly what these fields mean, what you should remember is that there’s always a part corresponding directly to the name of the assembly instruction – that’s called the opcode – and the rest of it somehow encodes the arguments. R=0000, for instance, means RAX.

## Slide 66: Memory operands and LEA
In most instructions, a memory operand accesses memory
LEA is special: it doesn’t access memory
Assembly | C equivalent
mov 6(%rbx,%rdi,8), %ax | ax = *(rbx + rdi*8 + 6)
add 6(%rbx,%rdi,8), %ax | ax += *(rbx + rdi*8 + 6)
xor %ax, 6(%rbx,%rdi,8) | *(rbx + rdi*8 + 6) ^= ax
Assembly | C equivalent
lea 6(%rbx,%rdi,8), %rax | rax = rbx + rdi*8 + 6

## Slide 67: Why use LEA?
CPU designers’ intended use: calculate a pointer to an object
  An array element, perhaps
  For instance, to pass just one array element to another function
Compiler authors like to use it for ordinary arithmetic
  It can do complex calculations in one instruction
  It’s one of the only three-operand instructions the x86 has
  It doesn’t touch the condition codes (we’ll come back to this)
Assembly | C equivalent
lea (%rbx,%rdi,8), %rax | rax = &rbx[rdi]
Assembly | C equivalent
lea (%rbx,%rbx,2), %rax | rax = rbx * 3