## Slide 1: 15-744: Computer Networking
L-26 Privacy

## Slide 2: Overview
Routing privacy
Privacy and Accountability
Wireless Privacy

## Slide 3: Randomized Routing
Hide message source by routing it randomly
  Popular technique: Crowds, Freenet, Onion routing
Routers don’t know for sure if the apparent source of a message is the true sender or another router

## Slide 4: Onion Routing
Sender chooses a random sequence of routers
  Some routers are honest, some controlled by attacker
  Sender controls the length of the path
R
R4
R1
R2
R
R
R3
Bob
R
R
R
Alice

## Slide 5: Route Establishment
R4
R1
R2
R3
Bob
Alice
{R2,k1}pk(R1),{ }k1
{R3,k2}pk(R2),{ }k2
{R4,k3}pk(R3),{ }k3
{B,k4}pk(R4),{ }k4
{M}pk(B)
Routing info for each link encrypted with router’s public key
Each router learns only the identity of the next router

## Slide 6: Tor
Second-generation onion routing network
  http://tor.eff.org
  Developed by Roger Dingledine, Nick Mathewson and Paul Syverson
  Specifically designed for low-latency anonymous Internet communications
Running since October 2003
100s nodes on four continents, thousands of users
“Easy-to-use” client proxy
  Freely available, can use it for anonymous browsing

## Slide 7: How does Tor work?

## Slide 8: How does Tor work?

## Slide 9: Tor Circuit Setup (1)
Client proxy establish a symmetric session key and circuit with Onion Router #1

## Slide 10: Tor Circuit Setup (2)
Client proxy extends the circuit by establishing a symmetric session key with Onion Router #2
  Tunnel through Onion Router #1

## Slide 11: Tor Circuit Setup (3)
Client proxy extends the circuit by establishing a symmetric session key with Onion Router #3
  Tunnel through Onion Routers #1 and #2

## Slide 12: Using a Tor Circuit
Client applications connect and communicate over the established Tor circuit

## Slide 13: Location Hidden Servers
Goal: deploy a server on the Internet that anyone can connect to without knowing where it is or who runs it
Accessible from anywhere
Resistant to censorship
Can survive full-blown DoS attack
Resistant to physical attack
  Can’t find the physical server!

## Slide 14: Creating a Location Hidden Server
Server creates onion routes
to “introduction points”
Server gives intro points’
descriptors and addresses
to service lookup directory
Client obtains service
descriptor and intro point
address from directory

## Slide 15: Using a Location Hidden Server
Client creates onion route
to a “rendezvous point”
Client sends address of the
rendezvous point and any
authorization, if needed, to
server through intro point
If server chooses to talk to client,
connect to rendezvous point
Rendezvous point
mates the circuits
from client & server

## Slide 16: Schedule Change
Second Exam – Friday 5/5
Project Writeups Due – Monday 5/8

## Slide 17: Overview
Routing privacy
Privacy and Accountability
Wireless Privacy

## Slide 18
anti-spoofing mechanism
+ shutoff protocol
cryptographic addresses
Accountability
Privacy
VS
operators want to know who sends each packet
so they can stop malicious senders
users want to hide who sends certain packets
so they can do stuff without the whole world knowing
Accountable Internet Protocol
[Andersen et al., SIGCOMM 2008]
No Privacy
Shutoff is Stop-Gap Fix
Requires “Smart NIC”
Tor Instead of IP
[Liu et al., HotNets 2011]
routers act as onion nodes
Heavyweight
No Accountability
unforgeable source addresses
hidden source addresses

## Slide 19
Destination Address
Source Address
…
return address
accountability
sender identity
error reporting
flow ID

## Slide 20
Destination Address
…
Return Address
Accountability Address
Separate Accountability
and Return Addresses

## Slide 21
Accountable and Private Internet Protocol
APIP:
Destination Address
…
Return Address
Accountability Address
Separate Accountability
and Return Addresses
+
Delegated Accountability
+
Hidden Return
Addresses
Return Address

## Slide 22: Delegated Accountability
Sender
Receiver
Accountability
Delegate
P
brief(P)
verify(P)
shutoff(P)
P
OK

## Slide 23: brief(P)
“I sent this packet.”
Sender to Delegate:
P
Delegate
Sender
F(P)
Fingerprint
Cache
04AF4DE779
B217C45091
30e26e83b2
cf24dba5f0
b0afd9c282
Batch fingerprints in Bloom filter
Delegate does not learn packet contents

## Slide 24: Delegated Accountability
Sender
Receiver
Accountability
Delegate
brief(P)
verify(P)
shutoff(P)
P
P

## Slide 25: verify(P)
“Do you vouch for this packet?”
Verifier to Delegate:
A
A’s Delegate
PA → B
Verified Flows
A → B
TWO CHECKS:
PA➞B in fingerprint cache
Flow A➞B not shut off
verify(P)
OK
verify(P)
Most effective at first hop
Verified flow entries periodically expire
Routers keep no state during verification

## Slide 26: Delegated Accountability
Sender
Receiver
Accountability
Delegate
brief(P)
verify(P)
shutoff(P)
P
P

## Slide 27: shutoff(P)
“Stop this flow.”
Receiver to Delegate:
B
A’s Delegate
PA → B
Verified Flows
A → B
PA → B
shutoff(P)
PA → B
verify(P)
DROP_FLOW
BLOCKED
Flows
A → B
Signature proves receiver sent shutoff
Delegate also facilitates long-term fix
Filtering happens at router, not NIC

## Slide 28: Flow Granularity
One flow ID for all clients
Large Anonymity Set
Granularity: Delegate ⬌ Destination
One flow ID per connection
No Collateral Damage for Shutoff
Granularity: TCP Flow

## Slide 29: Assigning Flow IDs
Unique
No Collateral Damage
Shared
Large Anonymity Set
Variety of Classes
Flexible
Delegate
Delegate’s Clients
Flow IDs

## Slide 30
Destination Address
…
Return Address
Accountability Address
Separate Accountability
and Return Addresses
+
Delegated Accountability
Accountable and Private Internet Protocol
APIP:
+
Hidden Return
Addresses
Return Address
Real-World Deployment

## Slide 31: Hiding Return Addresses
End-To-End Encryption
Address Translation
1
2
Destination
…
Return
Accountability
Destination
…
Return
Accountability
Destination
…
Opaque ID
Accountability
Protection From: | 
 | Source Domain
✓ | Local Observers
✓ | Transit Networks
 | Receiver
Protection From: | 
 | Source Domain
 | Local Observers
✓ | Transit Networks
✓ | Receiver

## Slide 32: Example Deployments
Fingerprint
Cache
Source Domain
Border Router
+ Delegate
Specialized Companies
as Delegates
Source Domains
as Delegates
No burden on source domains
Larger anonymity set
EXTERNAL
Delegate
DESTINATION
RETURN
DESTINATION
ACCOUNTABILITY
DESTINATION
RETURN
ACCOUNTABILITY
No briefing overhead
Lower verification latency

## Slide 33
Accountability
Privacy
unforgeable source addresses
hidden source addresses
every packet carries an accountability address
for reporting misbehavior
Delegated Accountability
return address can be hidden
since network just needs accountability address
Hidden Return
Addresses
Return Address
VS
&

## Slide 34: Overview
Routing privacy
Privacy and Accountability
Wireless Privacy

## Slide 35: Our Wireless World
tcpdump
PrivatePhoto1.jpg
Link Layer Header
Link Layer Header
Home location=(47.28,…
Link Layer Header
Buddy list: Alice, Bob, …
PrivateVideo1.avi
Link Layer Header
Link Layer Header
Blood pressure: high
Notes: More and more personal devices are being equipped with wireless capabilities like 802.11 and bluetooth. They include everything from media players and ipods to sensors on our clothing and our bodies.
Because of this trend, we now often carry wireless devices with us where ever we go, from our homes to our cars and even to places that we think should have more privacy.
Unfortunately, in this emerging wireless world, bad guys still exist. They can easily overhear any of our wireless transmissions, often with nothing more than a laptop computer. Thus, without protection, an eavesdropper can easily obtain private information.

## Slide 36: Best Security Practices
SSID: Bob’s Network
Key: 0x2384949…
Discover
802.11 probe
Is Bob’s Network here?
802.11 beacon
Bob’s Network is here
Username: Alice
Key: 0x348190…
802.11 auth
Proof that I’m Alice
802.11 auth
Proof that I’m Bob
Authenticate
and Bind
802.11 header
802.11 header
Send Data
Bootstrap
Out-of-band (e.g., password, WiFi Protected Setup)
tcpdump
Confidentiality
Authenticity
Integrity
Notes: Protocols such as 802.11 try to protect against such threats with the following best practices.
Beforehand, Alice, a client such as a laptop, and Bob, a service such as an access point, exchange keys in a secure, out-of-band manner. For example, by passing a password on a post-it note.
Now, whenever Alice opens up her laptop, it tries to discover if Bob is present with probes or listening for Bob’s beacons.
If she discovers that Bob is present, then they use the bootstrapped key to exchange information that proves to each other they are who they think they are.
This process enables them to encrypt the data they send each other in a manner that is confidential, authentic, and maintains its data integrity.

## Slide 37: Privacy Problems Remain
802.11 header
Send Data
MAC addr, seqno, …
Bootstrap
SSID: Bob’s Network
Secret: 0x2384949…
Username: Alice
Secret: 0x348190…
Discover
802.11 probe
Is Bob’s Network here?
802.11 beacon
Bob’s Network is here
tcpdump
802.11 auth
Proof that I’m Alice
802.11 auth
Proof that I’m Bob
Authenticate
and Bind
Is Bob’s Network here?
Proof that I’m Bob
Bob’s Network is here
MAC addr, seqno, …
Many exposed bits are (or can be used as) identifiers that are linked over time
Confidentiality
Authenticity
Integrity
Notes: Unfortunately, in our pervasive wireless world, the information that remains exposed during this process poses additional privacy threats.
This is because many bits that remain exposed are, or can be used as, identifiers that are linked over time.

## Slide 38: Problem: Long-Term Linking
Alice
Alice?
MAC: 12:34:56:78:90:ab
Alice’s iPod is here
802.11 beacon
Alice’s iPod is here
802.11 beacon
Easy to identify and relate devices over time
Is Alice’s iPod here?
802.11 probe
tcpdump
MAC: 12:34:56:78:90:ab
Alice’s friend?
Notes: For example, this enables long-term linking. Identifiers such as MAC addresses and network names remain present in link layer headers and during the discovery process.
These identifiers are consistent over long periods of time, so it is relatively easy to track the movement of devices and infer their relationships.

## Slide 39: Problem: Long-Term Linking
www.bluetoothtracking.org
Linking enables location tracking, user profiling, inventorying, relationship profiling, …
[Greenstein, HotOS ’07; Jiang, MobiSys ’07; Pang, MobiCom ’07, HotNets ’07]
Home
www.wigle.net
802.11 header
Is “djw” here?
“djw” is here
Notes: Long-term linking enables many attacks against our privacy such as location tracking, user profiling, and inventorying.
These attacks are just emerging but there are already real tracking networks, such as the bluetooth network in the netherlands listed on this slide. In addition, there are many concerns expressed in the popular media.

## Slide 40: Problem: Short-Term Linking
Alice -> AP
00:00:99:99:11:11
12:34:56:78:90:ab
12:34:56:78:90:ab
Alice -> AP
00:00:99:99:11:11
Alice -> AP
00:00:99:99:11:11
12:34:56:78:90:ab
12:34:56:78:90:ab
12:34:56:78:90:ab, seqno: 1, …
12:34:56:78:90:ab, seqno: 2, …
12:34:56:78:90:ab, seqno: 3, …
12:34:56:78:90:ab, seqno: 4, …
00:00:99:99:11:11, seqno: 103, …
00:00:99:99:11:11, seqno: 104, …
00:00:99:99:11:11, seqno: 102, …
Easy to isolate distinct packet streams
3-9 data streams overlap
each 100 ms, on average
tcpdump
Notes: A second problem is short-term linking. Most of the time, an eavesdropper will overhear data streams from many devices. But identifiers in link-layer headers make it easy for eavesdroppers to isolate individual data streams. The obvious identifier that he can use is a MAC address, but in many cases, other bits of information, such as sequence numbers will work as well.

## Slide 41: Problem: Short-Term Linking
Isolated data streams are more susceptible to side-channel analysis on packet sizes and timing
  Exposes keystrokes, VoIP calls, webpages, movies, …
[Liberatore, CCS ‘06; Pang, MobiCom ’07; Saponas, Usenix Security ’07; Song, Usenix Security ‘01; Wright, IEEE S&P ‘08; Wright, Usenix Security ‘07]
≈
DFT
transmission sizes
transmission sizes
300
250
200
100
500
120
Video
compression signatures
Device
fingerprints
Keystroke
timings
Notes: Short-term linking is problematic because isolated data streams are more susceptible to side-channel analysis. Recent research has shown that even when encrypted, the sequence of packet sizes and timings in a data stream can reveal its contents. This includes things like keys you type, words in your voice-over-IP calls, and webpages you visit.
Data packets have a wide interface so many more applications may inadvertently be vulnerable because they don’t add any additional protection before encapsulating data in them. Short-term linking helps enable them because they are less successful when multiple packet streams are mixed together.

## Slide 42: Fundamental Problem
Bootstrap
SSID: Bob’s Network
Secret: 0x2384949…
Username: Alice
Secret: 0x348190…
Discover
802.11 probe
Is Bob’s Network here?
802.11 beacon
Bob’s Network is here
tcpdump
802.11 auth
Proof that I’m Alice
802.11 auth
Proof that I’m Bob
Authenticate
and Bind
Send Data
Many exposed bits are (or can be used as) identifiers that are linked over time
Is Bob’s Network here?
Proof that I’m Bob
Bob’s Network is here
MAC addr, seqno, …
MAC addr, seqno, …
Notes: So fundamental problem in both long-term and short-term linking is that many exposed bits are, or can be used as identifiers that are linked over time.

## Slide 43: Goal: Make All Bits Appear Random
Discover
Authenticate
and Bind
Send Data
Bootstrap
SSID: Bob’s Network
Key: 0x2384949…
Username: Alice
Key: 0x348190…
tcpdump
?
Notes: Therefore, our goal in this talk is to develop a protocol that makes all bits appear random to third parties. This includes all the packets sent for discovery and authentication and all bits in link layer headers.

## Slide 44: Challenge: Filtering without Identifiers
Which packets are mine?
Which packets are mine?
Notes: Why is this hard to do? Since no longer have source or destination addresses in packets, filtering packets efficiently becomes much more challenging.

## Slide 45: Design Requirements
When A generates Message to B, she sends: PrivateMessage = F(A, B, Message) where F has these properties:
  Confidentiality: Only A and B can determine Message.
  Authenticity: B can verify A created PrivateMessage.
  Integrity: B can verify Message not modified.
  Unlinkability: Only A and B can link PrivateMessages to same sender or receiver.
  Efficiency: B can process PrivateMessages as fast as he can receive them.
A→B Header…
Unencrypted payload
Notes: More specifically, what I mean…

## Slide 46: Solution Summary
Unlinkability
Integrity
Authenticity
Efficiency
Confidentiality
802.11 WPA
MAC Pseudonyms
Public Key
Symmetric Key
SlyFi: Discovery/Binding
SlyFi: Data packets
Only
Data
Payload
Only
Data
Payload
Only
Data
Payload
Notes: For example, …

## Slide 47: Straw man: MAC Pseudonyms
Idea: change MAC address periodically
  Per session or when idle [Gruteser ’05, Jiang ‘07]
Other fields remain (e.g., in discovery/binding)
  No mechanism for data authentication/encryption
  Doesn’t hide network names during discovery or credentials during authentication
Pseudonyms are linkable in the short-term
  Same MAC must be used for each association
  Data streams still vulnerable to side-channel leaks
Notes: To try to get unlinkability, the first thing we might try is to remove the obviously identifying bits of information in packets, such as MAC addresses. For example, it has recently been proposed…

## Slide 48: Solution Summary
Unlinkability
Integrity
Authenticity
Efficiency
Confidentiality
802.11 WPA
MAC Pseudonyms
Public Key
Symmetric Key
SlyFi: Discovery/Binding
SlyFi: Data packets
Only
Data
Payload
Long Term
Only
Data
Payload
Only
Data
Payload
Notes: So MAC Pseudonyms by themselves do not give us…
It is also non-trivial to combine pseudonyms and WPA because WPA exposes identifiers in the discovery and binding process

## Slide 49: Straw man: Encrypt Everything
Bootstrap
SSID: Bob’s Network
Key: 0x2384949…
Username: Alice
Key: 0x348190…
Discover
Authenticate
and Bind
Send Data
Idea: Use bootstrapped keys to encrypt everything
Notes: To try to obtain the best of both worlds, we then may try to encrypt everything. After all, we already have…

## Slide 50: Straw man: Public Key Protocol
Probe “Bob”
Key-private encryption (e.g., ElGamal)
KBob
Check signature:
Try to decrypt
K-1Bob
KAlice
Based on [Abadi ’04]
K-1Alice
Sign:
Slow! (>100ms)
Client
Service
Notes: One way we can do this is …

## Slide 51: Straw man: Symmetric Key Protocol
Probe “Bob”
Client
Service
Symmetric encryption (e.g., AES w/ random IV)
Check MAC:
MAC:
KAB
KAB
KAB
Try to
decrypt
with each
shared key
KShared1
KShared2
KShared3
…
Slow! (scales w/ # keys)
Different symmetric key per potential sender
Can’t identify the
decryption key in the packet or else it is linkable
Notes: To address this problem, we might instead try to use symmetric key encryption, because it is much faster than public key encryption…

## Slide 52: Solution Summary
Unlinkability
Integrity
Authenticity
Efficiency
Confidentiality
802.11 WPA
MAC Pseudonyms
Public Key Protocol
Symmetric Key Protocol
SlyFi: Discovery/Binding
SlyFi: Data packets
Long
Term
Only
Data
Payload
Only
Data
Payload
Only
Data
Payload
Notes: So the encrypt everything approach

## Slide 53: SlyFi
Symmetric key almost works, but tension between:
  Unlinkability: can’t expose the identity of the key
  Efficiency: need to identify the key to avoid trying all keys
Idea: Identify the key in an unlinkable way
Approach:
  Sender A and receiver B agree on tokens: T1 , T2 , T3 , …
  A attaches Ti to encrypted packet for B
AB
AB
AB
AB
Notes: To try to regain efficiency, we make the following observation: …
The key idea we leverage in our design of our solution slyfi is…

## Slide 54: SlyFi
Probe “Bob”
Client
Service
Symmetric encryption
(e.g., AES w/ random IV)
Check MAC:
MAC:
KAB
KAB
KAB
KAB
Lookup Ti in a
table to get KAB
Ti
AB
AB
Required properties:
  Third parties can not link Ti and Tj if i ≠ j
  A doesn’t reuse Ti
  A and B can compute Ti independently
AB
AB
AB
AB
Ti = AESK (i)
AB
AB
Ti = AESK (i)
AB
AB
Main challenge:
Sender and receiver must synchronize i
Notes: That is, SlyFi is basically the same as the symmetric key approach, but …

## Slide 55: SlyFi: Data Transport
Data messages:
  Only sent over established connections
   Expect messages to be delivered
   Use implicit transmission number to synchronize i
Ti = AESK (i) where i = transmission #
AB
AB
Ti
AB
Ti+1
AB
Ti +2
AB
Ti +3
AB
Notes: For data messages we make the observation …

## Slide 56: SlyFi: Data Transport
Data messages:
  Only sent over established connections
   Expect messages to be delivered
   Use implicit transmission number to synchronize i
Ti = AESK (i) where i = transmission #
AB
On receipt of Ti , B computes next expected: Ti+1
Handling message loss:
  On receipt of Ti save Ti+1, … , Ti+k in table
  Tolerates k consecutive losses (k=50 is enough)
  No loss  compute one token per reception
AB
AB
AB
AB
AB
AB
Notes: For data messages we make the observation …

## Slide 57: SlyFi: Discovery/Binding
Discovery & binding messages:
  Often sent when other party is not present
   Can’t expect most messages to be delivered
   Can’t rely on transmission reception to synchronize i
Is Bob’s Network here?
Ti
AB
i = ?
Is Bob’s Network here?
Ti +1
AB
Is Bob’s Network here?
Ti +3
AB
Is Bob’s Network here?
Ti +2
AB
..
..
…...
Nope.
Nope.
Nope.
Notes: We can not use the same approach for discovery and binding messages however, because discovery messages are often sent when the other party is not present. For example, Alice sends discovery probes whenever she opens up her laptop, even if bob is not present.

## Slide 58: SlyFi: Discovery/Binding
Discovery & binding messages:
  Infrequent: only sent when trying to associate
  Narrow interface: single application, few side-channels
   Linkability at short timescales is usually OK
   Use loosely synchronized time to synchronize i
Ti = AESK (i) where i = current time/5 min
AB
AB
802.11 probe
802.11 beacon
802.11 auth
802.11 auth
Ti
AB
Ti
AB
Ti
BA
Ti
BA
Notes: Instead, we make two observations…

## Slide 59: SlyFi: Discovery/Binding
Discovery & binding messages:
  Infrequent: only sent when trying to associate
  Narrow interface: single application, few side-channels
   Linkability at short timescales is usually OK
   Use loosely synchronized time to synchronize i
Ti = AESK (i) where i = current time/5 min
AB
AB
At the start of time interval i compute Ti
Handling clock skew:
  Receiver B saves Ti-s, … , Ti+s in table
  Tolerates clock skew of 5s minutes
AB
AB
AB
Notes: Instead, we make two observations…

## Slide 60: Solution Summary
Unlinkability
Integrity
Authenticity
Efficiency
Confidentiality
802.11 WPA
MAC Pseudonyms
Public Key
Symmetric Key
SlyFi: Discovery/Binding
SlyFi: Data packets
Long
Term
Long
Term
Only
Data
Payload
Only
Data
Payload
Only
Data
Payload
Notes: Thus, we conclude that slyfi is efficient. For discovery and binding, it also provides …

## Slide 61: Overview
Routing privacy
Privacy and Accountability
Wireless Privacy
Private Middleboxes

## Slide 62: BlindBox: DPI for Users and Network Admins
Bob
Alice
IPS
“Rule Generators”
ATTACK
HACKS
183237
RULES
ATTACK
Rule = description of an attack.
Notes: The network admin’s requirement is that data be inspected for attacks — what if Alice is Malicious? And that’s what middleboxes here do. The way it works, usually, is…

## Slide 63: Intrusion Prevention
Bob
Alice
IPS
ATTACK
HACKS
183237
RULES
Bob does not get the benefits of Intrusion Prevention!
with HTTPS
ATTACK
0xf34…
????
I want privacy!
Notes: For that reason, Alice and Bob may use an encrypted protocol like HTTPS. However, this leads to problems for our network administrator and their middlebox.

## Slide 64: State of the Art Solution? Man in the Middle SSL
Bob
IPS
Bob has no privacy from middlebox!
I am Google
fake certificate
SECRET
Notes: So In practice, what winds up happening is the administrator man in the middles the connection, decrypting all the data — and we’re back to square one. No privacy for Bob.

## Slide 65: BlindBox [SIGCOMM ’15]
The first system to allow DPI middle boxes to inspect traffic without decrypting the traffic.
Detects blacklisted keywords in encrypted connections.
Learns virtually nothing about connections that do not contain blacklisted keywords.

## Slide 66: Threat Model
“Rule Generator”
Generates rules correctly
Runs detection functionality correctly
Aims to protect one honest endpoint from another dishonest endpoint. Does not address two dishonest endpoints.
Users should not learn McAffee’s ruleset.
but curious to see traffic contents (“honest but curious model”)
Alice
Bob

## Slide 67: BlindBox Encrypt: A Deterministic Strawman
Alice
Blacklist
ATTACK
HACKS
183237
AESK(ATTACK)
EXAMPLE ATTACK
Bob
EXAMPL
AESK(EXAMPL)
XAMPLE
AMPLE
…
ATTACK

## Slide 68: A problem with the strawman design
Alice
Blacklist
ATTACK
HACKS
183237
I LOVE MUFFINS. WHAT IS YOUR FAVORITE MUFFIN? ATTACK
MUFFIN
MUFFIN
This term appears twice in the connection!
Deterministic Encryption leaks substring frequency.
Bob

## Slide 69: BlindBox HTTPS: Overview
Alice’s Protocol Stack
Message
SSL Encrypt
SSL Decrypt
BlindBox Encrypt
SSL Traffic
ATTACK
HACKS
183237
BLACKLIST
BB Handshake
Encrypted Tokens
HACKS
BlindBox Verify
Bob’s Protocol Stack
Notes: Here’s how it works at a high level.

## Slide 70: One Slide Introduction to BB Handshake
An exchange between the middlebox and the client at the beginning of a new connection.
Middlebox learns AESK(kw) for every keyword in ruleset, iff keyword has a signature from rule generator.
Clients know secret key “K”
SECRET
HACKS
Middlebox and Rule generator know rules.
Middlebox does not learn K.
Clients do not learn rules.
Based on two known techniques: Garbled Circuits and Oblivious Transfer.
AES encryption
keyword
AESK(kw)
BLACKLIST

## Slide 71: MBArk: Can we improve privacy for outsourced, general appliances?
Enterprise
Cloud
Notes: Let’s look at the overview of service model. In this model,
Middleboxes that are traditionally running in the enterprise
are outsourced to the cloud

## Slide 72: Service Model
Enterprise
Cloud
Gateway
Encrypt / Decrypt traffic to/from the cloud
Notes: the gateway is the component in the enterprise that encrypt the traffic to the cloud and decrypt the traffic from the cloud
all the traffic from and to the enterprise will go through the gateway first

## Slide 73: Service Model
Enterprise
Cloud
Middlebox Rules
IP firewall rules,
IDS signatures, etc.
Notes: middlebox may have some form of rules, that tell the middlebox how to process the traffic, like the firewall rulesets or IDS signatures

## Slide 74: Initialization
Enterprise
Cloud
Enterprise encrypt rules using EncryptRanges.
Notes: In this service model, during the initialization step, we allow the enterprise to encrypt middleboxes rules, using the function EncryptRanges

## Slide 75: Initialization
Enterprise
Cloud
Middleboxes deploy encrypted rules.
Notes: After that, middleboxes deploy encrypted rules.
After this initialization step, let’s look at how the packet flows

## Slide 76: Packet Flow
Enterprise
Cloud
1. Outgoing traffic are sent to Gateway.
Notes: As we mentioned before, outgoing traffic from the enterprise are sent to the gateway.

## Slide 77: Packet Flow
Enterprise
Internet
Cloud
2. Encrypt the traffic
Encrypt packet headers field by field using EncryptValue
Encrypt payloads using stream cipher
Implication: no change to packet structure
Notes: Packets get encrypted at the gateway
Here, we encrypt packet headers field by field using EncryptValue. In order to prevent middleboxes from reading payloads, we encrypt payloads using stream cipher. The packet structure is unchanged.

## Slide 78: Packet Flow
Enterprise
Cloud
3. Forward to Cloud
Notes: Packets are then forwarded to the Cloud.

## Slide 79: Packet Flow
Enterprise
Cloud
4. Middleboxes process encrypted traffic.
No change to algorithms:
E.g., LPM, multi-dimensional classifiers, etc.
Notes: Middleboxes on the Cloud process the traffic as usual. The traffic is still in encrypted form. And the packet classification algorithms used by middleboxes are remained unchanged.

## Slide 80: Packet Flow
Enterprise
Cloud
5. Back to Gateway
Notes: Then the traffic is sent back to the gateway.

## Slide 81: Packet Flow
Enterprise
Internet
Cloud
6. Decrypt and Forward
Notes: Then the gateway decrypt the packet and forward it to the Internet.
The incoming traffic follows a similar procedure. It will first be encrypted by the gateway and forwarded to the Cloud for processing.

## Slide 82: Overview
Routing privacy
Web Privacy
Wireless Privacy

## Slide 83: An “Old” Problem
Many governments/companies trying to limit their citizens’ access to information
  Censorship (prevent access)
  Punishment (deter access)
  China, Saudi Arabia, HP
How can we defeat such attempts?
  Circumvent censorship
  Undetectably

## Slide 84: Proxy-Based Web Censorship
Government manages national web firewall
  Not optional---catches ALL web traffic
Block certain requests
  Possibly based on content
  More commonly on IP address/publisher
  China: Western news sites, Taiwan material
Log requests to detect troublemakers
  Even without blocking, may just watch traffic
But they don’t turn off the whole net
  Creates a crack in their barrier

## Slide 85: Goal
Circumvent censor via innocent web activity
  Normal web server and client cooperate to create covert channel
Without consequence for client
And without consequence for server
  Broad participation increases system robustness
  Ensure offering service doesn’t lead to trouble
  e.g., loss of business through being blocked
  Also, “law knows no boundaries”

## Slide 86: The Big Picture

## Slide 87: Requirements
Client deniability
  Detection could be embarrassing or worse
Client statistical deniability
  Even suspicion could be a problem
Server covertness/statistical deniability
  If server detected, can be blocked
Communication robustness
  Even without detecting, censor could scramble covert channel
Performance (bandwidth, latency)

## Slide 88: (Un)related Work
SSL
  Encrypted connection---can’t tell content
  Suspicious!
  Doesn’t help reach blocked servers
  Govt. can require revealing SSL keys
Anonymizing Proxies
  Prevent servers from knowing identity of client
  But proxy inside censor can’t reach content
  And proxy outside censor can be blocked
  And use of proxy is suspicious

## Slide 89: Safeweb/Triangle boy
Operation
  Client contacts triangle-boy “reflector”
  Reflector forwards requests to blocked server
  Server returns content to client (IP spoof)
Circumvents censorship
But still easily detected
  “Local monitoring of the user only reveals an encrypted conversation between User and Triangle Boy machine.” (Safeweb manual)

## Slide 90: Summary
Easy to hide what you are getting
  Just use SSL
And easy to circumvent censors
  Safeweb
But hard to hide that you are doing it

## Slide 91: Circumventing Censors
Censors allow certain traffic
Use to construct a covert channel
  Talk to normal servers
  Embed requests for censored content in normal-seeming requests
  Receive censored content hidden in normal-seeming responses
Requester: client asking for hidden content
Responder: server covertly providing it

## Slide 92: System Architecture

## Slide 93: Receiving Content is Easier Half
Responder is a normal web server, serving images (among other things)
Encrypt data using requestor key
Embed in “unimportant, random” bits of images
  E.g., high order color bits
  Watermarking
Encrypted data looks random---only requestor can tell it isn’t (and decrypt)

## Slide 94: Example
One image has embedded content
You can’t tell which (shows it’s working)

## Slide 95: Goals Analysis
Client looks innocent (receives images)
  Infranet users & nonusers indistinguishable
Server less so
  Any one image seems innocent
  But same image with different “random bits” in each copy is suspicious
  Evasion: never use same image-URL twice
    Justify: per-individual customized web site
    Human inspection might detect odd URL usage
  Evasion: use time-varying image (webcam)
Performance: 1/3 of image bits

## Slide 96: Upstream (Requests) is Harder
No “random content bits” that can be fiddled to send messages to responder
Solution: let browsing pattern itself be the message
Suppose web page has k links.
  GET on ith link signifies symbol “i” to requestor
  Result: log2(k) message bits from link click
Can be automated
To prevent censor from seeing message, encrypt with responder key

## Slide 97: Goals Analysis
Deniability: requestor generates standard http GETs to allowed web sites
  Fact of GETs isn’t itself proof of wrongdoing
  Known rule for translating GETs to message, but message is encrypted, so not evidence
Statistical deniability
  Encrypting message produces “random” string
  Sent via series of “random” GETs
  Problem: normal user browsing not random
    Some links rare
    Conditional dependence of browsing on past browsing

## Slide 98: Performance vs. Deniability
Middling deniability, poor performance
  Request URL may be (say) 50 characters
  16 Links/Page (say) means 4 bits
  So need 100 GETs to request one URL!
  And still poor statistical deniability
Can we enhance deniability?
  Yes, by decreasing performance further
Can we enhance performance?
  Yes, and enhance deniability at same time

## Slide 99: Paranoid Alternative
Settle for one message bit per GET
  Odd/even links on page
  Or generalize to “mod k” for some small k
User has many link choices for each bit
  Can choose one that is reasonable
  Incorporate error correcting code in case no reasonable next link sends correct bit
Drawback: user must be directly involved in sending each message bit
  Very low bandwidth vs time spent

## Slide 100: Higher Performance
Idea: arithmetic coding of requests
  If request i has probability pi, then entropy of request distribution is –S pi log pi
  Arithmetic coding encodes request i using log pi bits
  Result: expected request size equals entropy
  Optimal
Problem: requestor doesn’t know probability distribution of requests
  Doesn’t have info needed for encoding

## Slide 101: Solution: Range Mapping
Adler-Maggs
Exploit asymmetric bandwidth
Responder sends probability distribution to requester using easy, downstream path
Requestor uses this “dictionary” to build arithmetic code, send encoded result
Variation for non-binary
  Our messages aren’t bits, they are clicks
  And server knows different clicks should have different probabilities

## Slide 102: Toy Example
Suppose possible requests fewer than links on page
Responder sends dictionary:
  “link 1 means http://mit.edu”
  “link 2 means http://stanford.edu”
  Assigns common requests to common GETs
Requestor GETs link matching intended request
One GET sends full (possibly huge) request
Problem: in general, ∞ possible requests
  Can’t send a dictionary for all

## Slide 104: Overview
P2P Privacy

## Slide 105: Freenet
Addition goals to file location:
  Provide publisher anonymity, security
  Resistant to attacks – a third party shouldn’t be able to deny the access to a particular file (data item, object), even if it compromises a large fraction of machines
Files are stored according to associated key
  Core idea: try to cluster information about similar keys
Messages
  Random 64bit ID used for loop detection
  TTL
    TTL 1 are forwarded with finite probablity
    Helps anonymity
  Depth counter
    Opposite of TTL – incremented with each hop
    Depth counter initialized to small random value

## Slide 106: Data Structure
Each node maintains a common stack
  id – file identifier
  next_hop – another node that store the file id
  file – file identified by id being stored on the local node
Forwarding:
  Each message contains the file id it is referring to
  If file id stored locally, then stop
    Forwards data back to upstream requestor
    Requestor adds file to cache, adds entry in routing table
  If not, search for the “closest” id in the stack, and forward the message to the corresponding next_hop
id next_hop file
…
…

## Slide 107: Query Example
Note: doesn’t show file caching on the reverse path
4 n1 f4
12 n2 f12
5 n3
9 n3 f9
3 n1 f3
14 n4 f14
5 n3
14 n5 f14
13 n2 f13
3 n6
n1
n2
n3
n4
4 n1 f4
10 n5 f10
8 n6
n5
query(10)
1
2
3
4
4’
5

## Slide 108: Freenet Requests
Any node forwarding reply may change the source of the reply (to itself or any other node)
  Helps anonymity
Each query is associated a TTL that is decremented each time the query message is forwarded; to obscure distance to originator:
  TTL can be initiated to a random value within some bounds
  When TTL=1, the query is forwarded with a finite probability
Each node maintains the state for all outstanding queries that have traversed it  help to avoid cycles
If data is not found, failure is reported back
  Requestor then tries next closest match in routing table

## Slide 109: Freenet Request
1
A
B
C
D
E
F
Data Request
Data Reply
Request Failed
2
3
12
6
7
4
11
10
9
5
8

## Slide 110: Freenet Search Features
Nodes tend to specialize in searching for similar keys over time
  Gets queries from other nodes for similar keys
Nodes store similar keys over time
  Caching of files as a result of successful queries
Similarity of keys does not reflect similarity of files
Routing does not reflect network topology

## Slide 111: Freenet File Creation
Key for file generated and searched  helps identify collision
  Not found (“All clear”) result indicates success
  Source of insert message can be change by any forwarding node
Creation mechanism adds files/info to locations with similar keys
New nodes are discovered through file creation
Erroneous/malicious inserts propagate original file further

## Slide 112: Cache Management
LRU Cache of files
Files are not guaranteed to live forever
  Files “fade away” as fewer requests are made for them
File contents can be encrypted with original text names as key
  Cache owners do not know either original name or contents  cannot be held responsible

## Slide 113: Freenet Naming
Freenet deals with keys
  But humans need names
  Keys are flat  would like structure as well
Could have files that store keys for other files
  File /text/philiosophy could store keys for files in that directory  how to update this file though?
Search engine  undesirable centralized solution

## Slide 114: Freenet Naming - Indirect files
Normal files stored using content-hash key
  Prevents tampering, enables versioning, etc.
Indirect files stored using name-based key
  Indirect files store keys for normal files
  Inserted at same time as normal file
Has same update problems as directory files
  Updates handled by signing indirect file with public/private key
  Collisions for insert of new indirect file handled specially  check to ensure same key used for signing
Allows for files to be split into multiple smaller parts

## Slide 116: How does Tor work?

## Slide 117: How does Tor work?

## Slide 118: How does Tor work?

## Slide 119: Building a circuit
Create c1, E(gx1)
Created c1, gy1, H(K1)
Relay c1 (Extend, OR2, E(gx1))
Create c2 E(gx2)
Created c2, gy2, H(K2)
Relay c1(Extended, gy2, H(K2)

## Slide 120: Fetching a web page
Last onion router should get the IP address of Bob’s website to protect Alice’s anonymity.
Relay c1 (Begin <Bob>)
Relay c2 (Begin <Bob>)
TCP Handshake
Relay c2 (Connected)
Relay c1 (Connected)

## Slide 121
operators want to know who sends each packet
so they can stop malicious senders
users want to hide who sends certain packets
so they can do stuff without the whole world knowing
Accountability
Privacy
VS

## Slide 122
Accountable Internet Protocol
Tor Instead of IP
Accountability
Privacy
VS
[Andersen et al., SIGCOMM 2008]
[Liu et al., HotNets 2011]
anti-spoofing mechanism
+ shutoff protocol
No Privacy
Shutoff is Stop-Gap Fix
Requires “Smart NIC”
routers act as onion nodes
Heavyweight
No Accountability
cryptographic addresses

## Slide 123
Accountable Internet Protocol
Tor Instead of IP
Accountability
Privacy
VS
unforgeable source addresses
hidden source addresses

## Slide 124
Destination Address
Source Address
…
return address
accountability
sender identity
error reporting
flow ID

## Slide 125
Destination Address
…
Source Address
Source Address
Return Address
Accountability Address

## Slide 126
Destination Address
…
Return Address
Accountability Address
Separate Accountability
and Return Addresses
+
Delegated Accountability
+
Hidden Return
Addresses
Return Address
Real-World Deployment
Accountable and Private Internet Protocol
APIP:

## Slide 127
Destination Address
…
Return Address
Accountability Address
Separate Accountability
and Return Addresses
+
Delegated Accountability
+
Hidden Return
Addresses
Return Address
Real-World Deployment
How it Works
Feasibility
Flow
Granularity
Accountable and Private Internet Protocol
APIP:

## Slide 128: brief(P)
“I sent this packet.”
Sender to Delegate:

## Slide 129: brief(P)
P
Delegate
Sender
F(P)
Fingerprint
Cache
04AF4DE779
B217C45091
30e26e83b2
cf24dba5f0
b0afd9c282

## Slide 130: brief(P)
Batch fingerprints in Bloom filter
Delegate does not learn packet contents

## Slide 131: verify(P)
“Do you vouch for this packet?”
Verifier to Delegate:

## Slide 132: verify(P)
A
A’s Delegate
PA → B
Verified Flows
DROPPED P
(PENDING VERIFICATION)
A → B
TWO CHECKS:
PA➞B in fingerprint cache
Flow A➞B not shut off
verify(P)
OK
verify(P)

## Slide 133: verify(P)
Most effective at first hop
Verified flow entries periodically expire
Routers keep no state during verification

## Slide 134: shutoff(P)
“Stop this flow.”
Receiver to Delegate:

## Slide 135: shutoff(P)
B
A’s Delegate
PA → B
Verified Flows
A → B
PA → B
shutoff(P)
PA → B
verify(P)
DROP_FLOW
BLOCKED
Flows
A → B

## Slide 136: shutoff(P)
Signature proves receiver sent shutoff
Delegate also facilitates long-term fix
Filtering happens at router, not NIC

## Slide 137: Delegated Accountability
Sender
Receiver
Accountability
Delegate
verify(P)
shutoff(P)
P
P
Is This Technically Feasible?
brief(P)

## Slide 138
Is This Technically Feasible?
brief(P)
< 1GB
Storage Overhead
fingerprints at delegate
?
0.5%
Network Overhead
sending fingerprints
?

## Slide 139
Sender
Receiver
Accountability
Delegate
verify(P)
shutoff(P)
P
P
Is This Technically Feasible?
brief(P)

## Slide 140
Is This Technically Feasible?
verify(P)
78K
verifies per sec
94MB
?
Computational Overhead
at delegate
?
Storage Overhead
verified flow list at router
CuckooFilter: [Zhou et al., CoNEXT 2013]
ed25519: [Bernstein et al., 2012]

## Slide 141
Sender
Receiver
Accountability
Delegate
verify(P)
shutoff(P)
P
P
Is This Technically Feasible?
brief(P)

## Slide 142
Accountability
Privacy
unforgeable source addresses
hidden source addresses
VS

## Slide 143
Accountability
Privacy
VS
every packet carries an accountability address
for reporting misbehavior
Delegated Accountability
return address can be hidden
since network just needs accountability address
Hidden Return
Addresses
Return Address